## Slide 1
Chapter 8
Best Management Practices for
Stormwater Management

## Slide 2
8.1.1 Nonstructural vs. Structural BMPs
Nonstructural BMPs are the first line of defense!
Prevention oriented, very cost effective, and aesthetically acceptable to the public and other inspecting agencies.
Improve water quality by reducing the generation and accumulation of pollutants near their sources
Includes:
Planning and management (Basin Management Action Planning or BMAP)
Wetland and floodplain protection (ERP)
Public education (319 Grants and MS4s)
Proper fertilizer and pesticide application control (GI-BMP Program and Fertilizer Ordinances)
Solid waste collection and disposal (Waste Management Program)
Street cleaning (MS4s)
“Good Housekeeping” techniques on construction sites (CGP)
http://gibmp.ifas.ufl.edu
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 3
STORMWATER
Structural BMPs:
Control volume and discharge rate through physical containment and structural design and reduce pollutants through:
Settling
Filtration
Percolation
Chemical Treatments
Biological Uptakes of Nutrients; such as, N, P, K and many other pollutants impairing our waterbodies.
The practices are typically land intensive, require proper long-term maintenance, and can be costly in urbanized areas.
8.1.1 Nonstructural vs. Structural BMPs

## Slide 4
Source
Control
Swales
Filters
Ponds
Use multiple BMPs in sequence to create a
Treatment Train!
8.1.2 BMP Treatment Train

## Slide 5
STORMWATER
The more elements incorporated into the system, the better the performance of the “TREATMENT TRAIN”
Different BMPs explored in this chapter should be used together – finding the right sequence is key
Many BMPs in this chapter are susceptible to clogging, especially filtration techniques – long term maintenance essential
Treatment swales, sediment forebays, and stilling basins intercept sediments before reaching the filtration BMPs.
Grey Infrastructure: older control structures in existence for years already
Green Infrastructure: new technologies in the treatment train that remove nutrients like Nitrogen and Phosphorus + other pollutants
Grassed Swale
Wet detention with littoral plants
Bio-Swale
8.1.2 BMP Treatment Train

## Slide 6
8.1.2 BMP Treatment Train
Find out more about Green Stormwater Infrastructure
(GSI) in Florida
@
gsi.floridadep.gov

## Slide 7
8.1.2 BMP Treatment Train
Educational materials, technical resources and more
@
gsi.floridadep.gov

## Slide 8
On-line BMPs capture all the runoff, temporarily storing it before discharge
Off-line BMPs divert a portion, or “treatment volume,” of the runoff and isolate from the remaining discharge.
Also called a “first flush” system
Detention Pond Retention Pond
Inlet Filters
“First Flush” Pond
8.1.3 On-Line versus Offline BMPs

## Slide 9
Definition: Earthwork specifications help maximize the desirable physical properties of soil and compensate for deficiencies
Purpose: to ensure that inadequate earthwork does not cause premature failure of constructed improvements
Condition where practice applies: this practice applies on all construction sites and where maintenance is necessary
Nuclear Densometer –
Used to Determine Compaction and a Quality Control for FDOT
8.2 Earthwork Specifications
Stockpile of Topsoil

## Slide 10
Specifications: Subgrade Preparation
Smooth & compact if no fill required – both subgrade and fill should be largely free of organic material
Muck must be removed – but check first! – muck means wetlands and impacts require ACOE/DEP/local permits
Scarify to make bond between native soil and imported fill – otherwise fill and sod can “slide” off
Check all permits for specific fill restrictions or conditions
Florida DOT may have additional specifications for Road and Bridge fill
Free of roots, rocks, demolition debris
8.2 Earthwork Specifications

## Slide 11
STORMWATER
Specifications: Fill, Backfill, & Compaction
Fill should be clean and free of roots, rocks, demolition debris
Fill introduced and compacted in “lifts”
Large areas: 10 - 12” lifts of soil, heavy equipment packs
Around pipes: 4 - 6” lifts, small rollers, tampers – delicate!
Natural compaction: several wet months, sediment control required, not advised without other stabilization
Compaction w/ sprinkler; takes several days, only very sandy soils
Large areas: 10 - 12” lifts, heavy equipment
8.2 Earthwork Specifications

## Slide 12
STORMWATER
Plate Compactor: used around pipes, inlets, etc: 4 - 6” lifts of soil at a time
Smaller machines = finer control around delicate structures
8.2 Earthwork Specifications

## Slide 13
STORMWATER
Definition: A surface area used to store runoff for a selected treatment volume that is retained onsite with storage volume recovered when runoff percolates into the soil or evapotransporates
Purpose: to combine flood control, pollution control, and ground water recharge in the design of a stormwater storage basin
Condition where practice applies: where space is available, and soil and ground water conditions allow recovery within 72 hours
Retention basins are designed to stay dry most of the time – standing water only from poor maintenance or design
8.3 Stormwater Retention Basin

## Slide 14
STORMWATER
Construction:
Initial basin excavation within 1 foot of final elevation of
the basin floor
Interior side slopes vegetated as per specifications
Light equipment should be used to remove any accumulated sediments and to achieve final grade without compacting the basin floor
Scarify with rotary tillers or disc harrows to promote infiltration
All structural elements shall be designed by FL Registered P.E.
Prevent sediment-laden runoff from entering a finished basin
Final inspection:
Correct location, dimensions, material
Control structures - location, type, functioning correctly
Bottom - free of sediments, scour, excess compaction
8.3 Stormwater Retention Basin

## Slide 15
STORMWATER
Definition: on-site retention accomplished below the ground
Purpose: to combine flood control, pollution control, and ground water recharge in the design of an underground stormwater storage facility
Condition where practice applies: where space is limited, yet soil type and ground water level will allow percolation of excess runoff – offline system usually for “first flush”
Installed beneath a parking lot
8.4 Exfiltration Trench
Can take the form of tanks, perforated pipes or aggregate stone

## Slide 16
Construction:
Safety First!! *****Trenches are dangerous! *****
If there is water in trench or loose soils use a trench box
Place escape ladders every 25 feet
Excavate to proper dimensions
Stockpile spoils & materials at least 10’ from edge of trench – inspect all elements carefully after storms
All materials per specs., material quality important
Good fittings & connections, monitoring well
Backfill, compact, restore area
8.4 Exfiltration Trench

## Slide 17
STORMWATER
Final inspection:
Adequate access to inspect & maintain
Location, dimensions, materials per plan & specifications
No sediments inside
No settlement on surface
*If going into an access-way to inspect on the inside, practice confined space safety including gas detection (H2S).
8.4 Exfiltration Trench

## Slide 18
STORMWATER
Definition: a concrete or asphalt pavement with a high percentage of void spaces which allows percolation of runoff
Purpose: to reduce the volume and peak flow of runoff, and to reduce the concentration and loading of pollutants
Condition where practice applies: low volume traffic, parking, pedestrian areas
8.5 Permeable Surfaces -Porous Pavement

## Slide 19
STORMWATER
Close-up View
Florida Aquarium Parking Lot
8.5 Permeable Surfaces -Porous Pavement

## Slide 20
STORMWATER
Construction:
Subgrade prep. (no excess compaction)
Used as part of the “treatment train” with other infrastructure
P.E. on site during mixing and placement
8.5 Permeable Surfaces -Porous Pavement

## Slide 21
Final inspection:
Correct location, dimensions, grading
Perimeter: stable contributing area, stable outlet, no sediment sources nearby
Materials, mix must be sampled at placement time
Performance test w/ water
8.5 Permeable Surfaces -Porous Pavement

## Slide 22
STORMWATER
Definition: a pavement consisting of strong structural units having regularly interspersed voids filled with pervious material
Purpose: to reduce the volume and peak flow of runoff; and to reduce loading and concentration of pollutants
Conditions where practice applies: low volume traffic areas, parking, pedestrian areas
Not where pollutants will infiltrate into the ground water
8.6 Concrete Grid & Modular Pavement
Paver Stones (Concrete Grid)

## Slide 23
STORMWATER
Red Brick Pavers used for park at Kissimmee, FL
Great choice for pedestrian focused areas
8.6 Concrete Grid & Modular Pavement

## Slide 24
STORMWATER
Modular Pavement
8.6 Concrete Grid & Modular Pavement

## Slide 25
Construction:
Subgrade prep.(no excess compaction)
Geotextile underlay for strength
Install per manufacturer’s instructions
8.6 Concrete Grid & Modular Pavement

## Slide 26
Final inspection:
Location, dimensions, grading per plan
All materials per spec., no defects
Check perimeter, outlets; test with water
8.6 Concrete Grid & Modular Pavement

## Slide 27
STORMWATER
Definition: a basin designed to temporarily store excess runoff prior to gradual release
Purpose: to reduce the impact of peak flows by redistributing the volume at a slower rate over a longer time
Condition where practice applies: where soil and/or ground water conditions do not allow percolation of excess runoff, yet pollution reduction and flood attenuation are desired or required
Note: detention and retention structure definitions can be found in 62-331 F.A.C. and Applicants Handbook
8.7 Detention Basins

## Slide 28
STORMWATER
Detention Basins have a designed overflow control structure – such as this Engineered Weir
8.7 Detention Basins

## Slide 29
STORMWATER
Littoral plants bio-absorb nutrients (nitrogen, phosphorus), and other pollutants either from the water in basin or before the water reaches it
Aquascaping with plants for aesthetic enhancement and water quality improvement
8.7 Detention Basins

## Slide 30
Construction:
Subgrade preparation
Excavation, embankment, anti-seep collars
Inlets, outlets, control structures, filters
May require a littoral planting schedule
8.7 Detention Basins

## Slide 31
STORMWATER
Final inspection:
Basin location, dimensions, slopes, volume
Structures: location & type; backfill, compaction, stabilization
Vegetation per spec., good install, viable
Elevations: basin floor, structures, freeboard correct w/ respect to each other
Basin & structures free of sediments, debris
8.7 Detention Basins

## Slide 32
STORMWATER
Definition: a system of conduits which collect and convey stormwater after it has infiltrated and been percolated through soil, suitable aggregate and/or filter fabric
Purpose: to allow infiltration and percolation in stormwater basins where permeability is restricted due to high water table or soil texture
UNDERDRAIN
8.8 Underdrains & Stormwater Filter Systems

## Slide 33
STORMWATER
Nutrient Removal Baffle Box
Baffle Box Vault Cover
At Kissimmee Lakefront Park
8.8 Underdrains & Stormwater Filter Systems

## Slide 34
STORMWATER
Construction:
Subgrade preparation, excavation
Location, dimensions per plan; materials per specs.; fittings, connections per details
Backfill, compact, vegetate
8.8 Underdrains & Stormwater Filter Systems

## Slide 35
Final inspection:
Inspect during installation because there is little to see after completion, use shovel to verify materials & installation
Vegetation per specs., viable
8.8 Underdrains & Stormwater Filter Systems

## Slide 36
STORMWATER
Definition: natural or constructed vegetated waterways designed for the treatment and disposal of runoff
Purpose: to allow removal of sediments and pollutants in flowing conditions and infiltration in standing conditions
Condition where practice applies: where space is available for natural, low cost, low maintenance stormwater conveyance & treatment
GRASSED WATERWAYS AND SWALES
Swale Block
8.9 Swales

## Slide 37
STORMWATER
Mitered End
8.9 Swales

## Slide 38
STORMWATER
Construction:
Excavate to proper grade & cross-section
Slope is 3:1 or less
Subgrade preparation
Vegetation
  Hydroseeding
  Bermuda grass sprigging
  Seed w/ straw & mulch
  Sod (establishes fastest)
Swale blocks used to slow energy
  Especially over long distance or steep grade
8.9 Swales

## Slide 39
STORMWATER
Final inspection:
Correct location,
dimensions, cross-section
Swale blocks per plan & specifications
Vegetation viable & per specifications
8.9 Swales

## Slide 40
STORMWATER
Definition: a permanent waterway designed to safely convey stormwater away from developed areas – steeper than swales
Purpose: to provide for the conveyance of stormwater without damage from erosion or flooding
Condition where practice applies: constructed channels (ditches) & modified natural channels with intermittent flows
Not designed for constant flows!!
8.10 STORMWATER CONVEYANCE CHANNEL
Vegetated channel w/ inlets leading to below ground system
(example of BMPs used in sequence - treatment train)
Riprap armored channel

## Slide 41
STORMWATER
Construction:
Excavate to proper grade & cross-section
Subgrade preparation
Vegetated: stapled sod or blanket & seed
Concrete: mix, rebar, joints, hydrostatic relief holes per specs.
Riprap: hand placed to avoid damage to geotextile underlay
Gabions: per manufacturer’s instructions
Gabion Mattress – I-10 Walton County, DeFuniak Springs, Florida
8.10 STORMWATER CONVEYANCE CHANNEL

## Slide 42
GRASS CHANNEL
CONCRETE CHANNEL
8.10 STORMWATER CONVEYANCE CHANNEL

## Slide 43
STORMWATER
GABIONS
RENOMATS
8.10 STORMWATER CONVEYANCE CHANNEL

## Slide 44
CANAL
8.10 STORMWATER CONVEYANCE CHANNEL

## Slide 45
STORMWATER
Final inspection:
Correct location, dimensions, cross-section
No settling, piping, bypassing, overtopping, erosion or sedimentation
Adjacent vegetation viable & per specs.
8.10 STORMWATER CONVEYANCE CHANNEL

## Slide 46
Definition: a permanent concrete-lined channel constructed on a slope
Purpose: to conduct runoff safely down the face of a slope without causing erosion on or below the slope
Condition where practice applies: wherever concentrated runoff must be conveyed down a slope on a permanent basis
hydrostatic relief holes
8.11 Paved Flume

## Slide 47
STORMWATER
Construction:
Subgrade preparation
Excavate to proper grade and cross-section
Excavate for headwall, anchor lugs, curtain wall
Concrete, rebar, joints, hydrostatic relief holes per specs.
Compact and vegetate any backfill
PAVED FLUME
Needs Rip-Rap Energy Dissipater installed at the end to stop erosion
8.11 Paved Flume

## Slide 48
STORMWATER
Final inspection:
Correct location, dimensions, cross-section
No settling, piping, bypassing, overtopping, erosion or sedimentation
Adjacent vegetation viable & per specs.
8.11 Paved Flume

## Slide 49
STORMWATER
Definition: A channel constructed across a slope with a supporting ridge on the lower side
Purposes: To reduce slope length and to intercept and divert stormwater runoff to stabilized outlets at nonerosive velocities
Conditions Where Practice Applies:
Where runoff from higher areas may damage property
Where surface and/or shallow subsurface flow are damaging upland slopes
Where the slope length needs to be reduced to minimize soil loss
Diversions are applicable only below stabilized or protected areas
Diversions should not be placed on slopes > 15 %
8.12 Diversion

## Slide 50
Definition: small dams constructed across a swale or drainage ditch
Purpose: to reduce the velocity and erosive force of concentrated flows in stormwater conveyance systems
Condition where practice applies: in constructed waterways to allow the use of vegetative lining by reducing velocity; and in natural channels which will receive increased flows due to development
8.13 Check Dams

## Slide 51
Construction:
Subgrade preparation
Location & spacing per plan, materials per specs.
Key-in, backfill, compact, revegetate
Final inspection:
Correct location, spacing, materials
Center lower than ends, no end-around
No rolling stones, no rapid silting-in
CONCRETE CHECK DAM
8.13 Check Dams

## Slide 52
STORMWATER
Definition: structurally lined aprons or other acceptable energy dissipating devices placed at the ends of pipes or paved channels
Purpose: to prevent scour at stormwater outlets and to minimize the potential for erosion by reducing the velocity
Conditions where practice applies: applicable to the outlets of all pipes and paved channels where the velocity will exceed the permissible velocity of the receiving channel
FABRIC FORM
8.14 Outlet Protection

## Slide 53
STORMWATER
Construction:
Subgrade preparation
Excavate to proper grade & cross-section
Geotextile per specs.; trenched & pinned per details
Granular filter material per specs.; placed uniform & compacted
Stone placement: hand-placed, uniform, compact; no damage to underlay
8.15 Rip-Rap

## Slide 54
Final inspection:
Correct location, dimensions, materials
Good placement - uniform density
No damage to underlay fabric
Toe of slope entrenched, not eroding
Design cross-sectional area not diminished by riprap liner
8.15 Rip-Rap

## Slide 55
Definition:
a high-density polyethylene (HDPE) grid of open cells which are filled with pervious material along slopes or stream banks allowing the establishment of vegetation
Purpose:
to prevent erosion by stabilization of the soil surface to reduce the volume and peak flow of runoff
to reduce the concentration and loading of pollutants
Condition where practice applies:
vegetated slopes, parking and low traffic areas, stream bank stabilization, gravity wall fills
8.16 Grid Confinement Systems

## Slide 56
STORMWATER
8.16 Grid Confinement Systems

## Slide 57
STORMWATER
8.16 Grid Confinement Systems

## Slide 58
STORMWATER
Green Infrastructure:
Decrease impervious area and need for stormwater ponds
8.16 Grid Confinement Systems

## Slide 59
Final inspection:
Location, dimensions, grading per plan
All materials per specs.
Grid well secured, edge conditions okay
Can be difficult to spot once vegetation becomes fully grown
Photo Credit: R.H. Moore & Associates
8.16 Grid Confinement Systems

## Slide 60
Definition: Precast perforated concrete blocks that stabilize slopes or stream banks, but also allow vegetation.
Purpose: to prevent erosion by stabilization of the soil surface, to protect the banks of streams, lakes, estuaries, and excavated channels.
Condition where practice applies: areas in need of erosion protection, sloping areas, areas requiring stabilization due to traffic or maintenance activities, and low water interfaces
8.17 Cellular Concrete Block

## Slide 61
STORMWATER
8.17 Cellular Concrete Block
Ideal for low-water crossings

## Slide 62
Construction:
Subgrade preparation
Geotextile
Proper anchors, cables, connectors
Pervious backfill, vegetation
Final inspection:
Location, dimensions, grading per plan
All materials per specs.
Well secured, edge conditions OK
8.17 Cellular Concrete Block

## Slide 63
STORMWATER
Chapter 8 Review

## Slide 64
When clearing a site and preparing for fill, tree and root debris should be (burned and buried under fill / removed from the fill area)
Pipes and structures can be damaged by heavy compactors and should be backfilled and compacted in small lifts with small compactors (T / F)
A ______________ is designed to retain stormwater on site and allow time for percolation into the ground.
retention basin
Chapter 8 Review

## Slide 65
When constructing a retention basin with heavy equipment, special care must be taken to avoid excessive ____________ of surface soils, especially in the basin floor.
Retention basin storage volume must be recovered within ___ hrs.
The purpose of a _______________ is to temporarily store runoff and release it at a controlled rate.
All inlets, outlets, and other control structures should be inspected when?
Weekly and after each major storm event
By definition a swale should have side slopes no steeper than ___ horizontal to vertical.
compaction
72
detention basin
3:1
Chapter 8 Review

## Slide 66
A swale is a good place to recycle yard debris since it's organic. (True / False).
A _____________________________ is a permanent, designed waterway; shaped and lined with appropriate material (erosion resistant): to safely conduct (convey) runoff away from a developing area.
The purpose of a paved flume is to safely conduct runoff down the face of a slope. (T / F)
The purpose of a diversion is to direct stormwater to a stabilized area. (T / F)
The maximum spacing between check dams should be such that the bottom(toe) of the upstream dam is at _____ elevation as the top of the downstream dam.
Sediments should be removed before they reach ________ of the original height of the dam.
stormwater conveyance channel
same
½ (50%)
Chapter 8 Review

## Slide 67
A(n) ________________ device is designed to prevent scour at outlets and minimize erosion downstream by reducing the velocity of concentrated stormwater flows.
The three functions of riprap are:
protect soil surface from erosion
slow the velocity of flow
stabilize slopes
When placing ______ over geotextile great care must be taken to avoid damaging the geotextile while placing the stone.
outlet protection
riprap
Chapter 8 Review