## Slide 1
Improved Water Deliveries to
Northeast Shark River Slough
TOC Sub-committee Briefing
May 15, 2013

## Slide 2: Changes in Surface Water Flows to Everglades National Park (1959 vs 2005)

## Slide 3
West Shark River Slough
Northeast Shark River Slough
Comparison of Water Levels and Topography
in West vs Northeast Shark River Slough
Ground Elevation
along Tamiami Trail

## Slide 4
The Everglades National Park Protection
and Expansion Act of 1989
Authorized modifications to the Central & Southern Florida Project “to improve water deliveries into the park and shall, to the extent practicable, take steps to restore the natural hydrologic conditions in the Park.” (Army Corps)
Authorized the acquisition of 109,000 acres in Northeast Shark Slough and the East Everglades. (National Park Service)

## Slide 5
Mitigation
L-31N (S-356)
Conveyance
Tamiami Trail
L-67 extension
L-67A/C S-345s)
L-29 (S-355A/B)
Osceola Camp
Tigertail Camp
8.5 Square Mile Area
The ENP Protection and Expansion Act (1989)
Modified Water Deliveries Project
Authorized modifications to the Central & Southern Florida Project “to improve water deliveries into the park and shall, to the extent practicable, take steps to restore the natural hydrologic conditions in the Park.” (Army Corps)
East Everglades Acquisition
Authorized the acquisition of 109,000 acres in Northeast Shark Slough and the East Everglades. (National Park Service)

## Slide 6: Components of the MWD Project
Mitigation Features
Seepage Control Features
L-31N (S-356)
Conveyance Features
Tamiami Trail
L-67 extension
L-67A and C
L-29 (S-355 A and B)
Osceola Camp
Tigertail Camp
8.5 Square Mile Area

## Slide 7
Existing Culverts
Tamiami Trail
Project Location indicated by red box
Blue Shanty Canal
L-67ext
WCA
3A
WCA-3B
Northeast Shark Slough
Everglades National Park
S355A
G69
S355B
S334
S24
G70
S333
L-31N
L-29
Roadway Modifications
1-mile Bridge
1-Mile Bridge Construction
Modified Water Deliveries-Tamiami Trail Limited Re-evaluation Report

## Slide 8
LRR Project Hydrologic
Assessment Spreadsheet Model
A spreadsheet model was developed by the Army Corps to incrementally test the flow benefits associated with different combinations of L-29 canal stage constraints and bridge openings along eastern Tamiami Trail.
The combination of a one-mile bridge and an L-29 stage constraint of 8.5 (Alt 3.2.2a) was selected as the recommended alternative.
The model assumes that flow volumes from WCA-3A into Shark Slough are the same and a 45% West – 55% East distribution is the target.

## Slide 9
LRR Hydrologic Spreadsheet Model
No Action (no bridging or L-29 stage raising)
Avg. Annual Flows 177K ac-ft
Wet 30% Dry 70%

## Slide 10
LRR Hydrologic Spreadsheet Model
Initial Field Test (1-mile bridge and L-29 7.5 ft. constraint)
Avg. Annual Flows 204K ac-ft
Wet 42% Dry 58%

## Slide 11
LRR Hydrologic Spreadsheet Model
Second Field Test (1-mile bridge and L-29 8.0 ft. constraint)
Avg. Annual Flows 274K ac-ft
Wet 46% Dry 54%

## Slide 12
LRR Hydrologic Spreadsheet Model
Third Field Test (1-mile bridge and L-29 8.5 ft. constraint)
Avg. Annual Flows 340K ac-ft
Wet 49% Dry 51%

## Slide 13
LRR Hydrologic Spreadsheet Model
Base LRR 177K ac-ft Wet 30% Dry 70%
Bridge 7.5 204K ac-ft Wet 42% Dry 58%
Bridge 8.0 274K ac-ft Wet 46% Dry 54%
Bridge 8.5 340K ac-ft Wet 49% Dry 51%

## Slide 14
Tamiami Trail Next Steps Project
Alternative 6E (1st Increment)
NPS Design & Built
Contract in 2014

## Slide 15
Central Everglades Alt4R Features
Redirect WCA-3A
flows (Enlarged
S-333)
WCA-3B Inflows (Blue Shanty Flow-way)
Levees Degraded
(L-67C & L-29)
L-29 Divide Structure
Seepage Mgmt.
(Enlarged S-356)
2.6-Mile Bridge

## Slide 16
LRR Hydrologic Spreadsheet Model
Central Everglades Planning Project (for comparison only)
Avg. Annual Flows 700K ac-ft
Wet 54% Dry 42%

## Slide 17
LRR Hydrologic Spreadsheet Model
Monthly Median Flow Comparison