## Slide 1: Trout River BMAP, Lower St Johns River Basin
Discussion of Little Trout River inclusion into the Trout River BMAP

## Slide 2: Considerations for Including Little Trout River in the BMAP
Little Trout converges with the Middle Trout River and may be a contributor of nutrients to the Middle Trout watershed.
Adding Little Trout River to the BMAP increases the area where projects can be applied for reduction credit.

## Slide 3: Considerations Continued
MS4 permit language now requires permittees to implement plans to address impaired waters within their jurisdiction.
The addition of Little Trout in the Trout River BMAP would negate the necessity of MS4 permittees to address these impairments separately.
If a TMDL was later developed, projects already completed would count toward any reductions.

## Slide 4: Little Trout Impairments
In 2008, Little Trout River was verified impaired for dissolved oxygen (DO) with the causative pollutants of total phosphorus (TP) and biochemical oxygen demand (BOD).
Both parameters exceeded the Impaired Waters Rule (IWR) thresholds
  TP concentration of 0.249 mg/L versus the standard of 0.22 mg/L,
  BOD concentration of 2.05 mg/L versus the standard of 2.0 mg/L.

## Slide 5: Nutrient Summary Analysis
Total Nitrogen
  Proposed Numeric Nutrient Criteria 1.73
  Median Value based on 10 Obs. 1.4255
  Current Status Not Exceeding
Total Phosphorus
  Proposed Numeric Nutrient Criteria 0.101
  Median Value Based on 10 Obs. 0.34
  Current Status Exceeding

## Slide 6: Reasonable Assurance, Natural Conditions, & Category 4E
Reasonable assurance could be developed for this waterbody however the process for approval from EPA is difficult.
It is difficult for FDEP to prove the impairment is due to natural conditions because it does not meet the DO standard and TP is above the IWR threshold.
Category 4E: Impaired, but ongoing restoration activities are underway to restore the designated uses of the waterbody.

## Slide 7: Why Category 4E?
This would allow for stakeholders to begin restoration and allow the Department to delay in creating a TMDL.
Designation of 4E allows time for restoration projects to improve water quality while awaiting the next cycle of assessment.
Projects combined with other information regarding stream health would help to support the Department’s case to EPA for the change in assessment.

## Slide 8: Stakeholder Questions
What is a SCI and why is it important?
If the SCI score comes back really good, would that negate the nutrient impairment in Little Trout River?
What if a SCI is an inappropriate measurement for this watershed?
Old Kings Road is the sampling station but may not be ideal for SCI because of significant stormwater inputs. Bocephus Road may be better characterize the ambient water quality.

## Slide 9: Stakeholder Questions Continued
COJ has attempted an RA plan for the fecal coliform impairments in the past. What makes this approach better?
Even though FDEP delists a waterbody, EPA can add it back and create a TMDL. What happens if EPA does not accept this delisting?
If a restoration plan is created instead of adopting a TMDL, how does this affect a future SSAC determination under EPA’s NNC rule?
Other questions?