## Slide 1: Lake Jesup BMAP Street Sweeping Credit
July 19, 2012

## Slide 2: Reminder
Street sweeping credit was assigned in the BMAP using information from a U.S. Geological Survey (USGS) study in Massachusetts.
The study found that the average total phosphorus (TP) load per road mile was 14 g/mi/day.
For the Lake Jesup BMAP, this value was reduced by 50% for each of the following factors:
  Uncertainty in the value as an aggregate across a variety of rainfall conditions; and
  To account for the difference between Massachusetts values and Florida.
Resulted in a value of 3.5 g/mi/day.

## Slide 3: Reminder, continued
Credit for street sweeping was assigned using the following efficiencies (from studies by the Center for Watershed Protection, Orange County, and Florida Department of Transportation) based on frequency of sweeping:
Frequency | TP Removal Efficiency
Daily or 2 times/week | 7%
Weekly | 5%
2 times/month | 4%
Monthly | 3%
Quarterly | 2%
Annually | 1%

## Slide 4: New Method
In May 2011, the Florida Stormwater Association (FSA) released a report that quantifies nutrients loads associated with source control and maintenance practices.
The report includes concentrations of TP and total nitrogen (TN) per kilogram of dry weight of material collected.
This information was determined using data collected by municipal separate storm sewer systems (MS4s) across the state of Florida.

## Slide 5: New Method, continued
FSA developed a spreadsheet to estimate the TN and TP reductions associated with street sweeping (as well as catch basin and best management practice [BMP] clean outs).
Review the spreadsheet: FINAL MS4 Load Reduction Tool_Lake Jesup.xlsx

## Slide 6: Example Project
Monthly street sweeping on 10 miles of roadway; 15 cubic yards of dry material collected each month.
Credit under previous method:
  10 miles * 1,277.5 g/mi/yr *3% removal = 332 g/yr = 0.7 lbs/yr
Credit under new method:
  180 cy/yr * 27 cf/cy * 84.9 lbs/cf * 0.4536 kg/lbs *361 mg TP/kg * 0.000001 kg/mg * 2.205 lbs/kg = 149 lbs/yr

## Slide 7: Process to Update Credit
Stakeholders should gather information about the weight or volume of material collected annually through street sweeping.
As part of the next annual BMAP progress report, the spreadsheet will be sent with the BMAP information to update street sweeping credit.
The 2013 progress report will include the revised street sweeping credit for stakeholders that provide updated information.

## Slide 8: Questions?