## Slide 1
Update on
Wekiva Septic Tank Study
April 20, 2017

## Slide 2: Study Objectives
The results of study helps us better understand:
  Attenuation and leaching of nitrogen from existing septic systems into the soil and ground water
  Other sources of nitrogen in residential areas
  Conditions that may influence nitrogen attenuation local to this area

## Slide 3: Chronology

## Slide 4
Site ID | City | No. residents | Drainfield repair/replacement history | Maintenance info | Fertilizer use | Soil
A | Sorrento | 2 | infiltrators (original) | pumped regularly | yes, self applied | Candler fine sand
B | Apopka | 3 | infiltrators (2009) | pumped in 2013 | yes, self applied | Candler fine sand
C | Apopka | 3 | infiltrators (2010) | septic tank pumped in 2013 | yes, self applied | Candler fine sand
D | Apopka | 2 | pipe in gravel (original) | not pumped out lately | yes, commercial service | Candler fine sand
E | Apopka | 2 | pipe in gravel (1989) | not pumped | yard mostly mulched beds | Candler fine sand
F | Apopka | 4 | infiltrators (2010) | pumped in 2014 | not lately | Candler fine sand
G | Apopka | 3 | pipe in gravel (original) | pumped in 2014 | yard mostly mulched beds | Candler fine sand
H | Apopka | 2 | pipe in gravel (original) | not pumped | yes, commercial service | Candler fine sand
I | Longwood | 1-2 | infiltrators (1989) | pumped in 2015 | yes, commercial service | Urban land
J | Longwood | 2 | mounded pipe in gravel bed | pumped regularly | yes, commercial service | Urban land
K | Apopka | 2 | pipe in gravel (original) | pumped in 2015 | yard mostly mulched beds | Candler fine sand
Information on Study Sites

## Slide 5
11 Study Site Locations

## Slide 6: Scope
Lysimeters to monitor soil pore water below drainfields and at background locations
Riser installation and effluent monitoring
Monitoring wells at some locations
Collect data on water use to estimate loading

## Slide 7: Other Activities
Evaluate changes in septic tank treatment after pumping.
  By selectively sampling septic tank effluent, pre and post pumping we hope to help provide some actual data on the potential benefit of tank pumping.
Conduct alternative nitrogen reducing drainfield study.
  Bold and Gold or other similar reactive media
  Passive low-cost construction
  Wekiwa Springs State Park location
  Orchard Drive location
Use data for modeling purposes, “STUMOD”

## Slide 8
Nutrient Levels in Soil Pore Water

## Slide 9
Types of drainfields in study

## Slide 10
Septic Tank Effluent Sampling
Septic tank effluent samples collected bimonthly at 8 sites

## Slide 35: Summary Findings for Lysimeter Samples

## Slide 36
Information on attenuation to be used in soil attenuation modeling. Results from some of the sites where TN was mostly from drainfields are summarized below.
At Site E, 39 % of nitrogen was reduced with 10% due to dilution.
At Site G, 42 to 46 % of nitrogen was reduced in shallow and deep lysimeters with no dilution.
At Site J where there is a shallow water table, 35 % of the nitrogen was reduced in a shallow well with no dilution.
At Site K, 44 % of nitrogen was reduced with no dilution.
Overall attenuation of N by means other than dilution 35-46%
Information about drainfield-related N attenuation

## Slide 37
Soil Attenuation Modeling

## Slide 38: Septic Tank Effluent and Influence of Pumping
Midway through the study, 4 septic tanks were pumped. Others left as control.
Septic tanks at sites A, B, E and G were pumped in March 2016, between February and April monitoring events

## Slide 40
Statistics for all sites

## Slide 41
TN Trends after pumping

## Slide 42
Alternative Drainfield Research

## Slide 49
Chart: Shallow Lysimeters - Total Nitrogen mg/L
| 42627 | 42655 | 42683 | 42753 | 42789
L-1S | 57 | 39 | 29 | 28
L-2S | 4 | 32 | 26 | 44
L-3S | 3 | 13 | 10 | 13
L-4S | 12 | 3 | 8 | 13 | 14
L-5S | 3 | 2 | 8 | 1 | 2
L-6S | 3 | 2 | 3 | 1.5 | 2
L-7S | 19 | 13 | 37 | 67
STE1 | 80 | 45 | 60 | 61 | 40
Chart: Deep Lysimeters - Total Nitrogen mg/L
| 42627 | 42655 | 42683 | 42753 | 42789
L-1D | 14 | 46 | 13 | 20
L-2D | 11 | 24 | 21 | 23
L-3D | 8 | 3 | 10 | 10 | 14
L-4D | 13 | 11 | 5 | 5
L-5D | 4 | 3 | 5 | 2 | 3
L-6D | 31 | 27 | 20 | 11
STE1 | 80 | 45 | 60 | 61 | 40
Average 70-80% reduction
TN results through February

## Slide 50: Next Steps
Complete modeling of soil attenuation (May 2017)
Produce draft report (May 2017)
Finalize report (June 2017)
Continue monitoring at experimental site