## Slide 1: 2016 BMAP Annual Meeting Martin County Update
St Lucie River and Estuary Basin Management Action Plan (BMAP)
Annual Meeting
Martin County Engineering Department /
Ecosystem Restoration and Management Division
Greg Nolte
Project Manager
October 26, 2016

## Slide 2: Current Status & Completed Projects
Beginning of Year Status
2015 BMAP Progress Report – 34 Projects
  TN Reductions: 41,511 lbs / year *
  TP Reductions: 7,920 lbs / year *
2016 Completed Projects
Danforth Creek Hybrid Wetland Treatment Technology *
Manatee Pocket SW Prong Baffle Box
Martin County Golf Course Improvements
* Credits for Danforth Creek HWTT were included in the 2015 Progress Report and was listed as “Under Construction”. Construction was finalized and online in 2016.

## Slide 3: Danforth Creek HWTT
Hybrid Wetland Treatment Technology (HWTT) is a patented alternative treatment technology that combines wetland and chemical treatment in a series of processes designed to achieve high rates of nutrient removal within a smaller spatial footprint.
Treats 2,419 acre upstream basin
Addition to and in conjunction with Danforth Creek Phase 1 Project
Project site 9.14 acre – Total project site 20.6 acres
Variable pump system – maximum capacity 25 cfs
Chemical treatment utilizes Aluminum Sulfate (Alum) and polyaluminum chloride (PAC) introduced front end of system to coagulate and precipitate nutrients
Process includes an above ground, lined Contact Pond, a Settling Pond, a Floating Aquatic Vegetation (FAV) Pond and a Submerged Aquatic Vegetation (SAV) Pond
Starting with Contact Pond, each pond will cascade from one to next via gravity through internal weirs with final discharge into Danforth Creek

## Slide 4: Danforth Creek HWTT
Danforth Phase 1
Pump Station
Storage Building
Contact Pond
Settling Pond
FAV Pond
SAV Pond
Discharge
Danforth Creek

## Slide 5: Danforth Creek HWTT
Partnership with FDACS - $3,000,000 State Appropriations
Design / Build:
  Watershed Technologies and Federico, Lamb & Associates
Design and Permitting: Started Sep ’14, Completed Feb ‘15
Construction: Started Mar ’15, Completed Apr ’16
  Contractor: A-Shaping
  Preliminary Performance Efficiencies
    TN Reduction: ~60% Removal efficiency
    TP Reduction: ~90% Removal efficiency
    Fecal Coliform: ~90% Removal efficiency

## Slide 6: SW Prong Baffle Box
Southwest Prong is one of the many tributaries to the Manatee Pocket
Located between the Salerno Creek and Manatee Creek Basins
Watershed is approximately 200 acres that includes portions of New Monrovia, Murray Middle School, Emerald Lakes and Publix’s shopping center at Cove Road and US Highway 1
Large upstream portion of basin drains via an existing 48” x 76” ERCP
Project consisted of installation of a 10’ x 16’ second generation Baffle Box in-line with existing 48” x 76” ERCP

## Slide 7
SW Prong Baffle Box
Design Team: CAPTEC & AACE
Design and Permitting:
  Feb 2015 – Jul 2015
Construction:
  Sep 2015 - Jan 2016
  Contractor: Custom Built Marine Construction (CBMC)
  Funding:
    Martin County - $132,500
    SLRIT Grant - $100,000
    Costs:
    Design & Permit: $ 50,230
    Construction: $182,270
    Total Cost: $232,500

## Slide 8: SW Prong Baffle Box

## Slide 9: MC Golf Course Water Quality Improvements
Original golf course was built prior to today’s requirements for water quality treatment; lake only provided flood protection
Watershed is approximately 234 acres of golf course
Project consisted of retrofitting three outfall culverts with weirs and improvements to outfall ditch and existing weir
Project provides 19.5 ac-ft of water quality treatment, which equates to 1” over the contributing area

## Slide 10: MC Golf Course Water Quality Improvements
Design Team: CAPTEC
Design:
  Jan 2015 - Oct 2015
Construction:
  Nov 2015 - Mar 2016
  Contractor: Coastal Land Development(CLD)
  Funding:
    Martin County - $106,250
    SLRIT Grant - $ 50,000
    Costs:
    Design & Survey: $ 24,290
    Construction: $131,960
    Total Cost: $156,250

## Slide 11: MC Golf Course Water Quality Improvements
Before
After
Before
After

## Slide 12: MC Golf Course Water Quality Improvements
Before
After
Before
After

## Slide 13: MC Golf Course Water Quality Improvements
Before
After

## Slide 14: Martin County TMDL / BMAP Status
Chart: Nutrient Load Reduction, lbs/yr
| TN | TP
Current Reductions | 42268 | 8164
1st Priority Project* | 8952 | 4484.9
2nd Priority Projects* | 1484.1 | 512.7
Column1 | 1428.4

## Slide 15: Current Projects
All American Ditch Stormwater Quality Improvement Project

## Slide 16: Current Projects
Hilltop Street Water Quality Improvement Project

## Slide 17: Thank you! Questions?
Martin County Engineering Department /
Ecosystem Restoration and Management Division
Greg Nolte
Project Manager