## Slide 1: Lake Jesup Basin Management Action Plan (BMAP) 2019 Progress Report
Moira Homann
Florida Department of Environmental Protection (DEP)
Division of Environmental Assessment and Restoration
January 30, 2020

## Slide 2: Agenda
BMAP Annual Progress Report
  Summary of project status and reductions
  Monitoring activities
Updates
  Seminole County
  Orange County
  Water Management District Updates
    Cameron Flow Way and Channel C Update
    Phosphorus Technology Request for Information (RFI)
    Bench Scale Efficiency Testing of Phosphorus
    Water Quality Update
Alternative Restoration Plan Information

## Slide 3: BMAP Annual Progress
9 projects completed in 2019
54 projects added in 2019
62 ongoing projects
Project Status
Notes: Ongoing projects include street sweeping, BMP clean out, public education, and other activities that must continue each year to maintain the credit amount.

## Slide 4: BMAP Annual Progress
Project Types
Project Type | Count of Project Type
100% On-site Retention | 2
Agricultural BMPs | 2
Alum Injection Systems | 9
Aquatic Vegetation Harvesting | 1
Baffle Boxes- Second Generation | 8
Baffle Boxes- Second Generation with Media | 1
Bioswales | 5
BMP Cleanout | 9
BMP Treatment Train | 2
Catch Basin Inserts/Inlet Filter Cleanout | 2
Control Structure | 1
Dry detention pond | 3
Education Efforts | 15
Enhanced Public Education | 2
Exfiltration trench | 5
Exotic Vegetation Removal | 4
Grass swales without swale blocks or raised culverts | 1
Hydrodynamic Separators | 8
Hydrologic Restoration | 1
Land Use Change | 1
Project Type | Count of Project Type
LID- Tree Boxes/Tree Wells | 2
Muck Removal/Restoration Dredging | 2
On-line Retention BMPs | 2
OSTDS Phase Out | 5
Regional Stormwater Treatment | 3
Regulations, Ordinances, and Guidelines | 3
Sanitary Sewer and Wastewater Treatment Facility (WWTF) Maintenance | 1
Sanitary Sewer Inspections | 3
Shoreline Stabilization | 2
Stormwater System Rehabilitation | 13
Street Sweeping | 16
Study | 8
TBD | 1
Wastewater Service Area Expansion | 2
Wet Detention Pond | 15
Wetland Treatment | 1
WWTF Diversion to Reuse | 1
WWTF Nutrient Reduction | 1
WWTF Upgrade | 2
WWTF Upgrade | 1
Grand Total | 166

## Slide 5: BMAP Annual Progress
Total Phosphorus (TP) Load Reductions Achieved
Notes: The amendment sets a deadline for achieving load reductions no later than 2030, which is 20 years after the initial BMAP adoption. The reductions are split, with at least half of the required reductions occurring within the next 5 years and the remaining reductions occurring by 2030.
The 2010 BMAP had reductions spread over a 15-year period. The additional 5 years were added to account for the time that was needed to update the modeling before preparing this BMAP Amendment and to allow time to design, test, and implement in-lake projects.
DEP is requiring each entity to achieve at least 50 % of its required TN and TP reductions within the next 5 years
Ongoing projects are added into the first year. TP reductions have been exceeded.

## Slide 6: BMAP Annual Progress
TN Load Reductions Achieved
Notes: Ongoing projects are added into the first year. TN reductions have been exceeded.

## Slide 7: Monitoring Activities
Through both the WIN and Florida STORET (STOrage and RETrieval). databases, the Division of Environmental Assessment and Restoration (DEAR) implements Florida statutory requirements, DEP rule requirements and U.S. EPA funding requirements for management of environmental (non-regulatory) data for the state
DEAR uses of water quality data include but are not limited to:
  Assessment of waters for purposes of the Impaired Waters Rule (IWR)
  Development of:
    Water Quality Criteria
    Total Maximum Daily Loads (TMDL)
    Basin Management Action Plans (BMAP)
Providing data as required to U.S. EPA and to the public
Currently 85 Organizations actively providing Activity and Result data
Watershed Information Network (WIN)

## Slide 8: Monitoring Activities
373.026(2), Florida Statutes (F.S.): Statutory authority and responsibility for central data repository. All local governments, water management districts, and state agencies are directed to cooperate with the department or its agents in making available to it for this purpose such scientific and factual data as they may have, generate, or possess, as the department deems necessary. The department is authorized to prescribe the format and ensure quality control for all data collected or submitted.
Chapter 62-40.540(3), Florida Administrative Code (F.A.C.), Water Resource Implementation Rule: Rule authority for central data repository. All appropriate water quality data collected by the Department, Districts, local governments, and state agencies shall be placed in the FLORIDA STORET system within one year of collection.
Chapter 62-303, F.A.C., Identification of Impaired Surface Waters: Rule authority for STORET and successors to be primary source of data used for determining whether samples do not meet water quality criteria. As required by subsection 62-40.540(3), F.A.C., the Department, other state agencies, the Water Management Districts, and local governments collecting surface water quality data in Florida shall enter the data into FLASTORET within one year of collection. Other sampling entities that want to ensure their data will be considered for evaluation should ensure their data are entered into FLASTORET.
Central Data Repository Statute and Rules

## Slide 9: Local Updates
Seminole County
Orange County
St. Johns River Water Management District

## Slide 10: Lake Jesup water quality summary
Rolland Fulton
rfulton@sjrwmd.com
January 30, 2020
Notes: I am not very familiar with this basin, so this presentation is limited to a summary of water quality data. I am not prepared to try to relate water quality changes to pollutant sources or water quality improvement activities in the basin.

## Slide 11: Water quality assessment
Limited to SJRWMD stations from Middle Basin lakes and mainstem St. Johns River
Nutrients:
  Total Phosphorus
  Total Nitrogen
Chlorophyll-a
Secchi transparency
Phytoplankton biovolumes
Notes: Have not reviewed data from watershed tributaries.

## Slide 12
OW-4
SJR-DPP
LMAC
OW-6
OW-2
SJR-OLH
CLH
SRN
Location | Station IDs
St. Johns River Inflow to Lake Harney | SRN
Lake Harney | CLH, SJR-OLH
Lake Jesup | OW-6, OW-4, OW-2
Lake Monroe | LMAC, SJR-DPP
Station Locations
Notes: SRN – Harney Inflow (twice monthly); CLH – center Lake Harney (monthly); SJR-OLH – Harney outfall (monthly); 3 sites in Lake Jesup (monthly): OW-2 E off Grassy Point; OW-4 W of Bridget; OW-6 West arm; LMAC – center Lake Monroe (monthly); SJR-DPP Monroe outflow (twice monthly).

## Slide 13
Notes: Summary of mean TP concentration for last 5 years 2015-2019 (red); TMDL target concentrations (blue). Lake Jesup TMDL target TP = 0.094 mg/L. Mean concentrations ~ 0.15 at OW-2 (Grassy Point), ~ 0.13 at OW-4 (W of bridge) and OW-6 (West arm)
(Paired t-test O-2>O-4=O-6; Mann-Whitney U O-2=O-4=O-6).
Lakes Harney and Monroe TP target = 0.07 mg/L. Mean concentrations ~0.08-0.1 mg/L.

## Slide 14
Notes: Summary of mean TN concentration for last 5 years 2015-2019 (red); TMDL target concentrations (blue). Lake Jesup TMDL target TN = 1.32 mg/L. Mean concentrations ~ 2.4 at OW-2 (Grassy Point), ~ 2.2 at OW-4 (W of bridge) and ~ 2.3 at OW-6 (West arm) (Paired t-test O-2=O-4=O-6; Mann-Whitney U O-2=O-4=O-6).
Lakes Harney and Monroe TN target = 1.18 mg/L. Mean concentrations ~1.3-1.5 mg/L.

## Slide 15
Notes: Summary of mean Chlorophyll-a concentration for last 5 years 2015-2019 (green); TMDL target concentrations (blue). Lake Jesup TMDL target Chla = 30.5 mg/L. Mean concentrations ~ 66 at OW-2 (Grassy Point), ~ 83 at OW-4 (W of bridge) and ~ 78 at OW-6 (West arm) (Paired t-test O-2=O-4=O-6; Mann-Whitney U O-2=O-4=O-6).
Lake Harney chl target 10.75 ug/L in lake, 5.8 ug/L in outfall; actual mean concentrations slightly below those targets. Lake Monroe chl target 13.2 ug/L in lake, 9.1 ug/L in outfall; actual concentrations ~22 ug/L in lake and 15 ug/L in outfall.

## Slide 16
Notes: Summary of mean Secchi transparency for last 5 years 2015-2019. No TMDL targets for Secchi depths. Mean Secchi depths ~ 0.38 m at OW-2 (Grassy Point), ~ 0.41 m at OW-4 (W of bridge) and ~ 0.42 m at OW-6 (West arm) (Paired t-test O-2<O-4=O-6; Mann-Whitney U O-2=O-4=O-6).
Mean Secchi depths ~ 0.6 m in Harney and Monroe, about 0.8 m in the outfalls from both lakes

## Slide 17
Notes: Time series of TP in Lake Jesup. Next 4 slides have a similar design. Small points are individual measurements, larger, darker circles are annual averages, thick horizontal blue line is the TMDL target, and thin blue line is the time series of lake water levels. District does an annual assessment of status and trends for ambient water quality stations throughout the District, which includes our MSJ basin lake stations. The 2019 Status and Trend report is available on our website (https://www.sjrwmd.com/data/water-quality/#status-trends) – black arrows indicate time period for trend assessment (2004-2018) – decreasing trend in TP at all 3 Lake Jesup stations. But still recent concentrations average well above the TMDL target.
TP concentrations in Lake Jesup tend to be highest during periods of low water levels. In fact, concentrations of TP, TN, and Chla are all negatively correlated with water levels – so water quality tends to deteriorate during periods of low water levels. We see similar trends in the Ocklawaha Chain of Lakes. Potential reasons: Nutrients become concentrated in a smaller volume of water, greater resuspension of bottom sediments when the water depth is shallower, release of nutrients from lake and wetland sediments that dry out during low-water periods. Interestingly, we see an opposite trend with phosphorus in Lakes Harney and Monroe. In them, TP and particularly inorganic P are positively related to water levels – suggests that high river flows from the Upper St. Johns basin or other watershed runoff bring a lot of P into those lakes.

## Slide 18
Notes: Time series of TN in Lake Jesup. 2019 Status and Trend report – decreasing trend in TN at stations OW-2 and OW-4, no significant trend at OW-6 (western arm) (2004-2018 – arrows indicate time period for trend assessment). But still recent concentrations average well above the TMDL target.

## Slide 19
Notes: Time series of Chlorophyll-a in Lake Jesup. 2019 Status and Trend report – increasing trend in chla at all 3 Lake Jesup stations – opposite from decreasing trends in nutrients. Trend appears to be driven by low chlorophyll levels in first 3-4 years of assessment period. Recent concentrations average well above the TMDL target.

## Slide 20
Notes: Time series of Secchi transparency in Lake Jesup. 2019 Status and Trend report – increasing trend in Secchi at all 3 Lake Jesup stations (2004-2018 – arrows indicate time period for trend assessment). Consistent with decreasing trend in nutrients but opposite to increasing trend in chlorophyll. Increasing trend seems driven by generally low Secchi from 2005-2008.

## Slide 21
Notes: Average phytoplankton biovolumes 2014-17, divided into the major taxonomic groups. We stopped monitoring phytoplankton after 2017 at most of these sites. Phytoplankton biovolumes much higher in Jesup than other MB lakes – dominated by cyanobacteria (blue-green stippling). Most prominent genus in Lake Jesup is generally Cylindrospermopsis. Sometimes Microcystis, Anabaena, and Planktolyngbya prominent.

## Slide 22
Notes: Same phytoplankton data expressed as percent composition. Again, clearly see dominance by Cyanobacteria in Jesup, as well as in downstream Lake Monroe.

## Slide 23: Water Quality Restoration Alternatives to TMDLs
Ben Ralys
Moira Homann

## Slide 24: Restoration Alternatives
Two types of Restoration Alternative Plans
  Reasonable Assurance Plan
    Assessment Category 4b
    Not Placed on the 303(d) List
  Pollutant Reduction Plans
    Assessment Category 4e
    Included on the 303(d) List
These plans are addressed in the Impaired Waters Rule in Section 62-303.600, F.A.C.

## Slide 25: Benefits of an Alternative Restoration Plan
Provides a faster path to restoration
Allows stakeholders to control the path to restoration for their waterbody
  Developing a plan prior to state or federal action provides the best way for stakeholders to plan for efficient and effective management
  Avoid TMDL-related regulatory requirements
Acknowledges proactive efforts
  Stakeholders receive credit for pollutant reductions
  Benefits to downstream impaired waters
Provides time for good targets to be developed
Enhances public relations

## Slide 26: Restoration Alternatives
Category 4b Assessments and Documentation
Category 4e Assessments and Documentation
https://floridadep.gov/dear/alternative-restoration-plans

## Slide 27: Reasonable Assurance (4b) Plans
Basic Requirements:
  Description of Impaired Waterbody
  Description of Water Quality or Aquatic Ecological Goals
    The water quality – based targets or aquatic ecological goals (both interim and final) that have been established for the pollutant(s) of concern.
  Description of Proposed Management Actions To Be Undertaken
    Schedule for restoration projects, including funding sources
  Description of Procedures for Monitoring and Reporting Results
  Description of and Commitment to Proposed Corrective Actions

## Slide 28: Course of Action
Develop a RA Plan
Submit to the Department for Approval
RA Plan is approved by the Department and adopted by the Secretary
Updates are provided to the Department based on the schedule established in the plan
Updates are reviewed for confirmation of reasonable progress
Implementation of plan continues until targets are achieved

## Slide 29: Reasonable Assurance Plans
We currently have 5 Reasonable Assurance (or 4b plans) that have been adopted.

## Slide 30: Reasonable Assurance Plans
Main inclusions in a Reasonable Assurance Plan:
A restoration target (e.g. water quality, pollutant load)
A list of projects and/or activities that will achieve the restoration target
An implementation schedule that can span multiple years
Funding commitments
Requires U.S. Environmental Protection Agency (EPA) approval
Reasonable Assurance plans (4b) provide an implementation schedule and resource commitments that there are, or will be, pollutant loading reductions that will result in the waterbody achieving water quality targets to attain and maintain the designated use.

## Slide 31: Watershed Restoration
Done altogether in an RA Plan.

## Slide 32: Category 4e Plans

## Slide 33: Pollutant Reduction Plans
Main points of a Pollutant Reduction Plan:
A restoration target is typically the water quality criterion
Planned or on-going restoration activities
A list of projects and/or activities that will achieve the restoration target
An implementation schedule
Expected to attain water quality standards by the next time the waterbody is assessed by DEP (e.g. 5 years)
Does not require EPA approval
Pollutant reduction plans (4e) provide a demonstration that there are, or will be, management actions in place that will result in the waterbody achieving water quality targets (e.g. assessment thresholds or water quality standards) to attain the designated use before the next assessment cycle.

## Slide 34: Plan Development
Development of these plans is stakeholder driven
DEP has resources to assist stakeholders
  Facilitation
  Technical Analysis
  Review and Feedback

## Slide 35: Surface Water Grant (SWAG) Considerations https://floridadep.gov/wra/319-tmdl-fund
State grant for projects that reduce stormwater pollutant loadings in impaired waterbodies
~$5 million total is appropriated annually to DEP through the Florida legislature
“Shovel ready” capital improvement projects for treating waters not attaining standards (i.e., impaired)
New combined project proposals for all NPS grants, will be accepted year-round
Project selection expected twice per year
  Generally March-April and October-November
No set maximum or minimum funding request caps
No match required
  Cost sharing encouraged for project prioritization