## Slide 1: FDEP Cyanobacteria HAB Sampling Training
Dave Whiting, Deputy Director
Division of Environmental Assessment and Restoration
Florida Department of Environmental Protection
March 10, 2022

## Slide 2: CyanoHAB Surveillance
Bloom reports are reviewed daily
Sampling locations are prioritized based on potential for human exposure/harm, representativeness of multiple reports, previous sampling history and analysis results, personnel
Emails and phone calls are made to coordinate sampling among DEP, WMDs, FWCC, and participating county field staff
Agency Staff Coordination

## Slide 3: CyanoHAB Sampling
The where, when, and whys of the State’s cyanoHAB sampling strategy

## Slide 4: CyanoHAB Sampling
Florida’s total water area covers 4,308 square miles and ranks third in the nation [AK and MI]
The state has more than 11,000 miles of rivers, streams, and waterways
Florida has about 7,700 lakes that are larger than 10 acres
Florida’s coastline stretches 1,197 miles with 663 miles of beaches
http://www.psc.state.fl.us/Files/PDF/Publications/Consumer/Brochure/WMF.pdf
https://www.stateofflorida.com/facts.aspx
Water, water everywhere

## Slide 5: CyanoHAB Sampling
Large number/area of Florida’s aquatic resources makes intensive statewide HAB monitoring efforts cost prohibitive
Without intensive sampling, we can never say with high confidence, what is happening in everyone’s backyard due to the heterogeneity of our cyanobacteria HABs
Water, water everywhere

## Slide 6: CyanoHAB Sampling
Public health protection
Aquatic resource protection/management
To try to understand the factors that contribute to occurrence, persistence, severity, and decline of HABs
To determine if there are ways to effectively mitigate HABs when they occur
To be able to predict when HABs will occur
Why do we sample HABs?

## Slide 7: CyanoHAB Sampling
What gets collected?
Photo by FDEP, June 23, 2016, Leighton Park
Photo by FDEP, June 12, 2019 Flint Creek
Photo by FDEP, June 24, 2019, Manatee River
Representative water samples
Occasionally, scum samples are collected when cyanobacterial scum is dominant in the waterbody being sampled
Photo by FDEP, June 29, 2016, St. Lucie River

## Slide 8: CyanoHAB Sampling
Why collect “representative” rather than “worst case” samples?

## Slide 9: CyanoHAB Thresholds
EPA’s 2018 and World Health Organizations 2020 recommended cyanotoxin thresholds are based solely on incidental ingestion by children during normal recreational activity (i.e., swimming pool study) and only use toxicological data for MC-LR
Do not account for any other exposure routes (i.e., inhalation, dermal, fish/shellfish consumption)
How much is too much?

## Slide 10: CyanoHAB Thresholds
EPA recommended Criteria
World Health Organization thresholds
Calculation of provisional recreational water GV for MC-LR: = NOAEL ∗ bw UF ∗ C = 40 ∗ 15 100 ∗ 0.25 µg/L =
24 µg/L
where GVrecreation = guideline value for recreational exposure NOAEL = no-observed-adverse-effect level (40 μg/kg bw/day, based on Fawell et al., 1999) bw = body weight (default = 15 kg for a child) UF = uncertainty factor (100 = 10 for interspecies variation × 10 for intraspecies variation) C = daily incidental water consumption (default = 250 mL for a child)

## Slide 11: Cyanotoxins

## Slide 12: CyanoHAB Thresholds
Florida Department of Health does not use a numeric toxin threshold value for advisories
  Presence/Absence of Cyanobacteria bloom or toxins
Advise the public to avoid recreating and allowing pets or livestock in waters with visible algae present
Cyanobacteria bloom conditions change rapidly
Unable to sample, ship, analyze, and disseminate results rapidly enough to accurately inform the public about the risk of recreating in a water at the time of use
Usually takes 3 – 4 days from sampling to posting of results
The Precautionary Principle

## Slide 13: CyanoHAB Thresholds
Sampling a bloom doesn’t change the nature of the bloom, anymore than measuring the size of hailstones changes a storm event
Sampling does tell us something about the relative risk of a bloom, the same as knowing the size of hailstones tells us about the relative risk of the storm event

## Slide 14: CyanoHAB Sampling
Why not collect
“representative” and “worst case”
all the time?

## Slide 15: CyanoHAB Sampling
Presence of scum can be very ephemeral and change concentration by orders of magnitude within minutes or a few meters
Recreational advisory thresholds are based on concentration of toxin in water, not scum
Workload, cost, and speed of analytical turnaround a factor as well

## Slide 16: CyanoHAB Sampling
We collect water samples at the edge of scum when it is present and represents a small area of the sampling location (sort of worst case of representative condition)
We collect homogenized scum when it is dominant and representative of the sampling location
Photo by FDEP, Lake Munson, Leon County

## Slide 17: CyanoHAB Sampling
Cyanotoxins
  Microcystins (LR, RR, YR, LA, LF, LY, LW, WR, desmethyl LR, HilR and HtyR)
  Anatoxin-a
  Cylindrospermopsin
  Saxitoxins (in some waters)
Algal Identification
Chlorophyll a
Nutrients
What gets analyzed?

## Slide 18: CyanoHAB Sampling
FS 7000. GENERAL BIOLOGICAL COMMUNITY SAMPLING
  FS 7110. PHYTOPLANKTON BLOOM SAMPLING
  FS 7240. ALGAL MAT SAMPLING FOR TAXONOMIC IDENTIFICATION OR TOXIN ANALYSIS
  FS 7230 RAPID PERIPHYTON SURVEY
AB-17 Algal Bloom Response
AB-FIELD Cyanobacteria Bloom Response Field Data Sheet
AB-NOTIFY Algal Bloom Notification Form
What Standard Operating Procedures
Are Used?

## Slide 19: CyanoHAB Sampling
Private Ponds and Lakes?
Municipal stormwater ponds?
Residential development retention ponds?
Rivers and streams?
Public lakes?
Waters of the State?
Estuaries, Intercoastal waterways, and beaches?
We have occasionally sampled waterbodies that are not known to be Waters of the State if there is high potential for significant public exposure
Which waterbodies do we sample?
NO
NO
NO
YES
YES
YES
Sometimes

## Slide 20: Bloom Sample Types:
First, what is Scum?
A scum is a consolidated layer of algae floating on the water’s surface.
It is not streaks or specks.
It is not thick, green “soup”.
Surface Scum
20

## Slide 21: Bloom Sample Types:
Mix the surface scum of a 0.5 m area with the underlying water to mimic recreational exposure.
  For example, swimming or jet skiing would mix the upper scum layer into the underlying water
Collected in the top 5-10 centimeters of the water column.
Do not collect the sample by skimming the surface.
DEP bloom response does include this method, if appropriate to do so. (Refer to representative sampling).
Surface Scum
21

## Slide 22: Scum Sampling
Requires some judgement
22
Consolidated surface scum
Whole water column bloom or disturbed surface scum?

## Slide 23: Bloom Sample Types:
We sometimes get HAB reports that turn out to be pollen rather than cyanobacteria or algae.
Surface Scum
23
Lake Bradford, Tallahassee, Florida February 12. 2021

## Slide 24: CyanoHAB Sampling
Bloom reported to Hotline
No bloom observed upon visit
Sample/Not Sample?
Let’s play “Where do we sample?”

## Slide 25: CyanoHAB Sampling
Take a representative sample
Let’s play “Where do we sample?”

## Slide 26: CyanoHAB Sampling
What if there was an area of scum along a portion of the shoreline?
Let’s play “Where do we sample?”

## Slide 27: CyanoHAB Sampling
Collect a grab sample of water at edge of scum
Let’s play “Where do we sample?”

## Slide 28: CyanoHAB Sampling
What if there was a boat ramp, designated beach area, or other point of high recreational use?
Let’s play “Where do we sample?”
Beach

## Slide 29: CyanoHAB Sampling
Sample at edge of scum and at recreational area
Let’s play “Where do we sample?”
Beach

## Slide 30: CyanoHAB Sampling
What if a sizable portion of the lake was covered in scum?
Let’s play “Where do we sample?”

## Slide 31: CyanoHAB Sampling
What if a sizable portion of the lake was covered in scum?
Collect a grab sample at edge of scum AND a scum sample
Let’s play “Where do we sample?”

## Slide 32: CyanoHAB Sampling
What if the scum was affecting a portion or all of the recreational area?
Let’s play “Where do we sample?”

## Slide 33: CyanoHAB Sampling
Collect a grab sample at the edge of the scum AND a scum sample within the recreational area
Let’s play “Where do we sample?”

## Slide 34: CyanoHAB Sampling
What if the scum is much worst outside of the recreational area?
Let’s play “Where do we sample?”

## Slide 35: CyanoHAB Sampling
Remember, DOH only uses the presence of toxin for their Health Alerts, not the amount
Collect scum within the recreational area
Let’s play “Where do we sample?”

## Slide 36: CyanoHAB Sampling
Residential Canal in a development with scum present
Canal does not connect to Waters of the State
We don’t sample, refer to county or local government agency
Let’s play “Where do we sample?”

## Slide 37: CyanoHAB Sampling
Residential Canal in a development with scum present
Canal does connect to Waters of the State
Let’s play “Where do we sample?”

## Slide 38: CyanoHAB Sampling
Residential Canal in a development with scum present
Canal does connect to Waters of the State
Collect Grab sample at edge of Scum
Let’s play “Where do we sample?”

## Slide 39: CyanoHAB Sampling
Residential Canal in a development with scum present
Canal does connect to Waters of the State
Let’s play “Where do we sample?”

## Slide 40: CyanoHAB Sampling
Residential Canal in a development
Canal does connect to Waters of the State
Collect both a Scum and Grab sample
Let’s play “Where do we sample?”

## Slide 41: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Let’s play “Where do we sample?”

## Slide 42: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Collect a grab sample in the area with streaks present
Grab taken from streak is fine so long as it’s a streak and not a scum
Let’s play “Where do we sample?”

## Slide 43: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Scum accumulated along the shoreline
Let’s play “Where do we sample?”

## Slide 44: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Scum accumulated along the shoreline
Collect grab in area of streaks and edge of scum
Let’s play “Where do we sample?”

## Slide 45: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Scum accumulated along the shoreline
Let’s play “Where do we sample?”

## Slide 46: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Scum accumulated along the shoreline
Scale Matters
Let’s play “Where do we sample?”

## Slide 47: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Scum accumulated along the shoreline
Collect grab in area of streaks and edge of scum
Let’s play “Where do we sample?”

## Slide 48: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Scum accumulated along the shoreline
Let’s play “Where do we sample?”

## Slide 49: CyanoHAB Sampling
Flowing waters with streaks of cyanobacteria at the surface and within the water column
Scum accumulated along the shoreline
Collect Grab in area of streaks and Scum sample (possibly Grab edge of scum)
Let’s play “Where do we sample?”

## Slide 50: Recent Examples
Harbor Isle Lake
NW Lobe South Lobe
50

## Slide 51: Recent Examples
Lake Montgomery
51

## Slide 52: Resampling Frequency
52
Lake | Sampling Date | Microcystin Result (µg/L) | Keep Sampling?
Anderson | 2/17/2020 | 34 | ?
 | 3/9/2020 | 4.7 | 
 | 11/19/2020 | 1.2 | 
 | 12/10/2020 | 2 | 
Jennie Jewel | 2/17/2020 | 150 | ?
 | 2/26/2020 | 2.4 | 
 | 3/9/2020 | 8.5 | 
 | 5/18/2020 | not detected | 
Arnold | 2/25/2020 | 1.6 I (I) | ?
 | 3/3/2020 | 1.8 I (I) | 
 | 3/10/2020 | 0.74 I (I) | 
 | 4/15/2020 | not detected | 

## Slide 53: What happens with the Results?
Results are posted to the DEP Algal Bloom Dashboard
DOH reviews daily and contacts local county health departments

## Slide 54: DOH CyanoHAB Signage
Caution notifications issued when cyanobacteria present but toxins not detected
Human Health Alerts issued when cyanotoxins detected

## Slide 55: DOH CyanoHAB Signage
Daily email from DOH regarding cyanobacteria results includes a table to help local health departments with decisions regarding the need for notifications
DOH Blue-Green Algae Daily Update for Florida February 19, 2021 Listings below based on information downloaded 2/19/2021 7:40:51 AM |  |  |  |  |  | 
County | Sites with Bloom Present | Sites with Toxins Detected | Follow-up Sample Found No Toxins | Pending Toxin Results | No Longer Pending No Toxins Detected | Point Map Photo
Brevard | - | - | - | Lake Washington - Center (LWC) | Lake Washington - Center (LWC) | Point Map Photo
Leon | - | - | - | - | Lake Bradford - Western Shore | Point Map Photo
Okeechobee | - | - | - | Lake Okeechobee - LZ2 | - | Point Map No Photo
Orange | - | Lake Conway @ SW Shore | - | - | - | Point Map Photo
Orange | - | Lake Holden 90m S of Lake Holden Point | - | - | - | Point Map Photo
Orange | - | Lake Anderson - NW Corner | - | - | - | Point Map No Photo
Pinellas | - | - | - | - | Round Lake | Point Map Photo
Putnam | - | - | - | Crescent Lake-mouth of Dunns Creek (CRESLM) | - | Point Map No Photo
Putnam | - | - | - | Crescent Lake - mouth of Dunns Creek (CRESLM) | - | Point Map No Photo
Volusia | - | - | - | Lake George - Center (LEO) | Lake George - Center (LEO) | Point Map No Photo

## Slide 56: DOH CyanoHAB Signage
Caution signs, when used, may stay out until cyanobacteria not observed or until the end of the normal recreational season depending on county
Health Alert signs, when used, stay out until cyanotoxins are no longer detected
When only trace levels detected for extended period of time (6 sampling events), the county may remove the Health Alert sign

## Slide 57: Summary
Collaborative effort to respond to bloom reports
Collection and analysis of representative samples (which may include scum samples) to provide information on the risk to public health
Scale of bloom matters as to how you sample
DEP posts results to the Algal Bloom Dashboard to disseminate results to DOH and the public, usually within 3-4 days of sample being collected
County DOH staff issue Caution and Health Alerts, press releases and may post signage

## Slide 58: Thank you
Lab Staff
Communications
Division Office
ROC Teams
GIS Staff
FWRI
County and local
Public Services
SFWMD
DOH
SJRWMD