## Slide 1: Sampling and Application of the Stream Condition Index
Aquatic Ecology and Quality Assurance
2018

## Slide 2: SCI and Accompanying Protocols
Stream Condition Index
  Collection of organisms to be identified in the lab, metrics calculated from taxa list
Habitat Assessment
  Information critical to explaining SCI failures
Companion biological assessments
  Rapid Periphyton Survey
  Linear Vegetation Survey

## Slide 3: Course Overview
Provide conceptual information on the SCI and its development
Define expectations for samplers
  Site selection
  Habitats
  Water level issues
  Sampling techniques
Provide hands-on training
  Sweep and sort in field
  Habitat assessment

## Slide 4: History of Bioassessment in Florida
Beck’s Biotic Index, 1950s
Shannon-Weaver diversity, 1970s
  Biological integrity (Rule 62-302.500 FAC)
EPA Rapid Bioassessment using multi-metric index (Jim Karr approach), 1992
  Original Stream Condition Index, 1996
    Reference vs. test
  Current Revised SCI, 2007
    Human Disturbance Gradient
    Biological Condition Gradient

## Slide 5
Point Source Discharge
Upstream
Downstream
Beck’s Biotic Index
(# Pollution Sensitive Taxa)
Percent Pollution
Tolerant Chironomids
0
10
20
0
50
100
Typical Macroinvertebrate Response to Organic Loading Associated with Primary Wastewater Treatment, Typical in the 1950s and 1960s.

## Slide 6
Hester-Dendy samplers used for determining the Shannon-Weaver diversity index.

## Slide 7: Bioassessment Theory
Biota respond to a wide variety of cumulative factors, both natural and anthropogenic.
As the organisms integrate factors over time, a characteristic community structure emerges.
When human actions adversely affect a system, the biological population will change, leading to an impaired or imbalanced community.

## Slide 8: Human Stressors &Natural Factors Shape Biota
Biota
Producers: Algae, macrophytes, terrestrial
plant leaf litter, bacteria/detritus
1° Consumers:
Benthic invertebrates, zooplankton,
some fish
2°
Consumers:
Fish, wildlife, humans
Water quality factors
Physical factors
Human factors
pH
Dissolved Oxygen
Conductivity/Salinity
Light penetration
Temperature
Hydrology/flow
Habitat structure
Sediment/substrate
Nutrients
Desiccation
Major ions
Organic carbon
Toxic substances
Organic enrichment
Nutrient enrichment
Degradation of water quality:
Habitat disruption:
Physical destruction
Siltation/Sedimentation
Hydrological modifications
Ditching/draining
Impounding
Consumptive use
Introduction of exotics,
Harvesting game species

## Slide 9: Adverse Human Factors
Hydrologic modifications
  Consumptive use, impounding, ditching/draining
Habitat disturbance
  Physical removal, sedimentation
Degradation of water quality
  Toxic substances, nutrient and organic enrichment
Introduction of invasive exotic taxa
  Displaces natives
Harvesting biomass
  Disturbing predator-prey relationships

## Slide 10: Interpreting Bioassessment Results
Measures of ecosystem health that respond predictably to human influence = metrics.
Comparing reference to "test" sites allows determination of unacceptable departures from the expected condition.
The systems being compared should be similar except for potential human influences.
Natural stressors (e.g., flood vs. drought) should be understood, and controlled for in the sampling design, to determine when human actions cause biological degradation.

## Slide 11: Using the Human Disturbance Gradient to Develop SCI Metrics
Objectively quantify relative level of human influence based on four factors:
Landscape disturbance
  Landscape Development Intensity Index
Habitat alteration
  Habitat assessment data
Hydrologic modification
  Hydrologic scoring process
Chemical Pollution
  Ammonia, etc.

## Slide 12: Landscape Development Intensity Index (Brown and Vivas 2004, UF Center for Wetlands)
Specific landuse near a waterbody receives a score from good (1) to bad (10). Based on non-renewable human energy inputs.

## Slide 13
Summary of the Landscape Development Intensity Coefficients
Category Coefficient
Natural System 1
Pine Plantation 1.6
Pasture 3.4
Row Crops 4.5
Residential (low) 6.8
Residential (high) 7.6
Commercial 8.0
Industrial 8.3
Commercial (high) 9.2
Business District 10.0
  Based on non-renewable Energy inputs, Odom’s “Embodied Energy” concept.
Notes: Pass out complete table of coefficients.
Ranking of land use comes from the literature reviews primarily Harper (1994) and Beaulac and Reckhow (1982)

## Slide 14: Habitat Assessment Components
Substrate Types
Substrate Availability
Water Velocity
Artificial Channelization
Habitat Smothering
Bank Stability
Riparian Zone Buffer Width
Riparian Zone Vegetation Quality
Optimal
Poor
20 points
1 point

## Slide 15: HDG as the x- axis
These components were converted into a dimensionless index, with low values denoting low disturbance, and increasing values associated with more intense human influences.
The index was subsequently used as the x-axis for testing a wide variety of biological attributes associated with the measurement of ecological integrity

## Slide 16
SYSTEM
PROCESSES
IDENTITY
TOLERANCE
RARE OR ENDANGERED KEY TAXA
TAXONOMIC
COMPOSITION
TROPHIC
DYNAMICS
PRODUCTIVITY
MATERIAL:
CYCLES
PREDATION
RECRUITMENT
TAXA
RICHNESS
RELATIVE
ABUNDANCE
DOMINANCE
COMMUNITY
STRUCTURE
FEEDING
GROUPS
HABIT
VOLTINISM
INDIVIDUAL
CONDITION
DISEASE
ANOMALIES
CONTAMINANT LEVELS
DEATH
METABOLIC
RATE
TOXICITY TESTS
INVERTEBRATE SCI
INTEGRATED
BIOASSESSMENT
LIFE HISTORY
ATTRIBUTES
Major Attribute Categories for Determining Biological Integrity

## Slide 17: Metric Selection
The 10 selected metrics were chosen to:
Represent as many attribute categories as possible
Provide meaningful and predictable assessment of human effects
Avoid redundancy if several correlated metrics were providing similar information.

## Slide 18
Correlation between various metrics and the Human Disturbance Gradient. Arrows indicated metrics selected for the SCI, and associated attribute group.
voltinism
feeding
structure
composition
richness
richness
tolerance
tolerance
habit
0.00
0.10
0.20
0.30
0.40
0.50
0.60
0.70
0.80
0.90
Sensitive taxa
EPT taxa
Florida Index
Clinger taxa
Very Tolerant %
All Tolerant %
Trichop taxa
Eph taxa
Very tolerant taxa
Clinger %
Eph %
Trichop %
Total Taxa
Tanytarsini %
Filter-feeder no Chuemat.
Dominant %
Filter-feeder %
Tanytarsini %
Diptera taxa
Tanytarsini taxa
Long lived %
Absolute Spearmans r

## Slide 19: Taxa Richness Metrics
Total taxa richness (the number of different types of organisms present).
Trichoptera richness (caddisflies).
Ephemeroptera richness (mayflies).
These three measures have historically been shown to decrease with human disturbance.
Three richness metrics were chosen since each one may respond differently, depending on the type of disturbance.
Mayflies are more sensitive to metals, certain caddisflies may be more sensitive to flow disruption.

## Slide 20
Ephemeroptera Metric. The photo is of Tricorythodes, a sensitive mayfly.
Human disturbance gradient

## Slide 21: Trichoptera Taxa. The photo is of a caddisfly, Brachycentrus.

## Slide 22: Taxa Richness

## Slide 23: Feeding Groups Metric
Disruption of food webs has long been associated with human influence, especially organic pollution.
The relative abundance of filterers (percentage filterer individuals) had the highest correlation and most consistent relationship with the HDG.
Filter feeders extract nutrients by straining food particles from the water column. If the water flow or quality of the organic matter in the water is compromised, a reduction in filter feeders will occur.

## Slide 24
Human disturbance gradient
% Filter-feeders Metric. The photo is of a net-spinning caddisfly.

## Slide 25: Voltinism Metric
Voltinism refers to the number of distinct reproductive cycles for a given organism per unit of time.
Long-lived taxa require greater than one year to complete their life cycles.
Long-lived taxa richness would be expected to decrease if a disturbance event (e.g., sporadic illegal dumping, etc.) occurred at a site within a year of sample collection.

## Slide 26
Human disturbance gradient
Long-lived Taxa Metric. The photo is of a mollusk, the threatened “purple bank climber”.

## Slide 27: Organism Habit Metric
Clingers are those taxa morphologically adapted to hold onto substrates during routine flow conditions, and would be expected to decline as humans alter a stream’s hydrograph, especially during abrasive events caused by high stormwater inputs from impervious surfaces.

## Slide 28
Clinger Taxa Metric. The photo is of a damselfly larvae.

## Slide 29: Community Structure Metrics
Substantial shifts in proportions of major groups of organisms, compared to reference conditions, indicate degradation.
The percent dominant taxon, which increases in conditions where a few pollution tolerant organisms are very abundant, to the exclusion of other taxa, was selected as a metric.
Tanytarsini midges are sensitive to disturbance, including toxic metals. % Tanytarsini metric was included in the SCI as the best available measure of the chironomid assemblage.

## Slide 30: % Dominance Metric. Photo is Hyalla azteca, a tolerant amphipod.
Human disturbance gradient

## Slide 31: % Tanytarsini (Sensitive midges)

## Slide 32: Tolerance Metrics
A list of sensitive and very tolerant invertebrates were established by analyzing the responses of 1,200 individual species to the HDG.
The number of taxa selected as sensitive equaled around 12% of the taxa tested, and the number of very tolerant taxa was approximately 10% of the taxa tested.
Many sensitive taxa belonged to the Ephemeroptera, Trichoptera or Odonata; several chironomids were also included. All the Plecoptera were included as sensitive taxa.
The number of sensitive taxa and the percent very tolerant taxa were highly correlated with the HDG

## Slide 33
Sensitive Mayfly (Maccaffertium) vs. HDG
Increasing disturbance 

## Slide 34
Human disturbance gradient
Sensitive Taxa Metric. The photos include a plecopteran (stonefly) and odonate (dragonfly).

## Slide 35
% Very Tolerant Metric. Photos include lunged snails, tolerant midges, and leeches.

## Slide 36: Linking the Human Disturbance Gradient to SCI Thresholds
“Exceptional”
34
“Healthy”
“Impaired”
67
These zero HDG sites were selected by DEP District biologists to represent the very healthiest streams in Florida, experiencing minimal human disturbance. The majority are “healthy”, about 40% are “exceptional”.
40

## Slide 37: Establishing SCI Thresholds for Impairment
Biological Condition Gradient Approach
Reference Site Approach

## Slide 38
The Biological Condition Gradient Concept
Increasing Effect of Human Activity
Biological Condition
Natural structure & function of biotic community maintained
Minimal changes in structure & function
Evident changes in structure and minimal changes in function
Moderate changes in structure & minimal changes in function
Major changes in structure & moderate changes in function
Severe changes in structure & function
1
2
3
4
5
6
Notes: This figure is a generalized representation of the BCG. In your handout you have the detailed and complete BCG and the HDG. These are the two components of the model that describe the biological response (BCG) to increasing effects of human activity (HDG)..
The gradient of biological responses spans a range of condition - from natural, undisturbed conditions to severely y degraded. There are 6 tiers, or increments of biological change, along the gradient.
Key Points:
1. It is intended to be uses as the starting point for States and Tribes to think about how to more accurately describe the condition of a waterbody and to establish appropriate goals; the 6 tiers represent incremental, measurable changes along this gradient; it is up to the States and Tribes to determine number of tiers and where thresholds established.
2. The model is applicable to different places (geography); different methods; across political boundaries (incorporate into existing State and Tribal programs).

## Slide 39
Chemistry, habitat, and/or flow regime severely altered from natural conditions.
  Watershed, habitat, flow regime and water chemistry as naturally occurs.
The Biological Condition Gradient: Biological Response to Increasing Levels of Stress
Structure & function similar to natural community with some additional taxa & biomass; ecosystem level functions are fully maintained.
Evident changes in structure due to loss of some rare native taxa; shifts in relative abundance; ecosystem level functions fully maintained.
Moderate changes in structure due to replacement of sensitive ubiquitous taxa by more tolerant taxa; ecosystem functions largely maintained.
Sensitive taxa markedly diminished; conspicuously unbalanced distribution
of major taxonomic groups; ecosystem function shows reduced complexity & redundancy.
Extreme changes in structure and ecosystem function; wholesale changes
in taxonomic composition; extreme alterations from normal densities.
Natural structural, functional, and taxonomic integrity is preserved.
Levels of Biological Condition
Level of Exposure to Stressors
5
6
4
3
2
1
Biological Condition

## Slide 40: 10 BCG Attributes Extracted from Site Community Information
Historically documented, sensitive, long-lived or regionally endemic taxa
Sensitive and rare taxa
Sensitive but ubiquitous taxa
Taxa of intermediate tolerance
Tolerant taxa
Non-native taxa
Organism condition
Ecosystem functions
Spatial and temporal extent of detrimental effects
Ecosystem connectance

## Slide 41: BCG Ranking Criteria
Natural or native condition
Minimal changes in structure of the biotic community and minimal changes in ecosystem function
Evident changes in structure of the biotic community and minimal changes in ecosystem function
Moderate changes in structure of the biotic community with minimal changes in ecosystem function
Major changes in structure of the biotic community and moderate changes in ecosystem function
Severe changes in structure of the biotic community and major loss of ecosystem function

## Slide 42: BCG Experts
Expert name |  | Affiliation | Years
Jerrell | Daigle | DSA, Inc. | >20
Dana | Denson | FDEP Central District | 10-15
Doug | Durbin | Biological Research Associates | >20
John | Epler | John Epler Consulting | >20
Julie | Espy | FDEP Tallahassee | 5-10
David | Evans | Water and Air Research | >20
Michael | Heyn | FDEP Tallahassee | >20
Joy | Jackson | FDEP Tallahassee | 10-15
Deron | Lawrence | Biological Research Associates | 10-15
Laura | Line | Water and Air Research | 10-15
Rob | Mattson | St. Johns River Water Management District | >20
Peggy | Morgan | FDEP Southwest District | >20
Patrick | O'Connor | FDEP Northeast District | >20
Manuel | Pescador | Florida Agricultural and Mechanical University | >20
Marianne | Pluchino | Reedy Creek Improvement District | >20
Eric | Pluchino | FDEP Orlando District | >20
Donald | Ray | FDEP Northwest District | >20
Johnny | Richardson | Leon County | 10-15
Gitta | Schmitt | FDEP Southwest District | 5-10
Mary | Szafraniec | Southwest Florida Water Management District | 5-10
Albert | Walton | FDEP South District | >20
Gary | Warren | Florida Fish and Wildlife Commission | >20

## Slide 43: Proportional Odds Model Assignment of BCG Category vs. SCI Score

## Slide 44: BCG Workshop (October 24, 2006)
Experts independently ranked 30 data sets.
Consistency discussions occurred (Delphi Technique).
Provided expert opinion on where “impairment” line (not meeting interim goal of CWA) existed in rankings.
Later, expert rankings were used to modify the SCI thresholds
  Regression
  Change Point Analysis

## Slide 45: Linear Regression Model

## Slide 46
A Tier 1-2 Community “Minimally disturbed”
1 inch
Notes: This is an example of what a field biologist will be measuring – who is there, how many and what proportion of the community.
Example of first site – the undisturbed or minimally disturbed site. This represents a tier 1 community.
Blue: Most Sensitive/intolerant organisms
Green: Sensitive, can tolerant some degree of stress
Red: Tolerant

## Slide 47
A Tier 1-2 Community “Minimally disturbed”
Caddisflies
Mayflies
Stoneflies
1 inch
Notes: This is an example of what a field biologist will be measuring – who is there, how many and what proportion of the community.
Example of first site – the undisturbed or minimally disturbed site. This represents a tier 1 community.
Blue: Most Sensitive/intolerant organisms
Green: Sensitive, can tolerant some degree of stress
Red: Tolerant

## Slide 48
A Tier 1-2 Community “Minimally disturbed”
Beetles
Dragonflies,Damselflies
Caddisflies
Mayflies
Stoneflies
1 inch
Notes: This is an example of what a field biologist will be measuring – who is there, how many and what proportion of the community.
Example of first site – the undisturbed or minimally disturbed site. This represents a tier 1 community.
Blue: Most Sensitive/intolerant organisms
Green: Sensitive, can tolerant some degree of stress
Red: Tolerant

## Slide 49
A Tier 1-2 Community “Minimally disturbed”
Midges
Beetles
Dragonflies, Damselflies
Caddisflies
Mayflies
Stoneflies
1 inch
Notes: This is an example of what a field biologist will be measuring – who is there, how many and what proportion of the community.
Example of first site – the undisturbed or minimally disturbed site. This represents a tier 1 community.
Blue: Most Sensitive/intolerant organisms
Green: Sensitive, can tolerant some degree of stress
Red: Tolerant

## Slide 50
Stoneflies
Mayflies
Blackflies
Midges
Non-insects
Crane flies
Beetles
A Tier 3 Community “evident/moderate disturbance”
1 inch
Caddisflies
Notes: Ex of a moderately disturbed site
Nutrient enriched site. You see more of everything – increase in abundance, typical signal of low to moderate nutrient enrichment. Also see a beginning shift in community composition – increase in tolerant species. These changes are visually evident, measurable and statistically significant.

## Slide 51
A Tier 5-6 Community “Highly/Severely Disturbed”
Caddisflies
Snails
Midges
Leeches
Scuds
Beetles
Craneflies
1 inch
Notes: Downstream of a shopping mall, storm sewer outlet – a representative community where the more tolerant assemblages dominate.
Comtinuing along the gradient – to heavily and severaly disturbed sites, major shift in community composition and function.

## Slide 52: Reference Site Approach
Defining reference condition using minimally disturbed sites recognizes that natural stressors can affect the biology of a stream, introducing variability into the reference site data distribution.
Natural drought will cause dry or stagnant flow conditions.
High water, or floods, will limit the effectiveness of the sampling method.
Substrate diversity at some reference sites may be naturally limiting

## Slide 53: Reference Selection Criteria
Landscape Development Intensity Index < 2.
Habitat Assessment Index > 75% of total points.
Ammonia < 0.1 mg/L.
Hydrologic Index <6.
Exclude sites with average conductivity > 600 umhos/cm (eliminate “tidal” influence).
Exclude sites receiving NPDES-permitted wastewater treatment facility discharges, based on a review of GIS coverage information from the Water Facilities Regulation (WAFR) database.
Use samples with number of individuals identified ranging from 100-175 (inclusive).

## Slide 54: Category III (“Impairment”) Line Based on Reference Sites
Analysis to balance Type I and Type II errors given the inherent statistical error of the method.
The examination of the two most recent visits at 55 reference streams showed that the 2.5th percentile of reference data was in the range of 35-44 points. The middle of this range was 40 points, which represents an impairment threshold that balances Type I and Type II errors.

## Slide 55: Establishing SCI Thresholds for Impairment
Biological Condition Gradient Approach
  Workshop in 2006 with Florida experts
  SCI = 35 was the lowest score that still meets CWA (BCG category 4)
Reference Site Approach
  55 reference streams chosen through rigorous selection process
  SCI = 40 determined to be protective

## Slide 56: Using Multiples Lines of Evidence to Set the Exceptional Category
Biological Condition Gradient Approach concluded that SCI scores of 64 and above were similar to natural (minimally disturbed).
Reference site approach yielded 70.6.
Averaging these complimentary approaches= 67.

## Slide 57: Objectives Affect SCI Sampling Decisions and Interpretation of Results – from SCI PRIMER
Biota respond to natural and human stressors alike.
Study objectives must be clearly articulated, and you must control for confounding factors that may interfere with the appropriate interpretation of the SCI scores.
Especially consider:
  existing and antecedent flow conditions,
  habitat conditions, and
  water quality issues.

## Slide 58: Example TMDL Objective
Determine if water quality issues are adversely affecting biological health.
To place a waterbody on the verified list, must reasonably demonstrate the pollutant responsible for poor SCI scores.

## Slide 59: Factors to Control For During TMDL Sampling
Current and antecedent flow conditions
  If desiccation or stagnant conditions have occurred, the flow regime, NOT water quality, will be dominant influence
Habitat conditions at sampling site
  By sampling where habitat is NOT limiting, you can emphasize water quality factors

## Slide 60: BMP Effectiveness Example
Employed a “Before-After/Control-Impact” study design.
Sites were selected where habitat and water quality were currently acceptable to determine if silviculture practices caused harm.
  Controlled for prior habitat and water quality conditions to emphasize human activities and BMPs.

## Slide 61: Experimental Design
Proposed
Silviculture
Area
Control
Site
Test Site
A
B
C
A
B
C
Flow
1996
Control
Site
Test Site
A
B
C
A
B
C
Silviculture
with BMPs
Flow
1997, 1998
Before
Silviculture
Activities
After
Silviculture
Activities

## Slide 62
C 96
T 96
C
2-97
T
2-97
C
7-97
T
7-97
C 98
T 98
0
5
10
15
20
25
30
35
Clearcutting (3 & 4-96),
Site Prep (6 to 9-96),
Replanting (1-97)
Good
Excellent
Herbicide
Application (5-15-97,
Velpar & Oust)
ANOVA: No significant time or
treatment differences
SCI results of a Before-After-Control-Impact study assessing the effectiveness of forestry Best Management Practices.

## Slide 63: Objectives for Other DEP Programs
BMP Effectiveness Studies
Point Source Studies
Stream Restoration Studies
Minimum Flows and Levels Studies
Status and Trends Monitoring Network

## Slide 64: Water Level and the SCI
Method can only effectively capture organisms residing in the top 0.5 m (reachable substrates).
As water level increases, there is a one month lag time for taxa to colonize substrates.
Aquatic organisms die if site goes dry, minimum of 3 month recovery period. Wait 6 months if you do not have information about recovery at that site.

## Slide 65
0.8 m
Water level during day of sampling trip.
Water level 2 weeks ago, which was stable for the previous 6 weeks.
Substrate suitable for sampling, however, not effectively reached with the dip net method. Abort sampling.
Substrate which has not yet been colonized by benthos since it was dry 2 weeks ago.
Schematic cross section of a stream showing recent increase in water levels indicating the SCI sampling should not be conducted.

## Slide 66
Hydrograph showing the reachable substrates have been inundated more than one month. This is a good time to sample SCI.
0
0.5
1.0
1.5
0 7 14 21 28 35 42 49 56 63 70 77 84 91
Day of site visit
Water level (m)
Days

## Slide 67
Recent increase in water level. Reachable substrates have been inundated for less than 2 weeks. Abort sampling.
0
0.5
1.0
1.5
0 7 14 21 28 35 42 49 56 63 70 77 84 91
Day of site visit
Water level (m)
Days

## Slide 68
Before
Before
After
After

## Slide 69
Before
After
Before
After

## Slide 70
Hydrograph showing times when substrates are reachable.
0
0.5
1.0
1.5
0 7 14 21 28 35 42 49 56 63 70 77 84 91
Water level (m)
Days
Sampling Windows

## Slide 71: SCI Samplers must exercise Best Professional Judgment
Only an experienced, qualified SCI sampler can make the difficult field decisions necessary for proper application of the method.
Samplers MUST understand objectives.
There should be no artificial burdens that prevent samplers from making the correct scientific decision
  Contract issues

## Slide 72: Maintaining Linkages between the SCI and Important Associated Data
All associated data (flow conditions, habitat scores, etc.) must be linked to the SCI results, so that a determination may be made that each sample was, or was not, consistent with the study objectives.
Indiscriminate use of SCI scores will likely result in inappropriate or incorrect environmental decisions.
Data analysts and managers have responsibility to fully understand the complexities associated with the SCI scores, and use the data appropriately.

## Slide 73: The SCI Sampling Process
Sampling Site Selection and System Classification
Appropriate Antecedent Hydrologic Conditions
Optimal Habitat Selection
Sampling Technique
Field Sorting as a Training Tool
Apprenticeship

## Slide 74: Relevant SCI Field SOPs
SCI 1100 (FS 7420) – sampling method
  Assess conditions and appropriateness for sampling, establish 100 m stretch
  Complete phys/chem and HA
  Determine productive habitats and perform 20 dipnet sweeps
  Contain sample in jug and preserve
SCI 1200, 1300 (FA 4310, 5700) contain training and proficiency requirements

## Slide 75: Sampling Site Selection and System Classification
Site should be appropriate for sampling objective.
  Compare stream to stream, not stream to swamp-like or lake-like areas.
  Unless MFL study, sample during some (0.05 m/sec) flow.
  Generally sample areas with representative conditions, not atypical areas
    Habitat and flow

## Slide 79: Appropriate Antecedent Hydrologic Conditions
Antecedent hydrologic conditions must be appropriate for the purpose of the study.
How long have habitats in the top 0.5 m of the surface been inundated?
  DO NOT sample recently dry habitats
Hydrographs from area streams should be carefully examined
Samplers need to develop intimate familiarity with the hydrology of streams in their regions.

## Slide 81: Optimal Habitat Selection
Target productive habitats (roots, woody debris, leaf material, macrophytes and rock)
To be “major”, must have surface area greater than 2 m2
Target optimal flow
Think like a bug

## Slide 82: Optimal Habitat Selection (cont.)
Stream taxa are rheophyllic
  Prefer areas with water velocity, which usually have higher DO and food availability
Texture and architecture
  Fine roots, peeling bark, nooks and crannies
Ensure habitats have been inundated

## Slide 83
Leaf packs/mats

## Slide 84: Roots

## Slide 85: Aquatic vegetation Rock

## Slide 86: Sampling Technique
Samplers absolutely must provide sufficient agitation of substrates to dislodge the organisms, and ensure that all organisms are captured (into the net) without loss.
  Dip net should always be placed perpendicular to the flow
  Agitate substrates with net very close
  Scrub into the net (not parallel)

## Slide 87: Sampling Technique (cont.)
  Vigorously shake and scrape all surfaces of the habitats at least 3 times, without organism loss
  Leaf packs are placed directly into the net and the organisms dislodged “one leaf at a time” before discarding excess leaves
    Box technique for measuring packs
  Penetrate sand with fingers, to approximately 2 cm deep, and using a pulling motion, draw the organisms from the sand into the waiting dip net
    Include partially buried bivalves

## Slide 88: Sampling Technique (cont.)
  Leaf packs are preferred over leaf mats, unless only mats available
  For leaf mats, only sample the top 1-2 cm to avoid the anoxic layers below
  Large rivers can be sampled from the bow of a boat (best for reachable snags in deep areas) or by wading along the shoreline

## Slide 89: 20 Dipnet Sweeps for SCI
Productive habitats – snags, roots, leaves, rock, aquatic vegetation (need 2m2 for “major”)
“Minor” sweeps are in sand, muck, and in productive habitats with < 2m2 cover.
# Major habitats | # Sweeps in Majors | # Sweeps in Minor
1 | 10 | 10
2 | 7,7 | 6
3 | 5,5,5 | 5
4 | 4,4,4,4 | 4
5 | 3,3,3,3,3 | 5

## Slide 90: Field Sorting as a Training Tool
Field sorting provides the sampler immediate feedback regarding the degree of success associated with the field decisions and sampling effectiveness.
Sort individual sweeps via white tray, and examine taxa with hand lens.
Field sorting not part of actual SCI (Biorecon only).

## Slide 91
Field Sorting Yields
Megalopteran,“Gator Flea”

## Slide 92: Apprenticeship
Experienced SCI samplers must contribute to the training of novice staff.
Goal is to produce SCI samplers with the necessary critical thinking skills and sampling technique required by the SOP.
Training should consist of numerous field visits (minimum of 10), at a variety of sites (starting at reference sites, followed by disturbed sites) and different water levels.

## Slide 93
https://floridadep.gov/dear/bioassessment/content/bioassessment-training-evaluation-and-quality-assurance#sci

## Slide 94: Training Log
Complete for minimum of 10 practice sites (include 3 low impact sites, 3 high impact sites)
Trainer signs off on training
Evaluator conducts a “mock audit” when training is complete to ensure readiness
Contact DEP for audit
Pass online test and field audit
Online registry of SCI samplers
  http://fldeploc.dep.state.fl.us/sci/query.asp

## Slide 95: Auditing
The initial demonstration of capability audit is just a starting point
Samplers should be periodically observed while conducting the entire 20 dip nets to ensure acceptable data.
Refresher audit every 5 years
  On-line test and submitting actual data from a reference site

## Slide 96: Conclusions
A scientifically robust SCI requires proper application of the method and correct interpretation of the results
  Clearly defined objectives
  Control of confounding variables
  Post-hoc evaluation of associated data
  Trained professional staff for sampling and analysis

## Slide 97: For More Information
https://floridadep.gov/dear/bioassessment/content/bioassessment-training-evaluation-and-quality-assurance