## Slide 1: FDEP Pilot Study on the Occurrence of Emerging Substances of Concern (ESOCs) in Florida’s Flowing Waters
Division of Environmental Assessment & Restoration
Florida Department of Environmental Protection

## Slide 2: Questions/Objectives
Are ESOCs occurring at detectable limits in Florida ambient waters? What is DEP doing about it?
What is the appropriate monitoring design for a pilot study as a first step?
Do ESOCs have potential biological effects to Florida biota?
  Screen water samples for estrogenic/mutagenic effects.
  Study fish health (vitellogenin, intersex occurrence).
Are we interested in potential health effects from ESOCs bioaccumulation and fish consumption by Floridians?
Can sucralose be used as a reliable tracer compound for ESOCs?

## Slide 3: Categories of ESOCs
Organic Waste Water Compounds (OWC)
  Pharmaceuticals and Personal Care Products (PPCP)
  Synthetic Hormones
Current Use Pesticides
Brominated Flame Retardants
Akylphenolic Substances
Perfluorinated Compounds (PFCs)
ESOCs are compounds with a wide array of chemical characteristics that occur at very low levels of detection (parts per trillion or ng/L).

## Slide 4
Category | Exposure routes | Aquatic life effects | Water Solubility
Brominated fire retardants | House dust, sediment, food web, carcinogen, breast milk | Bioaccumulative, endocrine disrupting, toxic, persistent | Low
Pharmaceuticals & Personal Care Products | surface and ground water | Endocrine disrupting | High
Synthetic hormones | surface and ground water | Endocrine disrupting | High
Current Use Pesticides | Water, sediment, food web | Toxic | High
Perfluorinated Compounds | Food web, breast milk | Bioaccumulative, Endocrine disrupting | Low
Categories and Sampling Approach for ESOCs
Notes: Water solubility; need definition of polar and non polar

## Slide 5: Benefits of Whole Water Grab Samples
Only one sampling trip required.
Provides quantitative results.
Allows a comparison to sucralose concentrations.
Provides an ambient water sample to test for biological effects.
Notes: However, one must keep in mind that whole water sampling will not collect episodic events, is not integrative, there are many non-detects. Which is why we are adding the SPMDs and POCIS.

## Slide 6: Benefits of Integrative Samplers
Semi Permeable Membrane
Device (SPMD) useful for nonpolar compounds
Polar Organic Compound
Integrative Sampler (POCIS)
Time-Integrated Sample, capturing episodic events.
Allows for higher number of ESOCs based on greater exposure time.
May mimic contaminant accumulation in fish tissue.

## Slide 7: Measuring Biological Effects
Samples are extracted from both POCIS & SPMD and screened for potential estrogenic activity using bioassay techniques such as the yeast estrogen screen (YES) to measure hormonal effects.
Oocytes in testes – evaluation of intersex characteristics
Vitellogenin (egg yolk protein) in male fish blood
Human Cell lines – webinar/talk on Thursday with Dr. Nancy Denslow, UF researcher
Mutagenic bioassay (SOS Chromotest)
Other biological tests of interest:
Notes: The human estrogen receptor gene is integrated into the main genome and is expressed in a form capable of binding to estrogen response elements (ERE) within a hybrid promoter on the expression plasmid. Activation of the receptor by binding of ligand, causes expression of the reporter gene Lac-Z (4) which produces the enzyme b-galactosidase. This enzyme is secreted into the medium (5) and metabolizes the chromogenic substrate CPRG (normally yellow) into a red product (6), which can be measured by absorbance. (Routeledge, 1996)

## Slide 8: Study Design: Sucralose as a Tracer for Site Selection
Studies across the nation detect sucralose in surface waters with waste water influence.
Sucralose passes through waste water treatment systems with virtually no degradation, unaffected by chlorination and tertiary-grade treatment.
Therefore FDEP added sucralose to their surface and ground water monitoring networks for the year 2012.

## Slide 9: ESOCs Survey Site Evaluation Criteria
WMS monthly trend stations
  One year of sucralose data at each station
Three categories of detection:
  Consistent detections – Occurring > 80% of the time
  Inconsistent detections – Occurring < 80% of the time
  No detections
Within two miles of upstream waste water discharge site(s)
Regional coverage – sites selected in each region of state
Sucralose concentration level taken into consideration
  Concentration ranges from 0.024 ug/L – 7.3 ug/L.
Landscape (LDI) Development Intensity Index taken into account

## Slide 11: Cost estimates – Option 1: Whole water, POCIS, and SPMD chemistry analysis with estrogen and mutagen assays
AXYS Chemistry analyses |  |  |  | Whole | POCIS | SPMD | Per site | 30 smpl | 
Hormones LCMSMS |  |  |  |  | 525 |  | 525 | 15,750 | 
Hormones HR-GCMS |  |  |  | 925 |  |  | 925 | 27,750 | 
PPCP LCMSMS (AXYS List 1-6) |  |  |  | 1,875 | 1,875 |  | 3,750 | 112,500 | 
Pesticides* (whole analyzed by DEP) |  |  |  | - | - | - | - | - | 
Alkylphenols |  |  |  | 500 | 500 |  | 1,000 | 30,000 | 
PFCs |  |  |  | 385 |  | 385 | 770 | 23,100 | 
PBDEs |  |  |  | 750 |  | 750 | 1,500 | 45,000 | 
Telomers |  |  |  | 375 |  | 375 | 750 | 22,500 | 
HBCDD |  |  |  | 450 |  | 450 | 900 | 27,000 | 
Sum |  |  |  | 5,260 | 2,900 | 1,960 | 10,120 | 303,600 | 
USGS BLYES and SOS Chromotest |  |  |  |  |  |  |  | 90,000 | 
EST-lab POCIS & SPMD sampling devices rental cost** |  |  |  |  |  | $479.10/site |  | 15,061 | 
Total |  |  |  |  |  |  |  | 408,661 | 

## Slide 12: Cost estimates – Option 2: Whole water and POCIS chemistry analysis with estrogen assay
AXYS Chemistry analyses |  |  |  | Whole | POCIS | SPMD | Per site | 30 smpl | 
Hormones LCMSMS |  |  |  |  | 525 |  | 525 | 15,750 | 
Hormones HR-GCMS |  |  |  | 925 |  |  | 925 | 27,750 | 
PPCP LCMSMS (AXYS List 1-6) |  |  |  | 1,875 | 1,875 |  | 3,750 | 112,500 | 
Pesticides* (whole analyzed by DEP) |  |  |  | - | - |  | - | - | 
Alkylphenols |  |  |  | 500 | 500 |  | 1,000 | 30,000 | 
Sum |  |  |  | 3,300 | 2,900 |  | 6,200 | 186,000 | 
USGS BLYES |  |  |  |  |  |  |  | 48,040 | 
EST-lab POCIS only sampling devices rental cost** |  |  |  |  |  | $300.44 per site |  | 9,013 | 
Total |  |  |  |  |  |  |  | $243,053 | 

## Slide 13: Cost estimates – Option 3: Whole water and POCIS chemistry analysis with estrogen assay
AXYS Chemistry analyses |  |  |  | Whole | POCIS | SPMD | Per site | 30 smpl | 
Hormones LCMSMS |  |  |  |  | 525 |  | 525 | 15,750 | 
Hormones HR-GCMS |  |  |  | 925 |  |  | 925 | 27,750 | 
PPCP LCMSMS (AXYS List 1-6) |  |  |  | 1,875 | 1,875 |  | 3,750 | 112,500 | 
Pesticides* (whole analyzed by DEP) |  |  |  | - | - |  | - | - | 
Sum |  |  |  | 2,800 | 2,400 |  | 5,200 | 156,000 | 
USGS BLYES |  |  |  |  |  |  |  | 48,040 | 
EST-lab POCIS only sampling devices rental cost** |  |  |  |  |  | $300.44 per site |  | 9,013 | 
Total |  |  |  |  |  |  |  | $213,053 | 

## Slide 14: Next Steps
FDEP can create agreements with a series of labs, one for whole water chemical analysis and one for bioassay (YES) work.
Pending Division Approval, we hope to initiate a pilot study for fiscal year starting July 2013.
We propose that DEP WMS field team(s) collect the samples to save funding.