## Slide 1
Molecular Approaches to Assessing Contamination and Biological Effects in Aquatic Field Sites
Tara Sabo-Attwood, PhD
Joseph Bisesi, PhD, Nancy Denslow, PhD
University of Florida, USA
Department of Environmental & Global Health
Center for Environmental and Human Toxicology

## Slide 2
Aquatic Toxicology Facility

## Slide 3
Molecular Toxicology Lab

## Slide 4: Outline
Aquatic Contaminants (Hormonally Active Agents)
Focus on 2 molecular assays
  Hormone receptor binding with fluorescence polarization (Bisesi)
  GeneBLAzer hormone receptor activity (Sabo-Attwood)
  Utility in field applications

## Slide 5
Pesticides
SUSPECTED
HAAs
Personal care products
Metals
Pharmace-uticals
Industrial
chemicals
Synthetic & natural hormones
Hormonally Active Agents (HAAs)
estrogen, androgen, progesterone, glucocorticoid

## Slide 6: Environmental Assays
In vivo fish assays
Plasma Vtg
Plasma hormones
  E2, T, 11-KT
Microarray analysis
In vivo toxicity bioassays
FHM cumulative egg production
High-throughput in vitro assays
ER/AR/PR/GR transactivation assays
ER/AR binding assay

## Slide 7: Sensitivity of Molecular Assays
Percent Measured Effect
Reversible
Irreversible
Concentration of Toxicant X Time of Exposure
Population
Tissue
Molecular
100
50
0
nM uM mM

## Slide 8: Estrogen Equivalency
Correlation between chemically estimated EEQs and bioassay EEQs (Bulloch et al., 2010).

## Slide 9
VTG, ER
ERE
Hormone-Receptor Mediated
Gene Regulation
E2
mRNA
xenoestrogen
Hepatocyte nucleus
ER
Receptor binding
Receptor activation

## Slide 10: What is currently known about xenoestrogen-ER binding?
Various xenoestrogens (> 188) have been shown to bind the ER through a heterogeneous radioligand competitive binding assay, which measures the ability of compounds to displace [3H]-estradiol from the ER
Major shortcoming:
Time-consuming separations steps are needed to remove unbound probe before performing radioligand measurements
Blair et al., Toxicological Sciences, 2000, 54: 138-54

## Slide 11: Fluorescence polarization (FP): a novel approach for probing xenoestrogen-ER interactions in vitro
Fluorescence polarization measures the ability of compounds to competitively displace a high affinity fluorescent-ligand from the ER
Advantages:
Homogeneous, sensitive assay
Non-radioactive
Amenable to view binding events at equilibrium
High-throughput format (96-well plates)
Bolger et al., Environ. Health Perspectives, 1998, 106: 551-57

## Slide 12: Fluorescence Polarization - How it Works
ER ligand binding domain (LBD) with N-terminal thioredoxin and hexahistidine tags

## Slide 13: FP – Experimental Methods
Triplicate 12-point serial dilutions of xenoestrogens were prepared in 96-well plates
10 nM recombinant ER-LBD and 0.5 nM fluorescent-estrone probe were added to ligand dilutions and incubated at 25 °C for 1 hour prior to fluorometric measurements (ex λ = 488 nm, em λ = 520 nm)
FP values were converted to % inhibition using the following equation: I% = (A0 – A)/(A0 – A100) * 100

## Slide 14
Results for Single Chemicals
E2
Genistein
Tamoxifen
Nonylphenol
BPA
OH-PCB
DDE
PBDE-100

## Slide 15: Results for Single Chemicals

## Slide 16: Binding Parameters of Tested Xenoestrogens
Ligand Calculated IC50 RBA (%)
Estradiol 17.1 nM 100
4-OH-Tamoxifen 5.79 nM 295
4-Nonylphenol 212 nM 8.08
Bisphenol-A 1.48 μM 1.15
OH-PCB 142 nM 12.0
DDE 2.10 μM 0.813
PBDE-100 N.D. N.D..
OPEC N.D. N.D.
Ki = IC50/[1+(D/Kd)]
RBA = (IC50 E2)/ (IC50 test cpd) * 100

## Slide 17
Fluorescence Polarization: Field Example
Chart: Estridiol Binding Equivilancy (ng/L)
| Lease | WFG | Seminole | Blackshear | Whorley | Heath | Antioch | Hatcher | Dodge | Paradise | H2O
 | 11.7775 | 7.9626 | 4.5964 | 12.5134 | 10.2922 | 5.9635 | 5.0271 | 4.3127 | 5.2692 | 11.5153
Notes: Concentrated extracts from contaminated sites in rural georgia were found to contain low to non-detect levels of estrogens. But the estrogen data alone cannot explain the effects they were seeing in the biota. Other contaminants have been shown to cause endocrine disrupting effects associated with estrogenic exposures but the researchers were unable to measure every chemical in their extracts. They were looking for a method to determine total estrogenicity without trying to measuring every contaminant. Using our fluorescence polarization assay we were able to measure detectable estrogen receptor binding in all sample extracts from the sites they are interested in. These include sites with no measureable estrogen concentrations. The graph on the left shows our repeatable estradiol competitive binding curve that we used to calculate a estradiol binding equivalence. The graph on the right shows the measured estradiol binding equivalence for their sites. We are still in the process of comparing our assay data with measured chemical concentrations and biological impact. It is important to note that this assay only give us information about binding and that bind does not always directly lead to a predictable downstream effect. But it is a starting point for determining total estrogenicity of water samples, or comparing chemical estrogen affinity to known estrogenic contaminants.

## Slide 18: Androgen Receptor Binding
Rat androgen receptor ligand binding domain
Commercially available
Potential to build our own to decrease cost

## Slide 19: Receptor Activation - Invitrogen GeneBLAzer Assays
NHR
Beta-lactamase
GAL4 site
Fluorescent BLA substrate
Fluorescence measurement
BLA
Chemicals
+
Individual stable cell lines: ER, AR, PR, p53, PPARg and GR
High-throughput
GAL4 DBD
Stably Transfected 293T Cells
Division-Arrested

## Slide 20: Example: Estrogen Receptor Assay
GAl4-ER LBD = receptor
Gal 4 DNA
binding sites
Bla protein
Beta lactamase
409 nm
FRET, fluorescence resonance
energy transfer
520 nm
Receptor gene
Reporter gene
Substrate
Hydrolyzed
substrate
green
blue
Notes: FRET – fluorescence resonance excitation transfer

## Slide 21: In vitro assay protocol
Seed cells
Chemical exposure
Add assay reagents
and incubation
Fluorescence reading
Cell culture

## Slide 22: Profiles for Single Chemicals
BPA
NP
Bif
E1

## Slide 23: ER Antagonist Profiles
Estrone
Nonylphenol
Bifenthrin

## Slide 24: ER Round Robin Results
Chart: GeneBLAzer ERa assay AUS and CA water extracts
| AUS - A | AUS - B | AUS - C | AUS - D | AUS - E | AUS - F | AUS - G | AUS - H | AUS - J | AUS - K | CA - A | DMSO
Dilution series - 1 | 1.1002 | 0.43671 | 0.096442 | 0.1035 | 0.70459 | 0.14495 | 0.15561 | 0.12441 | 0.098838 | 0.11568 | 0.9476 | 0.1121
Dilution series - 2 | 0.72623 | 0.22998 | 0.1039 | 0.10114 | 0.42805 | 0.1602 | 0.13015 | 0.10126 | 0.078024 | 0.13542 | 0.42036
Dilution series - 3 | 0.43988 | 0.16464 | 0.0823 | 0.090213 | 0.23109 | 0.13641 | 0.11159 | 0.11309 | 0.092075 | 0.12421 | 0.18075
Dilution series - 4 | 0.19543 | 0.10969 | 0.082105 | 0.059721 | 0.15506 | 0.058325 | 0.10343 | 0.099645 | 0.104 | 0.11272 | 0.13717
Legend for samples
A= Effluent 2
B= Effluent 1
C= Ozonation
D= Storm water
E= Membrane
F= RO
G= River Water
H = AO
J= Blank
K= Drinking water
CA= SCCWRP proj
A B C D E F G H J K CA DMSO
Water Samples

## Slide 25: Androgen Receptor Assay
Legend for samples
A= Effluent 2
B= Effluent 1
C= Ozonation
D= Storm water
E= Membrane
F= RO
G= River Water
H = AO
J= Blank
K= Drinking water
Chart: GeneBLAzer AR assay AUS water extracts
| AUS - A | AUS - B | AUS - C | AUS - D | AUS - E | AUS - F | AUS - G | AUS - H | AUS - J | AUS - K | DMSO
Dilution series - 1 | 0.3913 | 0.31383 | 0.45535 | 0.26909 | 0.31558 | 0.33784 | 0.26699 | 0.29482 | 0.31784 | 0.34128 | 0.28665
Dilution series - 2 | 0.32874 | 0.29828 | 0.31111 | 0.29877 | 0.31131 | 0.31707 | 0.29713 | 0.30936 | 0.31661 | 0.30366
Dilution series - 3 | 0.29605 | 0.30403 | 0.36538 | 0.28625 | 0.30273 | 0.30301 | 0.29231 | 0.32041 | 0.31574 | 0.28476
Dilution series - 4 | 0.29862 | 0.29744 | 0.2964 | 0.28607 | 0.29559 | 0.30019 | 0.28056 | 0.28581 | 0.30395 | 0.2799
A B C D E F G H J K DMSO
Water Samples

## Slide 26
Water Reuse in Turf-Management: Kiawah Island, SC
P5
P25
P43
WWTP

## Slide 27
Chart: GeneBLAzer ERa Assay
| P5 | P25 | P43 | WWTE | C
Dilution 1 | 0.41244 | 0.27756 | 0.33328 | 0.61786 | -0.063869
Dilution 2 | 0.17304 | 0.13586 | 0.18417 | 0.31985 | -0.10731
Dilution 3 | 0.10813 | 0.049056 | 0.025784 | 0.19516 | -0.096112
Dilution 4 | 0.034325 | -0.040677 | 0.0078177 | -0.050253 | -0.091418
Chart: GeneBLAzer PR Assay
| P5 | P25 | P43 | WWTE | C
Dilution 1 | 0.21217 | 0.19424 | 0.14317 | 0.059493 | -0.026812
Dilution 2 | 0.083179 | 0.086814 | 0.12241 | 0.047154 | -0.042701
Dilution 3 | -0.0018782 | 0.019306 | 0.045926 | -0.021378 | -0.022235
Dilution 4 | 0.00956 | -0.028808 | 0.0087347 | 0.0068659 | -0.026371
Sample | BEQ using EC10 values (nM)
P5 | 106.3
P25 | 28.7
P43 | 93.5
WWTP | 45.1
C | ND
Sample | BEQ using EC10 values (nM)
P5 | 0.9
P25 | 0.3
P43 | 0.6
WWTP | 2.1
C | ND
Estrogen and Progesterone Activity of Kiawah Waters

## Slide 28: Conclusions
Bioanalytical approaches are complementary to analytical chemical approaches and can be used for monitoring – fast, easy, high-throughput
Bioanalytical approaches distinguish the bioactive fraction from the total
Potential to provide information to higher order population level effects

## Slide 29: Acknowledgements
Denslow Lab
Kevin Kroll
Candice Lavelle
Erica Brokemeier
Ignacio Rodriguez
Dr. Reyna Cristinia Colli-Dula
Dr. Sumith Jayasinghe
Dr. Viet Dang
Sabo-Attwood Lab
Dr. Joe Bisesi
Dr. Sumith Jayasinghe
Cody Smith
Lee Ferguson, Duke University
Funding: NIH
EPA
NSF
SFEI
USGS
Center for Environmental and Human Toxicology