## Slide 1: Site Evaluation for ESOCs Project
The Hitchiti Indians lived in north Florida on the shores of the Chattahoochee
river when first European contact occurred
‘Apalachicola’ means ‘people on the other side’
‘Withlacoochee’ means ‘crooked river’
‘Ochlockonee’ means ‘yellow water’
The Tocobaga Indians lived in the region of east Tampa Bay when the Spanish landed
‘Alafia’ means ‘river of fire’
Thomas Seal, Watershed monitoring section
Water quality assessment program

## Slide 2: Apalachicola River
Largest river in Florida, based on discharge, is formed by confluence of the Chattahoochee and Flint Rivers, and measures 112 miles long
The entire ACF drainage basin is 17,230 square miles; drainage basin of 430 mile long Chattahoochee is 8,770 square miles; the drainage basin of the 344 mile long Flint River is 8,460 square miles
Proposed ESOC site is located at state line downstream from Woodruff Dam, which forms Lake Seminole, one of the largest lakes in Georgia.
Discharge averages 16,500 cubic feet/second, but can range from a minimum of 5,000 cfs (mandated by ACOE) to over 175,000 cfs
Drainage basin receives sediments from the Blue Ridge, Piedmont and Coastal Plain provinces of Georgia (river sediments still contain visible muscovite mica flakes)
Multiple medium and large cities use both rivers for effluent discharges (Atlanta metropolitan area, Griffin, Columbus, Bainbridge)
Both basins have significant agriculture presence

## Slide 3: Withlacoochee River
Proposed ESOC site is located at state line
The river is only 112 miles long
The drainage basin is 2,120 square miles
Discharge average 1,870 cubic feet/second, but can range from a minimum of 100 cfs up to 78,000 cfs
Drainage basin receives sediments from only the Coastal Plain province
The river receives effluent from the city of Valdosta about 20 miles upstream of site; this particular WWTP has a long history of overflows during high rainfall events
The Withlacoochee River joins with the Suwannee River downstream from the site. The Suwannee R has an extra level of protection afforded it by Florida state law.

## Slide 4: Ochlockonee River
Proposed site is also located just south of the FL-GA state line
The river is 190 miles long, joins the Gulf of Mexico at Ochlockonee Bay
The drainage basin is 1,002 square miles at this sampling site
River discharge averages 1,870 cubic feet/second, but can range from a minimum of about 100 cfs up to 54,000 cfs
Drainage basin receives sediments from only the Coastal Plain province
The river receives effluent from the Georgia cities of Cairo, Thomasville and Moultrie upstream of the proposed site.

## Slide 5: Alafia River
The Alafia River is only 25 miles long, and is just a few feet above sea level for most of its length.
The chosen sampling site is downstream of the confluence of the North and South Prongs of the river, near a Tampa Bay Water freshwater withdrawal site.
Watershed = 335 square miles, which is located entirely in Hillsborough and western Polk County
Discharges an average of 200 cubic feet/second, but can range from a minimum of about 40 cfs up to 21,000 cfs
Numerous land uses influence the water quality of the river, including the City of Lakeland WWTP, numerous phosphate mine sites and phosphate ore processing sites, and agriculture
Salt water tidal influence occurs well upstream from Tampa Bay, as indicated by higher specific conductivity in samples

## Slide 6: ESOCs Site Sucralose Values
Apalachicola River = 0.95 µg/L maximum value
Withlacoochee River = 2.9 µg/L maximum value
Ochlockonee River = 2.6 µg/L maximum value
Alafia River = 7.3 µg/L maximum value (mean value 2.8 µg/L)
These values represent the maximum detected values over a 12 month period.

## Slide 7: ESOC River Site Water Chemistry
Color | Alafia | Apalachicola | Withlacoochee | Ochlockonee
Mean | 79 | 42 | 90 | 108
Median | 60 | 40 | 80 | 100
Min | 15 | 5 | 5 | 15
max | 250 | 160 | 400 | 300
Note lower color of the Apalachicola River due to larger drainage basin diluting black water from riverine wetlands which are common in the other smaller selected rivers.

## Slide 8: ESOC River Site Water Chemistry
Specific Cond | Alafia | Apalachicola | Withlacoochee | Ochlockonee
Mean | 477 | 130 | 160 | 134
Median | 465 | 131 | 159 | 114
Min | 184 | 69 | 49 | 37
max | 1052 | 174 | 277 | 386
Note the higher specific conductivity of the Alafia River, indicating human influences upstream
as well as possible tidal influence / upwelling

## Slide 9: ESOC River Site Water Chemistry
Alkalinity (mg/L CaCO3) | Alafia | Apalachicola | Withlacoochee | Ochlockonee
Mean | 93 | 42 | 54 | 27
Median | 94 | 41 | 53 | 23
Min | 40 | 18 | 4 | 4
max | 163 | 69 | 114 | 81
Note higher alkalinity of the Alafia River site due to higher calcium in the sediments upstream of site

## Slide 10: ESOC River Site Water Chemistry
NOx (mg/L) | Alafia | Apalachicola | Withlacoochee | Ochlockonee
Mean | 0.64 | 0.40 | 0.34 | 0.58
Median | 0.59 | 0.42 | 0.28 | 0.43
Min | 0.06 | 0.31 | 0.02 | 0.03
max | 3.5 | 0.76 | 1.9 | 2.8
Note higher total nitrogen in the Alafia River site, followed by the Ochlockonee River. Likely source is agriculture in both basins.

## Slide 11: ESOC River Site Water Chemistry
TSS (mg/L) | Alafia | Apalachicola | Withlacoochee | Ochlockonee
Mean | 7.2 | 6.0 | 5.7 | 8.2
Median | 5 | 6 | 4 | 8
Min | 2 | 2 | 2 | 2
max | 53 | 15 | 39 | 23
Note highest total suspended solids in the Ochlockonee River, likely indicating erosion of farm lands upstream.

## Slide 12: ESOC River Site Water Chemistry
Fecal Coliform | Alafia | Apalachicola | Withlacoochee | Ochlockonee
Mean | 853 | 48 | 119 | 109
Median | 80 | 7 | 28 | 48
Min | 4 | 1 | 1 | 2
max | 63,000 | 2,800 | 3,000 | 2,000
Note highest fecal coliform in the Alafia River, indicating multiple sources upstream. At some point all rivers are in violation for fecal coliforms based on Florida’s water quality standard.