## Slide 1
Chapter 3
Temporary BMPs for Erosion and Sedimentation Control

## Slide 2: 3.1 Importance of Construction Sequencing
Diversion
Tracking
Sod
Clear only areas to be
developed and clear
in stages
Greater Area and Time Exposure = More Material Eroded = More Failed BMPs, More BMP Repair, More Code and Permit Violations, More $$$

## Slide 3: 3.1 Construction Sequencing
Definition: Coordinating the construction schedule to minimize the amount of area disturbed at any one time and coordinating land clearing with the installation of erosion control measures
Purpose: to minimize the amount of disturbed area and manage runoff, thereby reducing erosion potential
Sequencing is important for all construction projects!
Have a plan before you clear!

## Slide 4: Planning Considerations:
Plan in phases
Clear only areas to be developed
Install controls before clearing
Prioritize sensitive areas
Stabilize finish grade immediately
Temporary seed for inactive areas
Work with the seasons
3.1 Construction Sequencing

## Slide 5
Three Phases to Sequencing:
Phase 1: initial installation of erosion and sediment controls prior to clearing
Phase 2: interim stormwater management plan - construction and connection of permanent stormwater management system
Phase 3: completed stormwater management system - built per plan, functions as designed
3.1 Construction Sequencing

## Slide 6: Phase 1: Installation of erosion and sediment controls prior to clearing
One Dozer Blade Width Clearing Allowed to Install Permitter Controls
*However, Please Verify With Local Agency.
*You must have an Environmental Resource Permit (ERP) to clear areas determined to be wetlands.

## Slide 7
Dewatering Plan may be required by the Water Management District or DEP.
Discharge only waters that meet State Surface Water Standards!
Phase 2: Construction and connection of permanent stormwater management system

## Slide 8
Stabilize Slopes Immediately After Final Grading.
Phase 2: Construction and connection of permanent stormwater management system

## Slide 9: Phase 3: Completed stormwater management system - built per plan, functions as designed
Pond Must Discharge Clean Water!

## Slide 10: 3.2 POLLUTION SOURCE CONTROLS ON CONSTRUCTION SITES
Definition: minimizing nonpoint source pollution from construction sites through good management and “housekeeping” techniques
Purpose: to reduce the availability of construction-related pollutants that can contaminate runoff water, or retain pollutants and polluted water on-site
This is an important practice that applies to all construction sites. Often overlooked!

## Slide 11: Pollution Source Controls on Construction Sites 1. Erosion and Sediment Controls
Silt Fence Installer-
Sediment Control
Inlet Protection –
Sediment Control
Rolled Erosion Control Product –
Erosion Control
Hydromulch –
Erosion Control
Notes: 3.2

## Slide 12: Pollution Source Controls on Construction Sites 2. Vehicle & Concrete Wash Areas
Concrete Polluants:
Chromium (carcinogen)
Alkaline pH
Very Important!
Designate an area then clean and maintain
Keep sediments off streets and out of storm drains
Notes: 3.2

## Slide 13
Build area into plan, if needed
No pollutant discharge during repair – must account for disposal
Offsite is best
Pollution Source Controls on Construction Sites 3. Equipment Maintenance & Repair
Notes: NEW PIC

## Slide 14
Clean and dispose as you go!
Pollution Source Controls on Construction Sites 4. Waste Collection & Disposa
Notes: 3.2

## Slide 15
May generate large amounts of dust. Use dust control to prevent airborne pollutants. Sprinklers commonly used.
Stockpiles should be hauled off regularly to a State of Florida permitted C& D Landfill.
Runoff should not be allowed to run directly into watercourses, or stormwater conveyance systems. An illicit discharge is subject to enforcement.
Pollution Source Controls on Construction Sites 5. Demolition Debris Area
Notes: 3.2

## Slide 16
GOOD IDEA!
Chemical & Hazardous Materials should always be stored in accordance with *OSHA and *RCRA rules.
Protects our groundwater resources.
*(Occupational Safety and Health Administration)
*(The Resource Conservation and Recovery Act)
Pollution Source Controls on Construction Sites 6. Material Storage, HazMat Storage
Notes: The Resource Conservation and Recovery Act (RCRA) is the public law that creates the framework for the proper management of hazardous and non-hazardous solid waste. The law describes the waste management program mandated by Congress that gave EPA authority to develop the RCRA program.Feb 12, 2019

## Slide 17
Adequately protected and covered
from wind & rainfall.
Silt fence or a small trench built
around the base of the pile and
out at least 20 feet, but depends on height and slope.
Vegetative cover over the pile.
Stockpiles should not be placed near perimeter of the site, near wetland areas, water bodies, storm drain inlets, or within 10 feet of infiltration or exfiltration system.
Pollution Source Controls on Construction Sites 7. Stockpile Erosion Protection
Notes: 3.2

## Slide 18
All sanitary facilities should
be located away from:
Curb inlets
Wetland areas
Waterbodies
Areas prone to flood; such as, stormwater conveyance systems (swales), dry detention ponds, or dry streambeds.
Note the Containment Tray and Tie-Down Straps
Pollution Source Controls on Construction Sites 8. Sanitary Facilities
Notes: 3.2

## Slide 19
Construction activities with exposed subsurface soils will generate dust.
This causes problems as air pollution affects the health and safety of workers and citizens which live nearby.
FDOT allows:
Frequent watering with watering trucks.
Dust suppressants, only if they are environmentally safe.
Pollution Source Controls on Construction Sites 9. Dust Control
Notes: 3.2

## Slide 20
The temporary removal of groundwater using well pumps in mining, quarrying, or construction.
*Chapter 5 will cover in more detail.
Pollution Source Controls on Construction Sites 10. Dewatering
Notes: 3.2

## Slide 21
Important to protect curb & drop inlets during construction activities.
SAVES MONEY
Pollution Source Controls on Construction Sites 11. Storm Sewer Inlet Protection
Notes: 3.2

## Slide 22: Temporary BMP Techniques and Technologies
3.3 Stabilized Construction Exit
3.4 Perimeter Control
3.5 Storm Drain Inlet Protection
3.6 Temporary Sediment Trap
3.7 Temporary Sediment Basin
3.8 Temporary Check Dam
We will now discuss a variety of specific techniques and technologies used in erosion and sedimentation control, including:
There are many more that exist and more are being invented and refined all the time, but these are the basics you should know!

## Slide 23: 3.3 Stabilized Construction Exit
Definition: A stabilized pad located at points where vehicles enter and leave a construction site
Purpose: To reduce the amount of sediment being transported onto public roads
Condition where practice applies:
Wherever vehicles are leaving a
construction site and moving onto
public roads or paved areas
Notes: 3.3 NEW PIC

## Slide 24
Prevent this:
With this:
3.3 Stabilized Construction Exit
Notes: 3.3

## Slide 25
Designing a Stabilized Construction Exit or Tracking Pad:
Clear & grade a trough 6 inches deep & 50’ long (minimum)
Geotextile – Use Geotextile Fabric (Plastic filter fabric similarly used under riprap.)
Secure fabric in with sod pins
Aggregate - FDOT No.1 (2 inch) stone
Light traffic - 1 lane = 12’ wide min.
Heavy traffic - 2 lanes = 25’ wide min.
Widened at roadway (20’ turning radius)
Optional wash rack with runoff sediment trap
3.3 Stabilized Construction Exit
Notes: 3.3

## Slide 26
Excavate trough 6 inches deep
Install FDOT #1 or 2” stone – 6 inches deep
Maintain Regularly
Install plastic filter fabric & pin in
3.3 Stabilized Construction Exit
Notes: 3.3

## Slide 27
Other options: Prefabricated Products
Mud Mats
Rumble Racks
Portable Wash Racks
3.3 Stabilized Construction Exit
Notes: 3.3

## Slide 28
More Options:
Geoterra
Ground Guard
3.3 Stabilized Construction Exit
Notes: 3.3

## Slide 29
Maintenance
Raking stone (hard steel rake)
Add more stone
Replace mats
Rinse rumble racks
Clean out sediment trap
Sweep or trailer-broom adjacent public roadway daily during increased hauling activity or as needed during slow activity.
Always follow proper safety procedures in affected traffic lanes. [SAFETY 1st!]
Always remember to use protective eyewear and the proper respirator mask to protect your lungs from silica dust when using a tractor broom.
*(See OSHA Requirements for eye and lung protection)
3.3 Stabilized Construction Exit
Notes: 3.3

## Slide 30
Use silt fence to manage the drainage area.
Add a sediment trap.
Loop the silt fence around the exit.
3.3 Stabilized Construction Exit
* This useful guide can be found on the EPA’s website:
www3.epa.gov/npdes/pubs/sw_swppp_guide.pdf
or search for “EPA SWPPP Guide”
Notes: You will also find links to:

## Slide 31
3.3 Stabilized Construction Exit

## Slide 32
Avoid This At All Costs
Major Liability Exposure
Lawsuits $!$!$!$!
3.3 Stabilized Construction Exit
Notes: 3.3

## Slide 33: 3.4 Perimeter Controls
3.4.1 Overview:
Perimeter controls intercept and detain small amounts of sediment under sheet flow conditions during construction activities where there are disturbed soils.
Includes these temporary & maintenance intense BMPs:
Silt Fence
Filter Socks
Temporary Diversion Berms
Temporary Fill Diversions
Temporary Slope Drains
Floating Turbidity Barriers
Special Note!
All BMPs are “Performance-Based”
If they are not working, replace them with a better preforming BMP.
Notes: 3.4.1

## Slide 34: 3.4.2 Silt Fence
Definition: a temporary sediment barrier consisting of woven and non-woven filter fabric attached to supporting posts and entrenched to anchor firmly.
Purpose: to slow the velocity of stormwater runoff and retain sediments onsite.
*Note: Black woven mesh silt fence (FDOT Type 3) will not stop turbid or fine silty particles. However, there are non-woven fabrics designed to stop to turbid and fine silty particles; such as, the Base Strand Reinforced Fencing (BSRF Type) which is a non-woven silt fencing.
Wrapped and Joined
Not Wrapped and Joined
Notes: 3.4.2

## Slide 35
Condition where practice applies:
Installed for sediment capture under sheet flow conditions.
Not intended for channel flow conditions (i.e., across ditches, paved ditches, or swales, or in live streams or waterways).
Not preferred around a drop inlet unless it is reinforced to prevent collapse from water pressure. (Water weighs 8.3 pounds per gallon).
Drainage area <1/4 acre/100’ of barrier
Slope length < 100’ behind barrier
Gradient behind barrier < 50%
Useful life < 6 months (can be longer
with proper installation & maintenance)
Reinforced >
< Not Reinforced
3.4.2 Silt Fence
Notes: 3.4.2

## Slide 36
There are many types of fencing, woven
& non-woven, and in many colors as well.
A double row increases protection - allow at least 3 foot spacing at a minimum .
Remember: 4” deep x 4” wide and lap, wrap, & roll for joining two rolls together.
For steep slope, place silt fencing away from the toe of the slope to increase holding capacity.
3.4.2 Silt Fence
Notes: 3.4.2

## Slide 37
Construction Specs:
Height: < 36”
Posts: 1”x2” wooden stakes. (2”x2” works better)
Or #5 rebar / metal T-Post w/ protective caps
Post spacing:10’ max. w/ wire backing, 6’ w/o wire; 12” deep minimum
Trench: 4” deep, 4” wide
Flap: 8”; bury, backfill, and compact soils on both sides.
For wire backed supported fence: see FDOT specs Type I
3.4.2 Silt Fence
Notes: 3.4.2 REMOVED DUPLICATE PHOTO, REPLACE

## Slide 38
Installation: Manually by Hand & Shovel or Silt Fence Entrencher
100’ Rolls with extra wood stakes.
Use a two-sided trencher or get your shovel moving!
Stretch fencing out.
Driven in with sledge hammer.
Place the Two Panel Sections together.
“Lap, wrap, & roll!”
Driven in with sledge hammer.
Flap buried and compacted on both sides.
3.4.2 Silt Fence
Notes: 3.4.2

## Slide 39
Silt Fence Entrencher or Silt Fence Plow
This Photo by Bobcat
This Photo by Hal Lunsford, Auburn University, ESC Field Day, 2015
Thread the silt fence under a rod and through the chute on the blade.
The blade is positioned for optimum fence placement and the attachment is lowered into the ground.
As the machine is driven, the silt fence unrolls & cuts fabric automatically.
Next install wood stakes every six feet and secure fencing to post with staples.
3.4.2 Silt Fence
Notes: 3.4.2

## Slide 40
Maintenance:
Inspected within 24 hours after each half inch or larger rain event and every seven calendar days according to the Construction Generic Permit (CGP). Repairs should be made immediately within seven calendar days.
Normal life expectancy for silt fence is six months. However, fabric will decompose faster due to extreme or hot weather.
Sediment build up should be removed when it reaches half the height of the barrier. *Suggestion: Regularly complete Preventive Maintenance (PM) to remove accumulation of sediment earlier.
Remove silt fencing once final stabilization is accomplished when construction activities are concluding. Remember to repair area where fencing is removed smooth out and reseed with permanent grass seed. You can hydro-seed area as well.
3.4.2 Silt Fence
Notes: 3.4.2 REPLACE BOTTOM PIC

## Slide 41
Bottom Trenched In, Compacted
Proper Splices Between Sections (Wrap & Roll)
Cannot Be Pulled Out With One Hand
SILT FENCE INSPECTION
3.4.2 Silt Fence

## Slide 45
What to look for and How to Maintain Silt Fence…..
Problems to look for: | Possible remedies:
Undercutting of fence | Retrench and compact
Fence collapsing | Stake size, depth, check drainage area Add support fencing
Torn / clogged fabric | Replace
Runoff escaping around fence | Extend fence
Sediment level near halfway to the top of fence | Remove sediments Also, check sources of erosion and take further action to control erosion source(s)
When job ends and site is stabilized | Remove silt fencing and reseed areas
3.4.2 Silt Fence

## Slide 46: 3.4.3 Filter Sock – SRFR or Wattle
Definition: a three-dimensional, tubular sediment control and storm water runoff filtration device.
Purposes:
to trap or filter small amounts of sediments
to slow the velocity of sheet flows and low to moderate level channel flows
Sediment Retention Fiber Roll (SRFR) are used to slow and spread runoff, reducing sediment entering retention ponds, lakes and other water bodies.
Condition where practice applies:
Drainage area < 1/4 acre / 100’ of barrier
Slope length < 100’ behind barrier
Gradient behind barrier < 50%
Can be used on pavement
Credit: American Association of State Highway and Transportation Officials
US Army Corps of Engineers
United States Department of Agriculture Natural Resources Conservation Service
U.S. Environmental Protection Agency
Notes: Federal Specifications for Compost Filter Socks for Sediment & Erosion Control
As specified by
American Association of State Highway and Transportation Officials
US Army Corps of Engineers
United States Department of Agriculture Natural Resources Conservation Service
U.S. Environmental Protection Agency

## Slide 47
Planning Considerations:
No formal design required
Does not require trenching (but can be trenched in for additional support)
Seed can be incorporated
Biodegradable / Photodegradable
Remove cloth to spread organic materials on job site
Apply along land surface contours
Life expectancy of 9 months
3.4.3 Filter Sock – SRFR or Wattle
Notes: 3.4.3

## Slide 48
Construction Specs:
Height: < 24”
Posts: 2 x 2 wooden, 3’ post spacing: 10’ max. driven 8”-12” deep minimum
May be used on pavement with concrete blocks used to secure
Should be staked on sides and not through the sock
3.4.3 Filter Sock – SRFR or Wattle
Notes: 3.4.3

## Slide 49
Installation:
Post spaced a maximum 10 feet apart
Post driven in 8 inches in clay or 12 inches in sand
For pavement – heavy concrete blocks or rock bags behind socks for stabilization
Overlap two sections about a foot and stake each sock
When no longer needed, cut open and spread organic materials out and apply grass seeding
Not for use in streams
3.4.3 Filter Sock – SRFR or Wattle
Notes: 3.4.3

## Slide 50
Maintenance:
Inspect every seven calendar days and within 24 hours of a half inch or greater rain event
Remove sediments when half the height of the barrier
Replace clogged, badly damaged or deteriorated socks
3.4.3 Filter Sock – SRFR or Wattle
Notes: 3.4.3
ADD ANOTHER PIC

## Slide 51: 3.4.4 Temporary Diversion Berm
Definition: A temporary ridge of compacted soil located at the top or toe of a sloping disturbed area
Purpose: To divert (off-site) runoff away from disturbed areas to a stabilized outlet; and to divert (on-site) runoff from a disturbed area to a sediment trapping device
Condition where practice applies: Wherever runoff must be temporarily diverted to protect slopes or retain sediments onsite
Structure life expectancy of 18 months or less
Notes: 3.4.4 NEED ANOTHER PIC

## Slide 52
Conditions:
Drainage area: 5 acres max.
Minimum dimensions: 18” high, 2’ top width, 4.5’ base width, 3:1 side slopes
Smooth & compact
If diverting from > 2% slope: stabilize w/ sod, gravel, plastic, etc.
Discharge: stabilized outlet or basin
Useful life: 18 mos., more if vegetated
3.4.4 Temporary Diversion Berm
Notes: 3.4.4

## Slide 53
Temporary Diversion Berm using Rock Bags
Temporary Diversion Berm using Filtrexx Compost Filter Sock
3.4.4 Temporary Diversion Berm

## Slide 54
Problems to look for: | Possible remedies:
Loose soil | Compact soil
Washouts or low spots on slopes | Add soil to breaches and low spots – then re-compact
Erosion of berm face | Check drainage area, sod, riprap and plastic
Berms in place longer than 30 days | Add temporary or permanent vegetation
What to look for and How to Maintain Temporary Diversion Berm:
3.4.4 Temporary Diversion Berm

## Slide 55
Definition: A channel and ridge along the top of actively used fill
Purpose: To divert runoff away from the unprotected fill slope
Condition where practice applies: Active fill slopes
3.4.5 Temporary Fill Diversion
Notes: 3.4.5

## Slide 56
Design & Construction:
Drainage area: 5 acres max.
Ridge: 9” high, 2’ back from face of slope
Channel should flow to slope drain, stable outlet, or basin
Compaction not required
Useable life: 1 day to 1 week
Maintenance: none, rebuild as required
3.4.5 Temporary Fill Diversion

## Slide 57
Definition: A flexible conduit extending from the top to the bottom of a slope
Purpose: To temporarily convey concentrated runoff safely down the face of a slope without causing erosion
Condition where practice applies: on disturbed slopes before permanent stormwater management structures are installed
3.4.6 Temporary Slope Drain

## Slide 58
Temporary Slope Drain
Headwall to prevent under washing
3.4.6 Temporary Slope Drain
Notes: 3.4.6

## Slide 59
Problems to look for: | Possible remedies:
Blocked inlet or outlet | Remove debris
Erosion at outlet | Extend pipe, install energy dissipaters; i.e., riprap, rock bag pad
Runoff bypassing inlet | Enlarge headwall, flare out entrance section; check drainage area
What to look for and How to Maintain Temporary Slope Drains
ABS Plastic Mitered End –
Protect discharge point from scouring
3.4.6 Temporary Slope Drain
Notes: 3.4.6 ANOTHER PIC?

## Slide 60
Definition: A floating, impermeable textile barrier which minimizes sediment transport from a disturbed area adjacent to or within a water body
Purpose: To provide sediment protection for a watercourse form upland disturbance or from dredging and filling within the watercourse
Condition where practice applies:
Working in a waterway
Working adjacent to a waterway
When dewatering discharge is directly into a water body
Applicable in tidal and non-tidal conditions
Photo from R.H. Moore and Associates, Tampa, FL
3.4.7 Floating Turbidity Barrier
Notes: 3.4.7

## Slide 61
3.4.7 Floating Turbidity Barrier
Notes: 3.4.7

## Slide 62
Staked for low depth conditions.
3.4.7 Floating Turbidity Barrier

## Slide 63
Planning, Design, Installation:
Type III - current to 3 knots, flow to 5 fps.
Type II - current to 2 knots, flow to 3.5 fps.
Type I - no current or flow
3.4.7 Floating Turbidity Barrier
Notes: 3.4.7

## Slide 64
Never Across The Flow
Install Along the Flow
3.4.7 Floating Turbidity Barrier
Notes: 3.4.7

## Slide 65
Tidal & wave conditions:
Maintain a 12” clearance to prevent sweeping the bottom>>>>>>
Channel flow - parallel to flow
Anchor lines attach to buoys, NOT to curtain floatation
3.4.7 Floating Turbidity Barrier
Notes: 3.4.7

## Slide 66
Maintenance:
Use manufacturer’s repair kit on tears and rips
The inspector will determine when the curtain is no longer required.
Prior to removal test the turbidity levels to verify they do not exceed 29 NTUs above background, or 0 NTUs in an Outstanding Florida Waterbody!
Do not use equipment boom to remove from the water; hand remove barrier for reuse
3.4.7 Floating Turbidity Barrier
Notes: 3.4.7

## Slide 67: 3.5 Storm Drain Inlet Protection
Definition: A sediment filter or an excavated mounding area around a storm drain drop inlet or curb inlet
Purpose: To prevent sediment from entering stormwater conveyance systems prior to permanent stabilization
Condition where practice applies: Where storm drain inlets are to be made operational before stabilization of the disturbed drainage area
Photo from RocSoxx 2018

## Slide 68
Different types of structures are applicable to different conditions
3.5 Storm Drain Inlet Protection

## Slide 69
Planning and Design:
Drainage area less than 1 acre!
Won’t interfere w/ construction activities
Installed on pavement or soil
Ponding: OK or problem?
Easy cleanout
Frequency of maintenance & repair
Curb Inlet
Drop Inlet
3.5 Storm Drain Inlet Protection
Notes: ADD PIC

## Slide 70
Types of Inlet Protection Devices:
Drop Inlet | Curb Inlet
Filter Fabric (geo-fabric or non-woven) | Gravel
Prefabricated | Block & Gravel
Gravel & Wire Mesh | Curb & Gutter
Block & Gravel | Drain Field Pipe
Sod | Filter Bags
Filter Bags | Filter Socks
Filter Socks | Prefabricated
3.5 Storm Drain Inlet Protection

## Slide 71
Filter Fabric Cloth
Filter Fabric Cloth requires regular maintenance
Often compromised by cuts or rips
Can be very heavy when loaded with soil
3.5 Storm Drain Inlet Protection

## Slide 72
Fabric Drop Inlet Sediment Filter
Inlet grate is optional
Stakes: Use 2”x4” - 3’ long sharpened and hammered in at least 8”
Top framed w/ 2x4s
Can be further strengthened with 2x4 cross supports from corner to corner (See top photo)
Trenched in fabric, backfilled & compacted.
Can strengthen interior with wire (See bottom photo.)
Can cause flooding, check surrounding roadway height to prevent accidents
Not on pavement
Use 2 x 4 Stakes, Instead of 1 x 2 Stakes!
3.5 Storm Drain Inlet Protection

## Slide 73
Mesh
Inlet grate required
Smooth & compact bare ground
1/2” hardware cloth, extend 1’ all around
2” stone, 12” deep, extend 18” all around
OK on pavement
Will cause ponding
3.5 Storm Drain Inlet Protection

## Slide 74
Block & Gravel Drop Inlet Filter
Inlet grate optional
Smooth & compact bare ground 2”
Concrete blocks: 12 - 24” high
1/2” hardware cloth: cover face of block
2” stone: to top of blocks
Also works on pavement
3.5 Storm Drain Inlet Protection

## Slide 75
Inlet grate optional
Prepare ground for sodding
4 ft. minimum all around
Not on pavement
Light sediment load only
Sod Drop Inlet Filter
3.5 Storm Drain Inlet Protection
Notes: NEW PIC

## Slide 76
Inlet grate over catch basin
On or off pavement
Remove accumulated sediments – very heavy when fully loaded
Filter Bag
3.5 Storm Drain Inlet Protection
Notes: REMOVE ANIMATE

## Slide 77
Entire circumference minimum 1 foot overlap
On or off pavement
Low flow conditions
Removal of sediments.
Filter Bag
3.5 Storm Drain Inlet Protection

## Slide 78
Fits over the inlet, secured to grate with toggle bolt or bolted to concrete.
On or off pavement.
Remove sediments at ½ height or sooner.
Silt Saver Inlet Protection Device
Prefabricated
Silt Saver Inlet Protection Device
3.5 Storm Drain Inlet Protection
Notes: REMOVE ANIMATE ADD ANOTER PIC WITH COVER ON

## Slide 79
Gravel Curb Inlet Filter
Smooth & compact bare ground
1/2” hardware cloth: 12” over and 12” out
2” stone: 12” over, 18” out
Will cause ponding
Optional 2x4 overflow, lessens ponding
Can be used on pavement
3.5 Storm Drain Inlet Protection

## Slide 80
Smooth & compact bare ground
concrete block, web up
2x4 through spacer blocks
1/2” hardware cloth, cover face of block
2” stone
OK on pavement
Block & Gravel Curb Inlet Filter
3.5 Storm Drain Inlet Protection

## Slide 81
Block & Gravel Curb Inlet Filter
Regular Gravel Curb Inlet Sediment Filter
Block with Rock Mesh Sock Inlet Filter
3.5 Storm Drain Inlet Protection

## Slide 82
Curb & Gutter Sediment Barrier
Gravel filled bags, 3/4” stone
1 bag high - use spacing chart
Several bags high - leave spillway
Best on pavement
3.5 Storm Drain Inlet Protection

## Slide 83
Drain Field Pipe Curb Inlet Filter
3.5 Storm Drain Inlet Protection

## Slide 84
Geohay Curb Inlet Filter
Easy to install & maintain
Flexible shape conforms to curb
Lightweight
Made from recycled materials
Can be backwashed and reused
High Water Flow Material
3.5 Storm Drain Inlet Protection

## Slide 85
Prefabricated Curb Inlet Filters
3.5 Storm Drain Inlet Protection

## Slide 86
Verify that water ponding is not a problem!
3.5 Storm Drain Inlet Protection

## Slide 87
Definition: A small temporary ponding area formed by excavation and/or embankment
Purpose: To detain runoff from small disturbed areas long enough for the majority of sediments to settle out
Condition where practice applies:
Drainage area: 5 acres maximum
Useable life: 18 months maximum
Capacity: 134 cubic yd. or 3600 cubic ft. / acre
Embankments: no steeper than 2:1
3.6 Temporary Sediment Trap

## Slide 88
Earth Outlet
Pipe Outlet
Stone Outlet
Storm Inlet
3.6 Temporary Sediment Trap

## Slide 89
Earth Outlet
Embankment: clear & grub, compact in lifts
Outlet width (ft.) = drainage area (ac.) x 6
Stone: 2” stone inside, riprap outside
1’ freeboard
Stabilization: vegetation preferred, most important on inside
3.6 Temporary Sediment Trap

## Slide 90
Pipe Outlet Sediment Trap
3.6 Temporary Sediment Trap

## Slide 91
Embankment: clear & grub, compact in lifts
Pipe: size per table page 4-73
Riser perforations: see Engineer’s specs.
1.5’ freeboard
Stabilization: vegetation preferred, most important on inside
Pipe Outlet Sediment Trap
3.6 Temporary Sediment Trap

## Slide 92
Stone Outlet Sediment Trap
3.6 Temporary Sediment Trap
Notes: FL PIC

## Slide 93
Temporary Sediment Trap For Mud Hog Discharge
3.6 Temporary Sediment Trap

## Slide 94
Storm Inlet Sediment Trap
Depth: 1’ - 2’
Stabilization: vegetation preferred, most important on inside
Can be used with inlet protection BMPs (Treatment Train System)
3.6 Temporary Sediment Trap

## Slide 95
Storm Inlets
Sediment Traps
3.6 Temporary Sediment Trap

## Slide 96
Other applications:
Build traps behind roads & driveways
Use baffles to improve effectiveness
Maintenance: all traps
Inspect: weekly, before & after each storm
Remove sediments when 1/2 full
Repair and re-stabilize
Verify that water ponding is not a problem
3.6 Temporary Sediment Trap

## Slide 97
Use baffles to improve effectiveness!
3.6 Temporary Sediment Trap

## Slide 98
Temporary Sediment Trap with Baffles
Flow-Through Alum Treatment System
3.6 Temporary Sediment Trap

## Slide 99
Dewatering Filter Bag may be used to further remove sediments
Pump Off
Pump On
3.6 Temporary Sediment Trap

## Slide 100
Definition: A temporary basin with a controlled stormwater release structure, formed by construction of a compacted earth embankment
Purpose: To detain runoff long enough for most sediments to settle out
Condition where practice applies: Drainage area over 10 acres per the Construction Generic Permit (CGP)
Useable life: 18 months
Capacity: 134 cubic yd. or 3600 cubic ft. / ac. - when 10 acres or more are disturbed area
Must be designed by Florida Licensed Professional Engineer
3.7 Temporary Sediment Basin

## Slide 101
Design and Construction:
Follow engineered plans
Embankment should be compacted with minimum top width 8 ft. and 2:1 slopes or flatter
Spillway pipe should have antivortex device and trash rack, not just an open pipe.
Freeboard of at least 1 foot between design high water and top of embankment
Stabilization: vegetation preferred, most important inside
3.7 Temporary Sediment Basin

## Slide 102
Floating skimmers help “skim” the clean water off the top while allowing sediments to settle.
They rise and fall with the water level unlike traditional pipe structures
3.7 Temporary Sediment Basin

## Slide 103
Use Baffles to Improve Effectiveness By Increasing The Flow Distance
Flow length should be at least twice the flow width – gives sediment more time to settle out of suspension
3.7 Temporary Sediment Basin

## Slide 104
Sediment Basins and Traps With Baffles
3.7 Temporary Sediment Basin

## Slide 105
Design Elevation With Emergency Spillway:
Minimum 1 ft. (12 in.)
Design Elevation Without Emergency Spillway:
Minimum 3 ft. (36 in.)
3.7 Temporary Sediment Basin

## Slide 106
Anti-Seep Collars Prevent Seepage and Piping Along Spillway Barrel
Must be watertight connection to pipe.
3.7 Temporary Sediment Basin

## Slide 107
Maintenance:
Inspect: weekly, before & after each storm
Remove sediments when half full or reduced to 55 cubic yards per acre of drainage area
The cleanout elevation should be marked on the riser or with a stick
Repair & re-stabilize
3.7 Temporary Sediment Basin

## Slide 108
Problems to look for: | Possible remedies:
Basin almost full | Remove sediments
Obstructed outlet | Remove debris
Basin not dewatering | Clean filter, underdrain, check “ bleeder”
Damaged embankment | Rebuild, re-stabilize
Spillway erosion | Line w/ geotextile, rock
Outlet erosion | Check grades, extend riprap
Riser floatation | More ballast, reconnect
Excessive runoff or sediments | Check drainage areas & patterns, enlarge basin
What to look for and how to Maintain Sediment Traps & Basins
3.7 Sediment Traps and Basin

## Slide 109
Definition: A small temporary dam constructed across a swale or channel
Purpose: To reduce the velocity of concentrated flows reducing erosion of the swale or ditch. Lower energy = less erosion!
Condition where practice applies:
In temporary ditches & swales
In ditches & swales during establishment of grass lining
3.8 Temporary Check Dam
Notes: PIC?

## Slide 110
Stone
Filter socks
Prefabricated materials
Types of check dams
3.8 Temporary Check Dam

## Slide 111
Triangular Silt Dike Rock, Straw Wattle Sand Bags
Geo-Ridge RocSoxx Wattle Compost Wattle+RECP
3.8 Temporary Check Dam

## Slide 112
Drainage area (for the entire swale): 10 acres max.
Max. height: 2’ (6” lower in center)
Spacing: Such that the bottom of upstream dam is equal to the elevation of the top of the downstream dam
Extend up swale side to above low point
“Key- in” to channel sides
3.8 Temporary Check Dam

## Slide 113
Spacing Between Check Dams
Spacing: Such that the Bottom of the Upstream Dam is Equal to the Elevation of the Top of the Downstream Dam
3.8 Temporary Check Dam
Notes: Replaced screen shot with clearer picture

## Slide 114
Maintenance
Inspect Weekly, before & after each storm
Remove Sediments @ ½ height
Repair and replace as required
Remove barrier if no longer needed in fully stabilized areas.
3.8 Temporary Check Dam

## Slide 115
What to look for and How to Maintain Temporary Check Dams
Problems to look for: | Possible remedies:
Sediment accumulation | Remove sediments after each storm
Flow escaping around ends | Extend ends, lower center
Displacement of check dam | Rebuild w/ stronger dam, check drainage area and the stone size
3.8 Temporary Check Dam