## Slide 1
Chapter 1 Erosion and Sedimentation
Notes: In this Chapter we will be discussing:
Erosion Process
Different Types of Erosion
Physical/Biological effects,
Hazards with Land Development
Principles of E&S Control

## Slide 2: Erosion
Process by which the land surface is worn away by the action of wind, water, and gravity
Notes: EROSION -----Process by which sediments are detached from soil mass, transported by the means listed WIND, WATER, and GRAVITY.

## Slide 3: Sedimentation
Settling of soil particles transported by wind and water
Notes: Erosion leads to sedimentation – occurs when velocity of wind/water carrying the sediment slows to the point at which it settles out of suspension. Heavier particles such as sand and gravel will settle out more rapidly then fine particles such as clay and silt.
Sediment deposition occurs when the velocity (energy) of the transporting stream decreases. Important in FL – streams here have low gradients and low velocities, so, deposition will dominate the transport of soil particles in water.

## Slide 4: Natural Erosion vs. Accelerated Erosion
Natural Erosion is relatively slow and uniform
Manmade erosion is 10 times greater than natural
Notes: Natural/geologic erosion – relatively slow rate and uniform rate since the beginning of time and is the major factor in creating the earth as we see today.
Examples of geologic erosion would be: valley’s, rolling farm lands, estuaries and barrier islands along the coast.
Geologic erosion produces about 30% of all sediment in the United States.
Accelerated erosion – increased rate of erosion/removal of vegetative cover or altering contour of ground. Accelerated erosion accounts for 70% of erosion in the US.
Farming and construction are the principal causes of accelerated erosion, although any activity that disturbs land can increase the natural erosion rate.

## Slide 5: Types of Erosion
Wind Erosion vs. Water Erosion
Annual Loss - 765 million tons (NRCS)
Annual Loss - 959 million tons and 2.6 tons/acre/year in Florida (NRCS)
Notes: Two different types of erosion previously mentioned.

## Slide 6
Stream & channel erosion
Overland erosion
Types of Erosion
Notes: Two types of water erosion – overland and channel
Overland erosion occurs when slopes stripped of cover raindrops hit splash and runoff – largest source of sediment during construction

## Slide 7
Types of Water Erosion
Notes: There are two principal types of water erosion: overland erosion and channel erosion. Overland erosion occurs on denuded slopes when raindrops splash and run off.
Overland erosion is the largest source of sediment during construction activities
The 5 types are”

## Slide 8: Splash (Raindrop) Erosion
Terminal speed of a large raindrop is about 20mph.
Raindrop impacts on exposed soil surfaces start the erosion process.
Notes: raindrops will dislodge the soil particles splash them into the air – now vulnerable to sheet erosion

## Slide 9: Sheet Flow Erosion
Notes: Sheet- cause shallow sheets of water rolling across the land – seldom the cause of erosion itself but the flow will move the detached particles caused by splash erosion. Shallow flow will concentrate/collect in low land spots

## Slide 10: Rill Erosion
Notes: Rill – shallow surface flow begins to concentrate/collect (yellow arrow) in the low land spots, increases velocity and turbulence in these areas, which causes more detachments and transportation of particles. Cuts tiny channels called a rill.

## Slide 11: Gully Erosion
Notes: Gully – Rills come together to form larger and larger channels – difference between a gully and a rill is the size

## Slide 12: Rill vs. Gully
What is the difference between a rill and a gully?
Rills are small - a few inches wide/deep
Gullies are large and difficult to correct
Given enough time, soil depth, and water flow – rills will become gullies
Notes: Again size is the difference between a rill and a gully
A rill will become a gully given enough time

## Slide 13: Stream and Channel Erosion (Mass Wasting)
Notes: Occurs as the volume and velocity of flow increase sufficiently to cause the movement of the stream bed and bank materials to erode

## Slide 14: 1.4 Four Factors Influencing Erosion
3) Topography
EROSION
1) Soil characteristics
4) Climate (rainfall)
2) Vegetative cover
Notes: Erosion potential of an area determined by four factors. These will be discussed separately but they are inter-related.

## Slide 15: Factors Influencing Erosion
Texture
Organic Matter
Structure
Permeability
SOIL
3
1) Soil characteristics
2) Vegetative Cover
3) Topography
4) Climate
Notes: Soil properties affect infiltration capacity of a soil and those that affect resistance of the soil to detach and transport by flowing or falling water.
Soils that contain high % of silt and very fine sand are generally the most erodible; as clay and organic matter increases. erodibility decreases. Clay can bind soils keeping erosion from occurring, making it erosion resistant. But if clay detaches it is carried easily by water and hard to settle out.
Organic matter soils – improve permeability, resist raindrop detachment and absorb rainwater which minimizes erosion. Gravels are the least erodible if well drained, graded, and some include larger sand grains. Coarse gravel highly permeable and good adsorption capacity (prevent or delay) reduces surface runoff. Chapter 2 (Soils) provides further explanation.

## Slide 16: Factors Influencing Erosion
Shields soil from impact of rain
Roots hold soil in place
Maintains soil’s capacity to absorb water
Slows velocity of runoff
Removes water through evapotranspiration
1) Soil characteristics
2) Vegetative Cover
3) Topography
4) Climate
Notes: Very important – can be controlled by scheduling vegetation removal in stages, decreasing area exposed and duration

## Slide 17
Factors Influencing Erosion
Orientation
Slope Gradient
Slope Length
1) Soil characteristics
2) Vegetative Cover
3) Topography
4) Climate
vs
Steeper slope and longer length = Water flows with higher velocity and energy, causing more erosion

## Slide 18: Factors Influencing Erosion
Florida’s average wet season: May to Mid-October
Florida’s dry season: November to May
Florida’s average annual rainfall over the last 10 years is 55.85” per year, ranging from 48.99” to 60.52”
Peak Hurricane Season: August to October according to the Nat’l Weather Service
1) Soil characteristics
2) Vegetative Cover
3) Topography
4) Climate
Notes: Frequency, intensity and duration of rainfall important to determine
Wet season erosion risks are high
Land disturbing activities should be scheduled to take place during periods of low precipitation and low runoff.
Stabilize prior to time of year when high potential will exist.

## Slide 19
Florida’s Average Annual Precipitation
Highest in Panhandle
Notes: Depending on where you are working in the state could impact your plans also so take that into consideration.

## Slide 20: 1.5 Impacts of Sedimentation and Erosion
Four billion tons of material reach water bodies in US
One billion tons of material reach oceans
10% overall due to construction activities
But, this can represent 50% of eroded material in watersheds undergoing development
Notes: 4 Billion tons of sediment are estimated to reach the ponds, rivers, and lake of our country alone.
1 billion tons to our oceans including the Gulf of Mexico.
10% of this sediment amount comes directly from erosion from land undergoing highway construction or land development.
This 10% represents more than half or 50% of the sediment load going into streams in watershed undergoing development.

## Slide 21: Sediment Yields to Streams
200 to 500 tons per square mile per year (t/mi2/yr) in stable urban area.
1,000 to 100,000 tons per square mile per year (t/mi2/yr) in active, developing area (5 to 200 times as much).
Cleared land vs. forest: 20,000 to 40,000 times as much.

## Slide 22
MASSIVE SEDIMENT YIELDS
Notes: You can see billions of tons of deposits over time in these alluvial fans of this delta region.

## Slide 23: Sediment
For every acre under construction without effective erosion control, about one dump truck load of soil per year washes into a nearby lake or water body. This soil contains materials which are toxic when released into water.
Pb – Lead
Cr – Chromium
As – Arsenic
Zn – Zinc
Cd – Cadmium
Cu – Copper
Hg – Mercury
Ni – Nickel
and Others!

## Slide 24: Transport vs. Deposition
Deposition is the dominant process here due to the slow speed of Florida’s streams, canals, and lakes.
Heavy particles (sand and silt) settle first, in pipes, ditches, canals, rivers, lakes.
Fine particles (clays and muck) stay in suspension for weeks in rivers, lakes, canals; a.k.a. turbidity.

## Slide 25
Deposition
Turbidity
Transport vs. Deposition
Notes: Examples of each impact

## Slide 26: Physical Effects of Sedimentation
Reduced hydraulic capacity of rivers and channels
Increased flooding
Increased maintenance costs for stormwater management systems
Lost capacity in water supply reservoirs
Decreased recreational value
Increased dredging of navigable waterways
Increased water treatment costs

## Slide 27
Increased dredging
Reduced hydraulic capacity
Increased maintenance
Decreased recreational value
Physical Effects of Sedimentation
Notes: Examples of physical effects of sedimentation

## Slide 28: Decreased Recreational Value

## Slide 29: Biological Effects of Sedimentation
Screens out sunlight - decline in plant growth
Disruption of food chain - decline in sport fish and increase in trash fish.
Small amounts impair fish spawning
Large amounts clog gills
Blankets bottom which destroys habitat and suppresses aquatic life

## Slide 30: Screens out Sunlight – Decline in Plant Growth

## Slide 31: Sedimentation Disrupts Ecosystems
ECOSYSTEM

## Slide 32
Increase in area exposed to stormwater and erosion
Alteration of runoff patterns
Alteration of ground water regime
Creation of south or west facing exposures with poor conditions for plant growth
Exposure of subsurface soils unsuitable for plant growth
1.6 Erosion and Sedimentation Hazards Associated With Land Development

## Slide 33
Increased volume of runoff, accelerated erosion, higher sediment yield, and higher peak flows caused by:
  Removal of existing protective vegetation
  Exposure of more erodible or less pervious subsurface soils
  Reduced permeability due to compaction by heavy equipment
  Enlarged drainage areas created by grading
  Increased impervious areas
1.6 Erosion and Sedimentation Hazards Associated With Land Development

## Slide 34
Offsite Impacts: Breached perimeter controls, mud in roads, damage to surface water and wetlands
Surface Water and Wetlands are damaged
Roadway hazards from tracked mud
1.6 Erosion and Sedimentation Hazards Associated With Land Development

## Slide 35
Plan the development to fit the particular topography, soils, drainage patterns, and natural vegetation of the site
Wetland area
Slope and clay soils
1.7 Principles of Erosion and Sediment Control

## Slide 36
Apply erosion control practices to prevent on-site damages
Rolled Erosion Control Product - RECP
1.7 Principles of Erosion and Sediment Control
Notes: Rolled Erosion Control Product (RECP) applied around pond with grass seed applied under the RECP.

## Slide 37: Apply perimeter control practices to protect disturbed areas from off-site runoff, and to prevent sediment damage to areas below the development site
1.7 Principles of Erosion and Sediment Control
Notes: Isolate the development site from surrounding properties, control sediment once it is produced, preventing transport from site. Diversions, berms, sediment basins …examples

## Slide 38
Keep runoff velocities low and retain runoff on-site
Stabilize disturbed areas immediately after final grading (i.e., sod), temporary seed area within one week if the final grading is several weeks away
1.7 Principles of Erosion and Sediment Control
Notes: Keep slope length short and gradients low…use stable outlets to convey stormwater around the site… these systems should be able to hold peak flows, should be operational ASAP after start of construction.

## Slide 39
Implement a thorough maintenance and follow-up program (repair, replace, improve, keep records)
Lack of inspection and maintenance
Inspected and maintained
1.7 Principles of Erosion and Sediment Control

## Slide 40: Chapter 1 Review
Notes: Please open to Chapter 1 of your review workbook. I will give you a 5 minutes to complete and then we will go over them together.

## Slide 41
is the process by which the land surface is worn away by the action of wind, water, and gravity.
is the settling out of soil particles transported by water and wind.
Soil erosion can be classified as ______ erosion or _______ erosion, and the sources can be either ________ or __________.
Water erosion can be classified as either _______ erosion or _______ and channel erosion.
Erosion
Sedimentation
wind
water
overland
stream
natural manmade
Chapter 1 Review

## Slide 42
Four processes of overland erosion are:
  Splash or rain drop erosion
  Sheet erosion
  Rill erosion
  Gully erosion
Four principal factors influencing soil erosion are:
  Soil characteristics
  Vegetative cover
  Topography
  Climate
List three physical effects of erosion and sedimentation:
  Increased flooding.
  Reduced hydraulic capacity in rivers, streams, channels, reservoirs.
  Increased maintenance of stormwater systems.
  Increased water treatment costs.
  Decreased recreational value.
Chapter 1 Review

## Slide 43
List three biological effects of erosion and sedimentation:
  Reduced light for aquatic plants
  Clogs fish gills
  Impairs spawning
  Disrupts food chain
  Blankets bottom, suppresses aquatic life
  Disrupts ecosystem
Plan the development to fit the terrain using the particular:
  Topography
  Soils
  Drainage patterns
  Natural vegetation of the site
  Minimize the extent of the area exposed at one time and the duration of exposure
Chapter 1 Review

## Slide 44
Apply practices to protect the disturbed area from off-site runoff and to protect off-site areas from sediment damage.
Apply practices to prevent excessive on-site damage.
Keep runoff velocities and runoff on the site.
It is very important to Stabilize disturbed areas
after final grading to prevent raindrop impacts from causing erosion.
Implement a thorough and _ (inspection) program as required in the Construction Generic Permit (CGP).
perimeter control
erosion control
low
retain
immediately
maintenance follow up
Chapter 1 Review