## Slide 1
Chapter 5:
Best Management Practices for Dewatering

## Slide 2: BMPs for Dewatering
Introduction
Dewatering Operations are practices that manage the discharge of pollutants when water (other than stormwater) must be removed from the work location so that construction may be carried out.

## Slide 3
Key Considerations for choosing a specific dewatering control method:
Sediment particle size
Limitations for receiving waters (turbidity, nutrients, pollutants)
Discharge rate
Area available for control technique
BMPs for Dewatering

## Slide 4
Dewatering Operations Flow Chart
This Chapter will discuss four types of control technologies:
Sediment Traps
Weir Tanks
Filters
Chemical Treatment
BMPs for Dewatering

## Slide 5
Typical Pumping Methods:
Rim Ditch (Sump)
Sock System (Horizontal Well)
Well Point System (Vertical Well)
BMPs for Dewatering

## Slide 6
Direct discharge usually does not meet WQ standards
Often results in compliance action by agencies
Initially cheapest for contractor
Most expensive to clean up
Can be used as part of “treatment train”
Rim Ditch Systems
Ditch surrounds work area and draws down groundwater
Poorest water quality (high turbidity, NTUs)!
BMPs for Dewatering

## Slide 7
Sock Systems
Generally, produces clean discharge water
Requires some sandy soils to function (does not work well in clay soils)
Placed along perimeter of project
Can be expensive to install
BMPs for Dewatering

## Slide 8
Well Point Systems
Produces cleanest water
Requires some sandy soils to function
Usually placed along excavation in terrace fashion (can also be linear)
Can be expensive to install
Often reduces downtime in wet weather, as it keeps the site dry
BMPs for Dewatering

## Slide 9
Well Point Systems
BMPs for Dewatering

## Slide 10
Well Point Systems
BMPs for Dewatering

## Slide 11
WHERE IS THIS DISCHARGE GOING?
BMPs for Dewatering

## Slide 12
Without Discharge Protection
With Discharge Protection
BMPs for Dewatering

## Slide 13
BMPs for Dewatering

## Slide 14
BMPs for Dewatering

## Slide 15
Challenges
BMPs for Dewatering

## Slide 16
Discharges of produced groundwater from a non-contaminated site, require an FDEP Generic Permit for compliance with the NPDES program.
  This can now be obtained as part of the CGP NOI.
  Effective February 10, 2015
Contaminated sites need to contact FDEP before dewatering.
Additional information: http://www.dep.state.fl.us/water/wastewater/iw/genperm.htm
Water Management District Permits
Local governments should also be contacted regarding compliance requirements for dewatering.
5.2 Limitations
BMPs for Dewatering

## Slide 17
5.2 Limitations
FDEP Generic Permit for Dewatering from Non-Contaminated Sites
  Greater than 500’ from known contamination areas
  File Notice of Intent (NOI) (select dewatering option)
  100$ Fee
  Coverage for 5 years
  File Notice of Termination (NOT)
  Can Obtain with CGP (Sites > 1 acre)
Individual Permits
  Required for Contaminated Sites
  Contamination status can be checked through FDEP’s “Contamination Locator Map” website or FDEP’s Map Direct with Institutional Controls Registry data layer
  Must Coordinate with FDEP
BMPs for Dewatering

## Slide 18
5.2 Limitations
BMPs for Dewatering

## Slide 19
5.2 Limitations
BMPs for Dewatering

## Slide 20
Tools applicant can use to determine cleanup restoration status.
Contamination Locator Map (CLM)
http://prodenv.dep.state.fl.us/DepClnup/welcome.do
Institutional Controls Registry (ICR)
https://floridadep.gov/waste/waste/content/institutional-controls-registry-guidance
Applicants may use other sources to determine whether contamination is present.
Remember - You can always contact your local DEP district office for advice!
BMPs for Dewatering
5.2 Limitations

## Slide 21
5.2 Limitations
BMPs for Dewatering
Map Direct with Institutional Controls Registry (ICR)
https://ca.dep.state.fl.us/mapdirect/

## Slide 22
5.2 Limitations
BMPs for Dewatering
Running a buffer search with 500’ radius around a chosen point or address

## Slide 23
5.2 Limitations
BMPs for Dewatering
Buffer search radius result showing contaminated sites within 500’ of the project site

## Slide 24
5.3 Implementation
FDEP Dewatering Permit Requirements
Log & Monitor Flow Rates; sample weekly, possibly daily
Develop & Implement Site Specific BMPs
Weekly inspection & maintenance
Maintain Records On-Site
  Flow Rates & Sampling
  Permit, NOI, Approval Letter
  Weekly Inspections
  Maintenance Records
  Records of Chemicals Used
Keep Records 3 years
BMPs for Dewatering

## Slide 25
FDEP Dewatering Permit Requirements
“The Permittee shall report any characteristic in the effluent that could indicate the presence of a pollutant or pollutants not previously identified or anticipated (e.g. sheen, odor), and the occurrence, or new knowledge of, and spills, leaks or contamination in the vicinity of the project that could impact the water quality of the effluent.”
Cease operations & Contact DEP
24 Hour Reporting – State Warning Point - 1-800-320-0519
  Report “unauthorized releases or spills of untreated groundwater from dewatering operations” >1000 gal where effluent limitations are exceeded, or
  Where information indicates public health or the environment will be endangered
All permits and approvals must be secured (getting one does not ensure others)
Don’t assume you are permitted unless you can see it and review it!
BMPs for Dewatering
5.3 Implementation

## Slide 26
Inspect & verify that BMP’s are in place and functional before dewatering activities.
Monitor BMP’s throughout dewatering and after rain events
Remove accumulated sediment to ensure BMP effectiveness
Logbook of daily turbidity readings
Flow Rates
5.4 Inspection & Maintenance
BMPs for Dewatering

## Slide 27
5.5.1 Temporary Sediment Traps and Sediment Basins
A temporary basin created to detain sediment-laden runoff and allow sediment to settle out before discharging
BMPs for Dewatering

## Slide 28
Purpose:
The removal of large and medium particles and some metals that settle out with sediment.
5.5.1 Temporary Sediment Traps and Sediment Basins
BMPs for Dewatering

## Slide 29
Purpose:
Effective for the removal of sand, silt, and some metals that settle out with sediment.
5.5.1 Sediment Basin
BMPs for Dewatering

## Slide 30
Where & How Are Sediment Traps/Basins Commonly Used?
Tips:
The inflow pipe should be located as far from the outfall as possible - increases time for settling
Outfall should be stabilized with rock or non-erosive material
BMPs for Dewatering
Notes: The inflow pipe should be located as far from the outfall structure as possible. This increases the amount of time the water is in the basin and allows more time for the sediment to settle out.
The outfall should be stabilized with rock or vegetation or other non-erosive material.
An offsite discharge sampling location should be identified and used, as needed or required by dewatering plan/permit.

## Slide 31
5.5.1 Sediment Trap & Basin
Daily inspections are recommended to prevent washouts, scouring and embankment blowouts.
Remove sediments when 1/2 full, or sooner.
Ensure banks are stabilized.
Maintenance:
BMPs for Dewatering

## Slide 32
Weir tanks and dewatering tanks separate water and waste (sediment, oil & grease, trash) by using weirs, baffles, and/or filter cloth.
5.5.2 Weir Tanks & Dewatering Tanks
BMPs for Dewatering

## Slide 33
Purpose: to separate sediment and other materials from water in dewatering operations.
BMPs for Dewatering
5.5.2 Weir Tanks & Dewatering Tanks

## Slide 34
Weir tanks are used in the treatment train to reduce turbidity in highway dewatering operation prior to discharge.
BMPs for Dewatering
Notes: The tanks are generally delivered to the site by a vendor who also provides assistance with the set up and operation of the dewatering operation. Tank size depends on site conditions.
High levels of flows may require the use of multiple tanks used in parallel or in series to provide pre-treatment for other treatment methods.

## Slide 35
Inspect for and remove sediment accumulation
Oil & grease disposal by a licensed company
Maintenance:
BMPs for Dewatering
5.5.2 Weir Tanks & Dewatering Tanks

## Slide 36
A dewatering tank removes debris & sediment. Flow enters through the top, passes through a filter, and discharges through the bottom of the tank.
BMPs for Dewatering
5.5.2 Weir Tanks & Dewatering Tanks

## Slide 37
5.5.3 Gravity Bag Filter
A nonwoven geotextile fabric bag that collects sand, silt, and fine particles.
BMPs for Dewatering
Notes: A gravity bag filter, or dewatering bag is a square or rectangular bag made of nonwoven geotextile fabric that collects sand, silt and some fines inside as water is pumped through it.

## Slide 38
Purpose: The removal of larger particles and some metals in dewatering operations.
BMPs for Dewatering
5.5.3 Gravity Bag Filter

## Slide 39
Where & How is a Gravity Bag Filter Commonly Used?
Water is pumped through the bag and seeps through the bottom and sides of the bag and onto the ground.
The ground should be stabilized or protected so that turbid conditions are not created by the bag.
BMPs for Dewatering

## Slide 40
5.5.3 Gravity Bag Filter
Maintenance:
Inspect bag regularly during use for:
  flow conditions
  bag conditions
  bag capacity
  secondary barrier, if applicable
Replace bag when it no longer functions
Dispose of offsite
BMPs for Dewatering

## Slide 41
Maintenance: If full, or no longer passes water, replace
BMPs for Dewatering
5.5.3 Gravity Bag Filter

## Slide 42
Maintenance: Secondary stabilization often required
BMPs for Dewatering
5.5.3 Gravity Bag Filter

## Slide 43
Water is treated by passing it though canisters filled with sand media.
5.5.3 Sand Media Filter
BMPs for Dewatering

## Slide 44
5.5.3 Pressurized Bag & Cartridge Filters
Pressurized Bag Filter
(Source: http://www.dot.ca.gov)
Cartridge Filter
(Source: http://www.dot.ca.gov)
These water filtering units consist of filter bags and/or cartridge filters to clean water.
BMPs for Dewatering

## Slide 45
5.5.3 Pressurized Bag & Cartridge Filters
Purpose: Effective for the removal trash, gravel, sand, silt, some metals, as well as the reduction of turbidity
Maintenance:
Inspect regularly
Replace Filter Bags
Replace Cartridges
BMPs for Dewatering

## Slide 46
5.5.4 Chemical Treatment
Reducing turbidity by applying a flocculant:
Polyacrylamide (PAM)
Aluminum Sulfate (Alum)
BMPs for Dewatering

## Slide 47
Reducing turbidity by applying a flocculant:
Polyacrylamide (PAM) Aluminum Sulfate (Alum)
BMPs for Dewatering
5.5.4 Chemical Treatment
PAM and Alum are both Anionic molecules and considered by the State of Florida to be non-toxic when used per manufacturer’s specifications
Cationic flocculants must have testing and approval before use (usually contain a toxic heavy metal)

## Slide 48
Purpose:
Chemical treatment is used to significantly reduce turbid conditions on a site. This should be considered where turbid discharges to sensitive waters cannot be avoided using available BMPs.
BMPs for Dewatering
5.5.4 Chemical Treatment

## Slide 49
Manifold System combining dewatering pumps with in-line flocculant blocks
BMPs for Dewatering
5.5.4 Chemical Treatment

## Slide 50
Chemicals used must have toxicity testing results and FDEP approval
Any discharge from chemically treated dewatering operations must be nontoxic to aquatic organisms.
The discharge must meet all water quality standards for turbidity: < 29 NTUs above background or < background for OFWs. pH must be similar to receiving water.
Lab tests & field monitoring required. Sample and test the pH and turbidity frequently or during each batch release of chemically treated water.
Considerations for Use
BMPs for Dewatering
5.5.4 Chemical Treatment

## Slide 51
Laboratory jar test
Certified applicator
The right chemical at the right dosage!
Where & How is Chemical Treatment Commonly Used?
BMPs for Dewatering

## Slide 52
Alum application from boat
Check turbidity after application and record – compare to already known background for that waterbody
BMPs for Dewatering
Where & How is Chemical Treatment Commonly Used?

## Slide 53
Completed application
Check pH!!
BMPs for Dewatering
Where & How is Chemical Treatment Commonly Used?

## Slide 54
Alum Treatment with Sediment Basin
BMPs for Dewatering

## Slide 55
This is not an approved treatment system!
The right chemical at the right dosage!
BMPs for Dewatering

## Slide 56
CTS-1 Continuous Treatment
Purpose: a designed flow-through system to provide continuous treatment of turbid water.
BMPs for Dewatering

## Slide 57
Continuous Flow Through Alum Treatment System
Pumps
Discharge
Inflow cell 1
Alum tanks
Cell 2
Cell 4
Cell 3
BMPs for Dewatering

## Slide 58
Polyacrylamide (PAM) - Floc Log Technology
BMPs for Dewatering

## Slide 59
BMPs for Dewatering

## Slide 60
Grit Pit For Heavy Sediment
Baffle Grid System
BMPs for Dewatering

## Slide 61
BMPs for Dewatering

## Slide 62
BMPs for Dewatering

## Slide 63
BMPs for Dewatering

## Slide 64
BMPs for Dewatering

## Slide 65
BMPs for Dewatering

## Slide 66
Water Clarification: Treatment Ditches using Baffle Grid and Mixing Trough with PAM
BMPs for Dewatering

## Slide 67
Additional Treatment Systems
BMPs for Dewatering

## Slide 68
CTS-2 Batch Treatment
Purpose: chemical treatment of turbid water using ponds or portable, trailer-mounted tanks.
BMPs for Dewatering

## Slide 69
Pump
Dual Channel System Allows For Continuous Discharge During Maintenance
Final (clean) Discharge
One channel is online while the other is down for maintenance
Long-term Operational System
Turbid Input
CTS-2 Batch Treatment
BMPs for Dewatering

## Slide 70
BMPs for Dewatering
CTS-2 Batch Treatment

## Slide 71
BMPs for Dewatering
CTS-2 Batch Treatment

## Slide 72
BMPs for Dewatering
CTS-2 Batch Treatment

## Slide 73
BMPs for Dewatering
CTS-2 Batch Treatment

## Slide 74
BMPs for Dewatering
CTS-2 Batch Treatment

## Slide 75
BMPs for Dewatering
CTS-2 Batch Treatment

## Slide 76
BMPs for Dewatering
CTS-2 Batch Treatment

## Slide 77
5.4 Inspection & Maintenance
Monitor turbidity and pH levels
Inspect, clean, repair all flocculants and sediment collection devices
Ensure effectiveness not impacted by rain events
BMPs for Dewatering

## Slide 78
Reminder: Obtain all Proper Approvals
Federal
State
  FDEP
  Water Management Districts (WMD)
Local
  County
  City
BMPs for Dewatering

## Slide 79
Reminder: Obtain All Proper Approvals
BMPs for Dewatering

## Slide 80
Reminder: Maintain Adequate BMPs and Replace/Repair as Needed!
BMPs for Dewatering

## Slide 81
What is Wrong With this?
BMPs for Dewatering

## Slide 82
What 35,000 NTUs Looks Like
BMPs for Dewatering

## Slide 83
Chapter 5 REVIEW
What are the types of dewatering systems that generally produce the clearest and non-turbid discharge from groundwater?
Well-Point and Horizontal Sock (Sock/Horizontal Pumps).
What kind of water quality does a rim ditch system produce?
The poorest water quality with the highest turbidity NTU levels.
What must a well-point and horizontal pump system have in order to function properly?
Primarily sandy soil.
What methods are used to manage (treat) nonstormwater discharges & remove sediment from construction pumping?
Sediment traps and basins, weir and dewatering tanks, and chemical treatment.
BMPs for Dewatering

## Slide 84
FDEP General Permit for Dewatering requires that you be how many feet from a “known contamination source?”
500 feet or greater.
What tools can be used by the permit applicant to determine the cleanup and restoration status of a known contamination site?
The Contamination Locator Map (CLM) and the Institutional Controls Registry Web Viewer.
What must the permittee do if they observe the presence of a pollutant or pollutants such as a sheen, or odor while dewatering?
Cease operations immediately, contact their DEP District Ground Water Section for guidance, and contact the 24 Hour Reporting – State Warning Point.
BMPs for Dewatering
Chapter 5 REVIEW

## Slide 85
When using chemical treatment systems, what should you remember?
“The right chemical at the right dosage.”
What two are the most common and approved flocculant chemicals utilized to control turbidity on a job site to reduce turbidity?
Anionic Polyacrylamide (PAM) and Aluminum Sulfate (Alum).
Before discharging chemically treated water, what should you test for?
pH and turbidity limits.
BMPs for Dewatering
Chapter 5 REVIEW