## Slide 1
Chapter 9
Inspection and Enforcement

## Slide 2
Specific duties and responsibilities of an inspector depend on the employing agency:
Public: city, county, state, federal, etc.
Private: engineering inspection company, construction company, other consultant company, non-profit group, etc.
There are many forms of training:
DEP class you are now taking (FSESCI), Envirocert through CPESC, Stormwater One, etc., plus large company specific training like Walmart and Home Depot.
However, there is no substitute for on-the-job training from experienced inspectors and instructors.
Supplement your understanding and knowledge of associated environmental issues by joining industry groups, subscribing to magazines and websites for BMP info
9.1 Introduction

## Slide 3
Conduct
Compliance
Handling violations
Documentation
9.2 The Role of the Inspector

## Slide 4
An inspector must conduct themselves with:
Integrity
Fairness
Commitment
9.2.1 Conduct

## Slide 5
An inspector must have the necessary technical expertise and be:
Organized
Unbiased and consistent
Professional and courteous
9.2.1 Conduct

## Slide 6
PROMOTE TEAMWORK!
Construction and inspection should be working towards the same goal
Collaborate and seek shared solutions – be willing to revise or change if something isn’t working
9.2.1 Conduct

## Slide 7
Build Partnerships
As an inspector – be the person that people come to first with issues or BMP failures because they know you are fair and a good partner towards achieving compliance
9.2.1 Conduct

## Slide 8
9.2.2 Compliance
Make sure you have the proper permits, such as:
CGP NOI Permit (FDEP NPDES) – remember to have your SWPPP before, right?
ERP for stormwater and wetland impacts (FDEP/WMD/ACOE/local)
County and city permits
Other specific permits (Air quality? Hazardous materials? Contaminated site? Etc.)
Compliance
Site permitted, all BMPs installed per plan & maintained
Performance oriented
No off-site impacts
Doesn’t matter if it should work, does it actually work?

## Slide 9
Inspection duties
Project permitted.
BMPs properly installed and maintained.
Erosion is controlled.
Off-site sedimentation is prevented.
Off-site turbidity is prevented.
Paperwork up-to-date
9.2.2 Compliance

## Slide 10
9.2.3 Handling Violations
Documentation
Write report onsite or as soon as possible after inspection for every site and every inspection.
Pictures, pictures, pictures!
Legible, concise, thorough and neat.

## Slide 11
9.2.3 Handling Violations
Are all BMPs installed correctly and maintained ?

## Slide 12
Is off-site sedimentation and/or turbidity being controlled?
9.2.3 Handling Violations

## Slide 13
If “YES” to all, the site is in compliance.
If “NO” to any, then the site is in violation.
9.2.3 Handling Violations

## Slide 14
Ask yourself these basic questions before and after each inspection
Is the project permitted?
Are all BMPs properly installed and maintained?
Is on-site erosion being controlled?
Is off-site sedimentation and/or turbidity being controlled?
Is paperwork complete and up-to-date?
If “YES” to all, the site is in compliance
If “NO” to any, the site is in violation
9.3.1 The Inspection

## Slide 15
Is on-site erosion being controlled?
9.3.1 The Inspection

## Slide 16
Is the project permitted?
9.3.1 The Inspection

## Slide 17
Be Reasonable
The rules are performance based - allow innovative thinking, BMP combinations
Understand the function of BMPs = know the tolerances, consequences of failure.
Listen with an open mind - make the contractor your partner in problem solving.
9.3.2 Tolerances

## Slide 18
Study Plans, Maps, Photos, Permit Files
Sensitive areas: wetlands, waterbodies, natural drainage system, severe grades, erodible soils
Critical erosion areas: cuts, fills, waterways, streambanks, outlets
Construction plans: Stormwater management, utilities, buildings, roads
Schedule: phases, BMP installation, temporary seeding
9.3.3 Preparing for an Inspection

## Slide 19
Perimeter: Off-site runoff, on-site runoff
Inspection and maintenance - Who? When?
Access to BMPs – stored onsite or off
Note stockpiles, borrow pits, haul roads, waste storage
Existing noncompliance, existing nonconforming land uses
Hi-lite plans, make lists
9.3.3 Preparing for an Inspection

## Slide 20
Communication: Inspector, contractor, owner
Contact person: Name, address, 24-hour phone number
Responsibility: Schedule, performance, plan changes, maintenance, contingencies
Inspection Schedule:
  Must be upheld – it’s a permit condition!
  Erosion control and stormwater management FIRST
  No construction while noncompliant discharge is left ignored
9.3.3 Preparing for an Inspection

## Slide 21
Plan changes: Thresholds, procedures
Critical areas identified – subcontractors informed
Contractor understands how and when perimeter and internal BMPs are installed.
Maintenance of BMPs: Who, when; supplies stockpiled for severe storms.
Affirmation: Provide copies of plans/permits to everyone; confirm understanding of plans, schedule, responsibilities. MUST sign and date.
9.3.4 Preconstruction Conference

## Slide 22
Before your inspection
Be familiar with the plans, details, schedule, and file history for each site.
Organize your route if you are inspecting several sites.
Always take the plans, file, and reporting forms.
Take measuring or surveying equipment.
Take photo or video equipment.
Personal protection: Boots, sun and insect protection, 2-way radio or cell phone.
9.3.5 Before You Leave the Office

## Slide 23
Take plans and file on-site.
Check in at contractor’s field office.
Take orderly, thorough, legible notes.
Walk the perimeter - from low to high.
Check internal BMPs - from low to high.
BMPs sized and installed OK, contributing area OK.
Ask questions and poke around; you’re an inspector!
9.3.6 Inspecting the Site

## Slide 24
Causes of Non-Compliance
Little or no effort to comply.
Inadequate design or changes in site conditions.
Faulty installation and/or poor maintenance.
Failure to plan for severe weather
9.3.7 Causes of Noncompliance

## Slide 25
Little or no effort to comply:
Not submitting a plan or applying for a permit.
Failure to follow approved plan.
9.3.7 Causes of Noncompliance

## Slide 26
Inadequate design or changes in site conditions:
Structural BMPs ineffective.
Ground cover failing due to slope or excessive runoff velocity and/or volume.
Contributing areas changed, additional BMPs required.
Maintenance overload.
9.3.7 Causes of Noncompliance

## Slide 27
9.3.7 Causes of Noncompliance

## Slide 28
Faulty installation and/or poor maintenance:
This is the MOST COMMON REASON in Florida.
This is the reason why YOU ARE HERE.
9.3.7 Causes of Noncompliance

## Slide 29
and/or poor maintenance
Faulty installation
“Air fence”
Don’t just add another row after first is covered!
9.3.7 Causes of Noncompliance

## Slide 30
Document all findings:
  Correct form(s)?
  BMPs maintained?
  Ready for next storm?
Subcontractors informed/complying?
Schedule compliance.
Notes/comments
Date and type of inspection
Fill out report on site, report to contractor - ok or not
Finalize report and digitize back at office – if needed
9.3.8 Inspection Reports

## Slide 31
2
3
Inspect from low to high
4
1
9.3.8 Inspection Reports

## Slide 32
Discharging clean?
Correct BMP for inlet type?
BMP installed correctly?
Materials storage problems?
9.3.8 Inspection Reports

## Slide 33
BMPs?
Off-site impacts?
Ready for next storm?
Dewatering?
Report
9.3.8 Inspection Reports

## Slide 34
9.3.8 Inspection Reports – Your Turn!

## Slide 35
9.3.8 Inspection Reports – Your Turn!

## Slide 36
You are inspecting now!
What should you say in your inspection report about this site?
9.3.8 Inspection Reports – Your Turn!

## Slide 37
You are inspecting ……
What should you say in your inspection report about this site?
9.3.8 Inspection Reports – Your Turn!

## Slide 38
You are inspecting ……
9.3.8 Inspection Reports – Your Turn!
What should you say in your inspection report about this site?

## Slide 39
You are inspecting ……
9.3.8 Inspection Reports – Your Turn!
What should you say in your inspection report about this site?

## Slide 40
You are inspecting ……
9.3.8 Inspection Reports – Your Turn!
What should you say in your inspection report about this site?

## Slide 41
You are inspecting ……
9.3.8 Inspection Reports – Your Turn!
What should you say in your inspection report about this site?

## Slide 42
You are inspecting ……
9.3.8 Inspection Reports – Your Turn!
What should you say in your inspection report about this site?

## Slide 43
You are done… but time for the crew to fix the violations.
Only when you get the report to the maintenance or repair crew; ASAP!
They have seven calendar days to complete repair or replace after your report.
9.3.8 Inspection Reports – Your Turn!

## Slide 44
9.4 Regulatory Agencies

## Slide 45
U.S. Environmental Protection Agency (EPA) – Oversees the federal wetlands program and the NPDES Stormwater Program.
U.S. Army Corps of Engineers (USACE) – Has jurisdiction over the permitting of the federal wetlands program, Section 404 of the federal Clean Water Act, and Section 10 of the federal River and Harbors Act.
Florida Department of Environmental Protection (DEP) – Has oversight of Florida’s wetlands programs and acts as the permitting authority for the state's NPDES Stormwater Program, dewatering activities, the Construction Generic Permit (CGP), and some aspects of Section 404 of the federal Clean Water Act.
9.4 Regulatory Agencies

## Slide 46
Water Management Districts – There are five water management districts in the state: Northwest Florida, Suwannee River, St. Johns River, Southwest Florida, and South Florida. These regional agencies implement the state's wetlands permitting program for most larger types of projects, as well as consumptive use and Environmental Resource Permitting (ERP) along with DEP.
Counties/Cities/Community Development Districts/Other Special Districts – These governmental entities have responsibilities for the MS4 under their jurisdiction, a multitude of local ordinances (Land Development Codes) that can be more restrictive than those of the federal, state, and regional governmental programs.
9.4 Regulatory Agencies

## Slide 47
Chapter 9 Review

## Slide 48
In addition to technical knowledge, the inspector must be able to effectively deal with ______.
In dealing with the public, it is most important to follow proper procedures, and to always be __________ and ____.
The erosion and sediment control rules are __________________. This means that the BMPs must be ________ in controlling erosion and preventing off-site sedimentation for the site to be in compliance.
Off-site sedimentation is excusable only if all BMPs have been installed per an approved plan (True/ False).
Inspector's job is to find out if:
a) an erosion and sediment control plan has been approved (permitted).
b) all BMPs are properly installed and maintained per plan.
c) off-site sedimentation is being prevented.
d) turbidity is being prevented.
e) All of the above
people
courteous
fair
performance based
effective
Chapter 9 Review

## Slide 49
Inspection reports should be written (at end of week/in your spare time/at the end of the day/first thing in the morning/while you are on the job site).
The first step in inspecting a project is to ______ plans and drawings (if available).
When reviewing plans, locate the project with respect to the watershed and determine how water ______ and ______ the site.
Which of the following should you bring with you for a site inspection?
Copy of the approved plan / Project file / Reporting forms / Camera / All the above
First thing to do after you arrive on the job site is to: Hide and spy for a while / Start inspecting the perimeter first / Check in with the superintendent / Start inspecting the interior drainage first.
review
enters leaves
Chapter 9 Review