## Slide 1: Nitrate Load Management in the Wakulla Springshed
Upper Wakulla River BMAP
February 21, 2012
John Buss, Manager
Water Resources Division

## Slide 2: Nitrate Load Management
Summary of Nitrate Problem & Needed Reductions.
What Has the City of Tallahassee Done?
What Remains to be Done?

## Slide 3: The Problem
Hydrilla and Algae at Wakulla Springs
High Nitrate Concentration
TMDL Regulation
Notes: What is Nitrate—a form of nitrogen. A nutrient for plants—aquatic plants large (hydrilla) and small (algae)
Not a Health Issue !
– groundwater vs. drinking water (MCL for DW = 10 mg/L vs. 0.35 mg/L affecting the aquatic environment)

## Slide 4: Milestones - Advancing Our Understanding of the Nitrate Problem at Wakulla Spring
2002 | NWFWMD Study (Chelette and Pratt.) | Identified and quantified sources of nitrogen loading to Wakulla Springs.
2005 | Hydrogeology Consortium. | Scientists concurred on the largest nitrate sources. Land use issues led to LAVA Study.
2007 | Leon CO. Aquifer Vulnerability Study (LAVA) | Identified those areas in Leon Co. most susceptible to groundwater pollution from surface land uses. Cody escarpment is apparent as a demarcation. Leads to adoption of a Primary Spring Protection Zone (PSPZ) in Leon County.
2008 | City Commits to AWT Project to Reduce City Nitrate Load. | Results in 75% reduction in nitrate discharge by Dec 2012.
Notes: Over the last 10 years a number of studies, reports, and regional workshops have been undertaken to further the understanding of the nitrate problem. Some of these activities and significant results are summarized above.

## Slide 5: Milestones Continued …
2009 | Tri-Party Memorandum on Regional Partnership. | Executed by City, Leon Co., Wakulla Co. Agreement to work at reducing nutrients from wastewater systems and to address system for better management of septic tanks. Led to initiation of Lombardo Study.
2009 | Second Regional Workshop on Wakulla Spring Restoration | Discussion of progress and future work to reduce pollutants in the groundwater. Septic tanks identified as next target.
2010 | Primary Spring Protection Zone (PSPZ) Established in Comp. Plan | Within Woodville and USA, AWT technology is preferred method for new development. Where AWT not available, High Performance Septic Tanks required.
2011 | COT Master Sewer Plan. | Provides service plan and costs estimate to Leon Co. for target areas outside City without sewer service.
2011 | Lombardo Report Completed. | To achieve the Wakulla TMDL, maximum practicable nitrogen removal is needed when addressing existing septic tanks in the springshed south of the Cody Scarp. In areas north of Cody Scarp, conventional septic tanks with proper inspection and maintenance is needed.

## Slide 6
Recent Studies – USGS & Lombardo
Load Quantification Particularly Useful
2010 USGS (Hal Davis, et. al)
  Modeled nitrate movement in groundwater from sprayfield, septic systems and other sources, comparing 2007 to 2018.
2011 Lombardo Associates
  Assimilated the relevant data and conclusions from the previous work to formulate guidance on actions local government can take to better manage the wastewater load from the rural areas of Leon and Wakulla counties.
    ( Much of the data that follows is based on Lombardo, but USGS report is very similar.)
Notes: A good part of my summary

## Slide 7
Chart: Nitrogen kg / yr
 | 0
 | 229900 | 0 | 0 | 0
Annual Nitrogen Load to Wakulla Spring
( Pre- AWT)
229,900 kg/yr

## Slide 8
Sources of Annual Nitrogen Load
( Pre- AWT)
229,000 kg/yr
Chart: Nitrogen kg / yr
 | 229900
SE Farm Sprayfield | 0 | 111000
OSTDS | 0 | 49200
Inflow | 0 | 44000
Fertilizer | 0 | 9000
Creeks/Sinks | 0 | 7800
Livestock | 0 | 6500
Atmospheric Dep | 0 | 2400
2,400

## Slide 9
Chart: Nitrogen kg / yr
 | 0
 | 229900 | 0 | 0 | 0
Allowable Nitrogen Load to Wakulla Spring
( Pre- AWT)
229,900 kg/yr

## Slide 10: Nitrate Load Management
Summary of Nitrate Problem & Needed Reductions.
What Has the City of Tallahassee Done?
What Remains to be Done?

## Slide 11: What Has the City Done?
Implemented Source Controls through Ordinances and Educational Outreach
  Fertilizer Ordinance; Pet Waste Ordinance; Fertilizer Applicator Certification Program; TAPP Program; PSPZ Ordinance
Structural Projects
  Millions in Stormwater Treatment
  Millions in Wastewater Projects
Operational Changes
  Implemented Water Quality Charge in SW Fee
  Eliminated Disposal of Bio-Solids in Springshed
  Implemented Effluent Reuse.
  Implemented Assessment and Upgrade of Collection System
Notes: Treatment trains to reduce nitrogen and disinfect

## Slide 12: What Has the City Done?
$227 million upgrade to Advanced Waste Water Treatment (AWT)
Reducing Nitrate Concentration by 75% (Total Nitrogen < 3 mg/L)
Compare to Septic System Discharge at approximately 30 mg/L
Lowered Nitrogen “footprint” of 170,000 residents
- far below per capita footprint of others in Springshed
Notes: Treatment trains to reduce nitrogen and disinfect

## Slide 13: What Has the City Done?
2008 | 2009 | 2010 | Jan 2011 | 2012 | Jan 2013 | Jan 2014
Effluent
Nitrogen
< 9 mg/L
Effluent
Nitrogen
< 6.5 mg/L
Effluent
Nitrogen
< 3 mg/L
Effluent
Nitrogen
< 12 mg/L
Permit Req.
Permit Req.
Permit Required
Achieving <3 mg/L
- Achieved Nitrogen Reduction Far Ahead of Schedule
Notes: We met our goal EARLY -- 75% reduction
13

## Slide 14
229,000 kg/yr
Pre - AWT
Post - AWT
Chart: Nitrogen kg / yr
| Pre - AWT | Post - AWT
SE Farm Sprayfield | 111000 | 30100
OSTDS | 49200 | 51200
Inflow | 44000 | 47800
Fertilizer | 9000 | 9400
Creeks/Sinks | 7800 | 7800
Livestock | 6500 | 6800
Atmospheric Dep | 2400 | 2400
Impact of City’s AWT Project
73% Load Reduction - - Exceeded 56% Required
155,5000 kg/yr

## Slide 15
What Has the City Done?
Chart: Removal of Biosolids Nitrate-N Loading Reductions
| 1996 | 2001 | 2004 | 2006 | 2007
Nitrate-N load to the Aquifer (kg/yr) | 85000 | 72000 | 27000 | 0 | 0

## Slide 16: What Has the City Done?
Land Use Planning Initiatives
The City, along with the County adopted Wakulla Springs protection Comprehensive Plan policies on January 7, 2009
Both the City and County adopted Primary Springs Protection Zone (PSPZ) ordinances effective April 10, 2009

## Slide 17: Sewage Collection System Assessment and Rehabilitation Program
  Initiated in 2011
  To date televised 380 mi of older systems (95% Complete)
  Repair & Replacement Projects Ongoing
  $10 million Program
  Completion 2021
  Assessment & Rehabilitation of Older Sewers
Notes: FY2011 Budget for $10 million: Repair and Improvement (Smoke Testing, Collection System Rehab&Maint., Pump Station Improvement, FROG, etc.

## Slide 18
Stormwater Capital Improvement Projects
Abbiegail Pond
Bond Pond
Frenchtown Pond
FSU-RSF
Last 12 years City-wide $97.4 Million 149 Projects
Notes: NOTE: DEP available funding is about $8-9 Million for the entire state for stormwater projects

## Slide 19: Reductions Through Source Control Public Education & Ordinances
TAPP (Think About Personal Pollution)
$1.7 million since 2006
Passed Pet Waste Ordinance (June 2008)
Passed Fertilizer Applicator Ordinance (Jan 2009)
City issued 557 certifications to applicators since 2009

## Slide 20: Reductions Through Source Controls (Pet Waste)
Nitrogen content 21/2 times cow manure
39,350 dogs
= 13.5 ton/da feces
Nitrogen Load
= 34 tons/yr.
30% of dog owners began picking up within the last 6-12 months
Notes: Details are available and the main point is that this translates to a cost-avoidance of $2.5M/year
Think back to the “value” of nutrients – the cost of removing an ounce of phosphorous from polluted runoff is $847.
Again, it’s far cheaper to prevent pollution than it is to clean it up.

## Slide 21: Reductions Through Source Controls (Fertilizer Use Citywide)
Households that applied fertilizer (2007 vs. 2012) decreased 49%.
Level of Nitrogen Applied per Household decreased 27%
Chart: 
| 2000-2001 | 2001-2002 | 2002-2003 | 2003-2004 | 2004-2005 | 2005-2006 | 2006-2007 | 2007-2008 | 2008-2009 | 2009-2010 | 2010-2011 | 2011-2012
Total (tons) P2O5 | 118 | 106 | 77 | 94 | 139 | 125 | 70 | 57 | 48 | 38 | 34 | 26
Total N (tons) | 233 | 248 | 272 | 275 | 549 | 424 | 303 | 241 | 271 | 199 | 179 | 147
Source: Florida Department of Agriculture & Consumer Services, Bureau of Compliance Monitoring

## Slide 22: Nitrate Load Management
Summary of Nitrate Load & Needed Reductions.
What Has the City of Tallahassee Done?
What Remains to be Done?

## Slide 23
Additional Nitrate Reduction Required
(45,600 kg )
229,000 kg/yr
Pre – City AWT
Post – City AWT
Chart: Nitrogen kg / yr
| Pre - AWT | Post - AWT
SE Farm Sprayfield | 111000 | 30100
OSTDS | 49200 | 51200
Inflow | 44000 | 47800
Fertilizer | 9000 | 9400
Creeks/Sinks | 7800 | 7800
Livestock | 6500 | 6800
Atmospheric Dep | 2400 | 2400
110,000 kg TMDL
45,600 kg
Additional Reduction Required

## Slide 24
Additional Nitrate Reduction Required
(45,600 kg )
Post – City AWT
Chart: Nitrogen kg / yr
| SE Farm Sprayfield | OSTDS | Inflow | Fertilizer | Creeks/Sinks | Livestock | Atmospheric Dep
SE Farm Sprayfield | 30100 | 0
OSTDS | 51200 | 0
Inflow | 47800 | 0
Fertilizer | 9400 | 0
Creeks/Sinks | 7800 | 0
Livestock | 6800 | 0
Atmospheric Dep | 2400 | 0
* Inflow includes OSTDs north of PSPZ
*

## Slide 25
Additional Nitrate Reduction Required
(45,600 kg )
Post – City AWT
Chart: Nitrogen kg / yr
| SE Farm Sprayfield | OSTDS | Inflow | Fertilizer | Creeks/Sinks | Livestock | Atmospheric Dep
SE Farm Sprayfield | 30100 | 0
OSTDS | 51200 | 0
Inflow | 47800 | 0
Fertilizer | 9400 | 0
Creeks/Sinks | 7800 | 0
Livestock | 6800 | 0
Atmospheric Dep | 2400 | 0
* Inflow includes OSTDs north of PSPZ
Inflow perhaps can be reduced by management efforts in the More Vulnerable LAVA Mapped Areas

## Slide 26: LAVA Model Results
Project Results

## Slide 27
Septic Tanks Located
North and South of The Cody Scarp
Notes: This map shows the PSPZ with the location of Septic Tanks

## Slide 28
Additional Nitrate Reduction Required
(45,600 kg )
Post – City AWT
Chart: Nitrogen kg / yr
| SE Farm Sprayfield | OSTDS | Inflow | Fertilizer | Creeks/Sinks | Livestock | Atmospheric Dep
SE Farm Sprayfield | 30100 | 0
OSTDS | 51200 | 0
Inflow | 47800 | 0
Fertilizer | 9400 | 0
Creeks/Sinks | 7800 | 0
Livestock | 6800 | 0
Atmospheric Dep | 2400 | 0
* Inflow includes OSTDs north of PSPZ
OSTDs
Possibly the Low Hanging Fruit

## Slide 29: Lombardo Guidance
Due to significant natural attenuation , there is limited value in seeking additional nitrogen removal north of the Cody Scarp.
To achieve 0.35 mg/L nitrate in Scenario 1, the maximum practicable nitrogen removal is required for all septic systems in the Scenario 1 area.
That means either central sewer or advanced or performance-based septic systems as opposed to conventional septic systems.
Notes: Attenuation = reducing the nitrate levels. Above the Cody Scarp more of a clay overburden

## Slide 30: OSTDs – The Numbers
In Priority Area | Septic Systems
Leon County | 7,500
Wakulla County | 1,100
Tallahassee | 118
Notes: Leon / SPZ
Wakulla
City

## Slide 31: Questions ?

## Slide 32
Chart: Nitrogen kg / yr
 | 0
 | 229900 | 0 | 0 | 0
Allowable Nitrogen Load to Wakulla Spring
( Pre- AWT)
229,900 kg/yr

## Slide 33
229,000 kg/yr
Pre - AWT
Post - AWT
Chart: Nitrogen kg / yr
| Pre - AWT | Post - AWT
SE Farm Sprayfield | 111000 | 30100
OSTDS | 49200 | 51200
Inflow | 44000 | 47800
Fertilizer | 9000 | 9400
Creeks/Sinks | 7800 | 7800
Livestock | 6500 | 6800
Atmospheric Dep | 2400 | 2400
Impact of City’s AWT Project
73% Load Reduction - - Exceeded 56% Required
155,5000 kg/yr

## Slide 34
Additional Nitrate Reduction Required
(45,600 kg )
229,000 kg/yr
Pre – City AWT
Post – City AWT
Chart: Nitrogen kg / yr
| Pre - AWT | Post - AWT
SE Farm Sprayfield | 111000 | 30100
OSTDS | 49200 | 51200
Inflow | 44000 | 47800
Fertilizer | 9000 | 9400
Creeks/Sinks | 7800 | 7800
Livestock | 6500 | 6800
Atmospheric Dep | 2400 | 2400
110,000 kg TMDL
45,600 kg
Additional Reduction Required

## Slide 35
What Has the City Done?
Chart: Removal of Biosolids Nitrate-N Loading Reductions
| 1996 | 2001 | 2004 | 2006 | 2007
Nitrate-N load to the Aquifer (kg/yr) | 85000 | 72000 | 27000 | 0 | 0

## Slide 36: Distributive Property of Mathematics
X (a + b + c) = Xa + Xb + Xc
56% ( Total Load ) = 56%(a) + 56%(b) + 56%(c)
So if each of the sources is reduced by 56%
the overall 56% reduction is achieved.