## Slide 1
Bureau of Watershed Restoration
Summary of Water Quality Data and the Existing Monitoring Network : Current & Recent Nitrate Trends in Wakulla Springs & River
Gary Maddox, P.G.
Ground Water Management Section
March 28, 2013

## Slide 2: QUESTIONS:
  How do recent (2007-2012) nutrient concentrations in Wakulla Springs & River compare with levels measured during the TMDL Verified Period (February 28, 2000 – June 30, 2007)?

## Slide 3: QUESTIONS:
  How do recent (2007-2012) nutrient concentrations in Wakulla Springs & River compare with levels measured during the TMDL Verified Period (February 28, 2000 – June 30, 2007)?
  Which tunnels are contributing elevated nitrates to Wakulla Springs & River?

## Slide 4: QUESTIONS:
  How do recent (2007-2012) nutrient concentrations in Wakulla Springs & River compare with levels measured during the TMDL Verified Period (February 28, 2000 – June 30, 2007)?
  Which tunnels are contributing elevated nitrates to Wakulla Springs & River?
  What potential source areas contribute to water quality in major Wakulla tunnels (based on dye-tracing studies)?

## Slide 5: .
WAKULLA SPRINGSHED & WBID 1006 BOUNDARIES
Springshed coverage from NWFWMD (Barrios), 2008

## Slide 6: Wakulla Cave Access Well Locations

## Slide 7: Wakulla Main Spring Sampling Tube

## Slide 8: Wakulla B- & C-Tunnel Access Well

## Slide 9: Wakulla Surface Water & Ground Water Quality Stations

## Slide 10: Wakulla River Surface Water Quality Stations @ County Road 365 Bridge

## Slide 11: Nitrate Reduction Downstream from Wakulla Main Spring

## Slide 12: Wakulla Main Spring vs. Wakulla River @ County Road 365 Bridge

## Slide 13: Ground Water Sources – Wakulla Main, B-Tunnel & C-Tunnel

## Slide 14: Ground Water Sources – Wakulla Main & D-Tunnel

## Slide 15: Ground Water Sources – Wakulla Main & K-Tunnel

## Slide 16: Wakulla Main Spring Nitrate & Tallahassee Regional Airport Precipitation

## Slide 17: Wakulla River Discharge 2004 - 2009
from Harrington, 2010

## Slide 18: Relative Contribution from Inventoried Land Surface Nitrogen Sources to 1990-1999 Average N-Loading in Southern Leon and Wakulla Counties
Figure from Chelette, Pratt & Katz, 2002

## Slide 19: Dye-Tracing Results (2005-2007)
ESTABLISHED CONNECTIONS:
Fisher & Black Creeks → Wakulla-Leon Sinks Cave System → Wakulla R-Tunnel → Wakulla K-Tunnel
Ames Sink → Indian, Sally Ward, Wakulla B-Tunnel
SE Sprayfield → Indian, Sally Ward, McBride Slough, Wakulla B- Tunnel
Map from Kincaid et al, 2007

## Slide 20: CONCLUSIONS:
  How do recent (2007-2012) nutrient concentrations in Wakulla Springs & River compare with levels measured during the TMDL Verified Period (February 28, 2000 – June 30, 2007)?

## Slide 21: CONCLUSIONS:
  How do recent (2007-2012) nutrient concentrations in Wakulla Springs & River compare with levels measured during the TMDL Verified Period (February 28, 2000 – June 30, 2007)?
    Recent nitrate concentrations in Wakulla Main, B- and C-Tunnels have dropped relative to the TMDL Verified period;

## Slide 22: CONCLUSIONS:
  How do recent (2007-2012) nutrient concentrations in Wakulla Springs & River compare with levels measured during the TMDL Verified Period (February 28, 2000 – June 30, 2007)?
    Recent nitrate concentrations in Wakulla Main, B- and C-Tunnels have dropped relative to the TMDL Verified period;
    Nitrate concentrations in D-Tunnel may have dropped relative to the TMDL Verified period, but there is too little post-Verified Period monitoring data to confirm this;

## Slide 23: CONCLUSIONS:
  How do recent (2007-2012) nutrient concentrations in Wakulla Springs & River compare with levels measured during the TMDL Verified Period (February 28, 2000 – June 30, 2007)?
    Nitrate concentrations in K-Tunnel appear to be relatively constant, but there is too little post-Verified Period monitoring data to confirm this;

## Slide 24: CONCLUSIONS:
  How do recent (2007-2012) nutrient concentrations in Wakulla Springs & River compare with levels measured during the TMDL Verified Period (February 28, 2000 – June 30, 2007)?
    Nitrate concentrations in K-Tunnel appear to be relatively constant, but there is too little post-Verified Period monitoring data to confirm this;
    Nitrate trends in the Wakulla River, measured at the bottom of the WBID, mirror those at Wakulla Main Spring, but with lower nitrate levels.

## Slide 25: Wakulla Long-Term Nitrate Trend

## Slide 26: SUMMARY STATISTICS
PERIOD OF STUDY:
February 28, 2000 – December 31, 2012
TMDL VERIFIED PERIOD:
February 28, 2000 – June 30, 2007
POST-TMDL VERIFIED PERIOD:
July 1, 2007 – December 31, 2012

## Slide 27: CONCLUSIONS (con’t):
  Which tunnels are contributing elevated nitrates to Wakulla Springs & River?

## Slide 28: CONCLUSIONS (con’t):
  Which tunnels are contributing elevated nitrates to Wakulla Springs & River?
    Data from Wakulla B-, C-, D- & K-Tunnels all continue to show mean nitrate concentrations in excess of the 0.35 mg/L Narrative Nutrient Criteria; however, B-, C- & D-Tunnels appear to be the major contributors;

## Slide 29: CONCLUSIONS (con’t):
  Which tunnels are contributing elevated nitrates to Wakulla Springs & River?
    Data from Wakulla B-, C-, D- & K-Tunnels all continue to show mean nitrate concentrations in excess of the 0.35 mg/L Narrative Nutrient Criteria; however, B-, C- & D-Tunnels appear to be the major contributors;
    B-Tunnel has the highest measured mean nitrate concentration;

## Slide 30: CONCLUSIONS (con’t):
  Which tunnels are contributing elevated nitrates to Wakulla Springs & River?
    Data from Wakulla B-, C-, D- & K-Tunnels all continue to show mean nitrate concentrations in excess of the 0.35 mg/L Narrative Nutrient Criteria; however, B-, C- & D-Tunnels appear to be the major contributors;
    B-Tunnel has the highest measured mean nitrate concentration;
    K-Tunnel has the lowest measured Wakulla Tunnel nitrate concentrations. It receives much of it’s flow from R-Tunnel (Wakulla-Leon Sinks Cave System).

## Slide 31: Ground Water Sources – Principal Wakulla Tunnels

## Slide 32: CONCLUSIONS (con’t):
  What potential source areas contribute to water quality in major Wakulla tunnels (based on dye-tracing studies)?

## Slide 33: CONCLUSIONS (con’t):
  What potential source areas contribute to water quality in major Wakulla tunnels (based on dye-tracing studies)?
    B-Tunnel: SE Leon, NE Wakulla (including the SE Sprayfield, Ames/Kelley Sinks, and the Woodville area)

## Slide 34: CONCLUSIONS (con’t):
  What potential source areas contribute to water quality in major Wakulla tunnels (based on dye-tracing studies)?
    B-Tunnel: SE Leon, NE Wakulla (including the SE Sprayfield, Ames/Kelley Sinks, and the Woodville area)
    C-Tunnel: Same as B-Tunnel

## Slide 35: CONCLUSIONS (con’t):
  What potential source areas contribute to water quality in major Wakulla tunnels (based on dye-tracing studies)?
    B-Tunnel: SE Leon, NE Wakulla (including the SE Sprayfield, Ames/Kelley Sinks, and the Woodville area)
    C-Tunnel: Same as B-Tunnel
    D-Tunnel: Similar to B-Tunnel

## Slide 36: CONCLUSIONS (con’t):
  What potential source areas contribute to water quality in major Wakulla tunnels (based on dye-tracing studies)?
    B-Tunnel: SE Leon, NE Wakulla (including the SE Sprayfield, Ames/Kelley Sinks, and the Woodville area)
    C-Tunnel: Same as B-Tunnel
    D-Tunnel: Similar to B-Tunnel
    K-Tunnel: Apalachicola National Forest surface water streams - Fisher Creek, Black Creek via R-Tunnel, and Lost Creek via O-Tunnel; also Spring Creek Springs Group

## Slide 37: .
WAKULLA TUNNELS & DYE-TRACING RESULTS
Map courtesy of Dr. Todd Kincaid
(H2H Associates)

## Slide 38: Questions?