## Slide 1: Using Nitrate Isotopes to Identify Sources of Nitrogen in the Wakulla Springs Basin
Brian G. Katz
Florida Department of Environmental Protection
Tallahassee, FL
Brian.Katz@dep.state.fl.us
Wakulla Springs BMAP meeting
April 18, 2013

## Slide 2: Outline of Presentation
Brief background information on nitrate isotopes and ranges of nitrate isotope values for various N sources
Nitrate isotope data for water samples collected in the Wakulla Springs basin

## Slide 3: What are Nitrate (NO3) Isotopes?
All elements have more than one isotope, some of which are stable (do not decay) and some are unstable (radioactive).
The nitrate (NO3-) molecule contains nitrogen and oxygen. Nitrogen has 2 stable isotopes (15N and 14N); oxygen has 3:
(18O, 17O and 16O).
Changes in the ratios of the less abundant isotope (15N relative to 14N) and (18O relative to 16O) reflect biological and physical processes and can be used as tracers of these processes.

## Slide 4: How are Nitrate Isotope Data Reported?
Changes in the ratio of nitrogen isotopes (15N/14N) are reported relative to atmospheric nitrogen in parts per thousand (‰).
If a sample has a value of 0 ‰ then it has the same composition as atmospheric N
If it has a higher value, it contains more 15N;
a lower value then more 14N.
d15N (‰) = ([15N/14N]sample/[15N/14N]standard -1)*1000

## Slide 5: How are Nitrate Isotope Data Reported?
By convention, changes in the ratio of oxygen isotopes (18O/16O) in nitrate are reported relative to standard mean ocean water (VSMOW) in parts per thousand (‰).
d18O (‰) =([18O/16O]sample/[18O/16O]standard -1)*1000

## Slide 6: Ranges of d15N and d18O of nitrate from different sources– and from transformation processes
Chart: d15N-Nitrate, per mil
DUMMY DATA
Denitrification trend line

## Slide 7: Isotopic Fractionation
During biological processes (e.g. nitrification, denitrification), the lighter isotope (14N) ends up being concentrated in the products while the heavier isotope ends up being concentrated in the reactants.
So, during denitrification (NO3- N2), the resulting N2 (product) has a lower d15N than the residual NO3 (reactant), which develops a higher d15N.

## Slide 8
14N16O3
14N16O3
14N16O3
14N16O3
14N16O3
15N18O3
15N18O3
15N18O3
15N18O3
14N16O3
Denitrification– conversion of nitrate to nitrogen gas (N2)
by bacteria
14N16O3
14N16O3

## Slide 9
Davis and others (2010)
Wakulla Springs Cave System—water samples collected during March-December 2011

## Slide 10
Chart: delta 15N-NO3, ppt, air
| 6.292260146896 | 7.1530028319999843 | 7.5502720799999965 | 7.4087637279999994 | 6.9874629007219999 | 7.1828880485909776
St. Marks Springs | 6.5127 | 6.6409 | 6.8465 | 6.1812 | 7.0862 | 7.4953
Wakulla B Tunnel | 4.8815 | 3.2976 | 3.6851 | 3.9932 | 3.5961
Wakulla Main Spring | 5.3782 | 4.9054 | 4.6785 | 5.518 | 3.7439 | 3.2813
Wakulla C Tunnel | 5.3354 | 4.3525 | 5.2271 | 5.1084 | 4.4765
Wakulla D Tunnel | 4.3575
Wakulla K Tunnel | 5.3954
Wakulla A-D Tunnel | 6.8479
Wakulla A-K Tunnel | 5.6003
Indian Spring | 4.0583
K-tunnel
Wastewater,
manure
Nitrate isotope data– water samples collected by FDEP (March-Dec 2011)

## Slide 11
Sources of nitrate and direction of groundwater flow based on dye trace studies for Wakulla Springs and associated tunnels.

## Slide 12: Sucralose as a Tracer of Wastewater
Studies around the world have detected sucralose in groundwaters with wastewater influence.
The vast majority of sucralose passes through wastewater and water treatment systems into the final effluent.
It is not affected by chlorination treatment and even survives tertiary-grade wastewater treatment.

## Slide 13
Median Sucralose concentrations (ppb) in Wakulla Springs and associated tunnels
(2011-2012)
0.035
0.013
0.033
0.011
0.02

## Slide 14
**Distinct N and O isotopic signature for nitrate was found for downgradient waters affected by sprayfield effluent–
Tallahassee Sprayfield Study
11 miles
Nitrate moves with chloride and plots along a dilution line from the sprayfield effluent.

## Slide 15
Evidence for some denitrification in shallow lysimeters and old HK drainfield well;
BUT application of fertilizers is a complicating factor.
Information about fertilizer application timing and rates
Is consistent with the lower 15N signal.
Septic Tank Study—Woodville Karst Plain

## Slide 16
Summary
Nitrate isotopes (15N/14N and 18O/16O of NO3) can provide important information about contaminant sources and nitrogen transformation processes.
Nitrate isotopes are one tool in the toolbox– other information needed on the land use, hydrology and other chemical indicators to understand sources and processes.

## Slide 17
Questions ??
Contact:
Brian Katz
Florida Department of Environmental Protection
Bureau of Watershed Management
2600 Blair Stone Rd.
Tallahassee, FL 32399
Brian.Katz@dep.state.fl.us

## Slide 18: Determining d15N and d18O of nitrate in water (Revesz and Casciotti, 2007)
A culture of denitrifying bacteria (Pseudomonas chlororaphis and P. aureofaciens) is used to convert nitrate (NO3) is converted to nitrous oxide (N2O), which is analyzed by mass spectrometry
The denitrifying bacteria are used in the enzymatic conversion of NO3 to N2O
NO3 - NO2-NO 1/2 N2O