## Slide 1: Biosolids Rule/Permitting
Maurice Barker
Division of Water Resource Management
November 28, 2018

## Slide 2: Chapter 62-640, F.A.C., Biosolids
Originally adopted in 1990
  Primarily based on draft EPA Part 503 rule and previous DER solid waste rules contained in Chapter 17-7, F.A.C.
  Revised in 1998 – primarily for consistency with final EPA Part 503 rule which became effective in 1993
  Revised in 2010 to improve site accountability and nutrient management; key changes included:
    Site permits
    NMPs with phosphorus assessment (P-Index)
    Class AA fertilizer requirement

## Slide 3: Rule 62-640.100, F.A.C.
Scope, Intent, Purpose, and Applicability:
  Intent to regulate biosolids to protect public health and the environment
  Encourages highest levels of treatment, acceptance, innovative, etc.
  Minimum requirements for the treatment, management, use and disposal of biosolids
  Applies to all domestic wastewater facilities, appliers, distributors, biosolids, septage regulated by DEP, composting facilities, out-of-state importers
  Does not apply to industrial wastewater sludges
Other rules noted: solid waste rules for disposal and composting, air rules for incineration and burning for energy, transportation

## Slide 4: Rule 62-640.200, F.A.C.
Definitions:
  Classes of biosolids; biosolids
  Distribution and marketing
  Incorporation
  Nutrient management plan
  Restricted public access
  Treatment

## Slide 5: Rule 62-640.210, F.A.C.
General Technical Guidance and Forms
  Technical guidance documents are listed to provide guidance
    Guidance documents are not enforceable regulations - specific regulatory items are adopted and incorporated at other places in the chapter
    Part 503 and guidance documents from EPA, USDA, IFAS, etc.
  Forms
    Five forms are included in the rule: biosolids site permit application form, two annual summary forms for land application, treatment facility biosolids plan, and site log

## Slide 6: Rule 62-640.300, F.A.C.
General requirements
  Treatment facility permit is required to address the treatment and management of biosolids (treatment and management)
  A biosolids application site permit is required for land application sites
    Individual site permit requirements
    Can be under a facility permit if used only by that facility
  Biosolids storage – facility biosolids storage plan is required

## Slide 7: Rule 62-640.400, F.A.C.
Prohibitions
  Prohibited - ocean disposal, disposal in waters, disposal of hazardous waste, disposal to collection system without consent, use or disposal except in accordance with permit, treatment in truck
  Shall not result in violation of Florida surface water quality standards
  Shall not cause violation of odor prohibition in Rule 62-296.320(2)
  Cannot ship non-Class AA to Florida unless shipped to a DEP permitted facility
  Shall not spill biosolids or track off-site
  Shall not land apply in NEEPP watersheds without phosphorus demonstration
  Shall not store >1 dry ton of Class AA >7 days unless properly stored

## Slide 8: Rule 62-640.500, F.A.C.
Nutrient Management Plans
  Submitted with site permit application
  Prepared by certified nutrient management planner or P.E.
  Establishes application rates; includes phosphorus assessment
  Nitrogen calculations
  Phosphorus areas; NEEPP watersheds

## Slide 9: Rule 62-640.600, F.A.C.
Pathogen Reduction and Vector Attraction Reduction (VAR)
  Adopted and incorporated EPA Part 503’s Class A and Class B pathogen reduction requirements
    Except - Alternative 4 for Class A was not adopted; also, requirements were clarified for Alternative 3 for Class A
    Septage treatment provision regarding Class B pathogen reduction and VAR
  Adopted and incorporated EPA Part 503’s VAR requirements

## Slide 10: Rule 62-640.650, F.A.C.
Monitoring, Record Keeping, Reporting, and Notifications
  Requirements may be increased or decreased based on site specific circumstances
  Biosolids monitoring – incorporated 503.8 (analysis methods), established monitoring parameters, frequency, representative samples after final treatment but before use
  Soil sampling – initial site metals; soil fertility
  Ground water monitoring – sites applying over 400 lbs PAN per acre per year
  Treatment facility records – quantities, monitoring, hauling, annual summary
  Treatment facility reporting – Monthly discharge monitoring report, annual summary for land application

## Slide 11: Rule 62-640.650, F.A.C. (continued)
Monitoring, Record Keeping, Reporting, and Notifications (continued)
  Site records – hauling records, application zone logs, onsite records, NMP, and soil and water monitoring, records to demonstrate compliance with NMP
  Site reporting – annual summary (copies to facilities) with loadings to each zone and cumulative loading of each metal
  Notifications – use of alternate site by facility, water quality violations, discrepancies in transported quantities, importing Class AA, 60 days before closing site or biosolids treatment facility, discovery of biosolids not meeting requirements, molybdenum

## Slide 12: Rule 62-640.700, F.A.C.
Requirements for Land Application of Class AA, A, and B Biosolids
  Site shall be permitted and follow site NMP
  Biosolids must meet requirements
  Biosolids parameter limits and cumulative limits for sites
  Site requirements – uniform application over zone; application of alkaline-treated biosolids; biosolids storage at site; advisory signs; setbacks to surface waters, conduits to groundwater (e.g. sinkholes), drinking water wells, storage areas, buildings occupied by the general public, property lines; site pH; 2ft depth to water table at time of application; rainfall causing ponding; site slope
  Class B restrictions – restricted public access required; harvesting restrictions; grazing restrictions; nursery use; sod; change of ownership and continuation of restrictions

## Slide 13: Rule 62-640.800, F.A.C.
Additional Requirements for Land Application at Reclamation Sites
  Maximum application of 50 dry tons/acre
  Incorporate same day as application
  Vegetative cover must be planted within 3 months
  Any topographic grading must be completed before application
  Mining reclamation sites shall be in compliance with DEP rules on mining reclamation

## Slide 14: Rule 62-640.850, F.A.C.
Distribution and Marketing of Class AA Biosolids
  Clarifies which rule provisions are not applicable to distribution and marketing
  Distributed and marketed biosolids must meet Class AA requirements and meet fertilizer requirement (license or sell to someone with license); compost can be enrolled in USCC STA program if outside NEEPP watersheds
  Information submitted with permit application – fertilizer license; planned quantities and marketing operations; transportation, storage, and application procedures; fertilizer label/information sheet; contingency plans, etc.
  Reporting – monthly DMR with quantities distributed and marketed
  Information sheet with label – facility, storage/application recommendations
  Out-of-state notification to DEP to ship to Florida

## Slide 15: Rule 62-640.860, F.A.C.
Other Solids
  Other solids – cleanings (sand/grit) from facility treatment process (not from sewers or headworks)
  Beneficial use must be permitted and must be demonstrated
  Must be monitored and meet parameter limits
  Must meet pathogen reduction and vector attraction reduction
  Must meet land application requirements and be consistent with NMP

## Slide 16: Rule 62-640.880, F.A.C.
Additional Requirements Related to Biosolids Treatment Facilities (BTFs)
  BTFs accept biosolids from other facilities for treatment prior to use
    Examples – small lime stabilization facility treating biosolids and/or combinations of septage, portable toilet waste, grease, etc.; large Class AA pelletization facility; WWTF accepting from small facilities into digester; etc.
  Written agreements are required between BTFs and each source facility
  BTF preliminary design report requirements; staffing requirements; hauling records with source facilities
  Rules for pathogen reduction, vector attraction reductions, monitoring, record keeping, reporting, land application; distribution and marketing, etc., all apply to BTFs

## Slide 17: Biosolids Management Options
A wastewater treatment facility (WWTF) can choose from several biosolids use or disposal options:
  Transfer to another facility
  Landfill (allowed in all facility permits)
  Land application
  Distribution and marketing (fertilizer)
  Incineration
  Bioenergy (potential)
A wastewater treatment facility can also choose to receive biosolids from other facilities for further treatment and disposal

## Slide 18: Biosolids Permitting
Two primary permit-types related to biosolids:
Treatment facility permits – the permits for facilities that generate and/or treat biosolids
  Wastewater treatment facilities (WWTF)
  Biosolids treatment facilities (BTF)
  Septage management facilities (SMF)
    The treated material from a DEP-permitted SMF is regulated as biosolids
Biosolids Land Application Site Permits – the permit for the site (e.g. farm or ranch) where biosolids are land applied
  Site permits are not applicable for Class AA biosolids distribution and marketing (Class AA distribution and marketing is addressed in the treatment facility permit )

## Slide 19: Biosolids Permitting – WWTF/BTF/SMF
The permit application (DEP Form 62-620.910(2)) for a wastewater treatment facility will identify (as applicable):
  The amount of biosolids generated by the facility
  Whether the facility will receive biosolids from other facilities
  The biosolids use or disposal method(s) and quantity(ies)
  Identification information of the facilities, if applicable, where biosolids will be landfilled, incinerated, treated, etc.
  The Class of biosolids provided by the facility (AA, A, B, other)
  Any treatment process(es) for pathogen reduction
  Vector attraction reduction option(s)
  Biosolids analysis results

## Slide 20: Biosolids Permitting – WWTF/BTF/SMF
The facility permit application (DEP Form 62-620.910(2)) also requires additional information for wastewater facilities receiving biosolids, biosolids treatment facilities (BTFs), and septage management facilities (SMFs), as applicable:
  Types and amounts of waste (e.g. biosolids, septage, portable toilet waste, etc.) treated at the facility
  Information on the facilities transporting the biosolids
  Biosolids analysis from the facilities transporting the biosolids
  Manifest system /hauling records

## Slide 21: Biosolids Permitting – WWTF/BTF/SMF
Other information submitted with the facility permit application includes, as applicable:
  Process flow diagram, site plan, location map, preliminary design report
  Facility biosolids storage plan
  Written agreements between receiving facilities/source facilities
  For land application - Treatment Facility Biosolids Plan (DEP Form 62-640.210(2)(a))
    Identifies biosolids land application sites to be used by the facility
    Signed by treatment facility and site permittees
  For Class AA - planned distribution and marketing operations, fertilizer label or information sheet, contingency plans, and fertilizer license number (s)for Class AA, as applicable

## Slide 22: Biosolids Permitting – WWTF/BTF/SMF
The biosolids-related parts of the permit application are reviewed to ensure proper management of biosolids by the facility
  Does the facility have the equipment, staffing, etc., to properly treat the biosolids?
  Can the facility properly manage the quantity of biosolids generated and/or received?
The facility permit will specify:
  Class of biosolids; allowed use and disposal methods for the facility
  Pathogen reduction and vector attraction reduction methods
  Monitoring requirements
  Reporting requirements
  Recordkeeping requirements

## Slide 23: Class A/AA Pathogen Reduction
There are six alternatives for achieving Class A pathogen reduction under Part 503 but alternative 4 is not allowed under Chapter 62-640, F.A.C.
EPA Alternative | Description
1) Thermally Treated | Maintain the biosolids at a high temperature for an amount of time calculated from one of four time-temperature formulas in Part 503, which vary based on the biosolids percentage of total solids and the heating process.
2 ) High pH-High Temperature Process | Elevate pH > 12 for 72 hours, maintain temperature above 52oC for 12 hours while pH >12, and air dry biosolids to over 50% total solids after the 72 hour period of pH > 12.
3) Other Process | Establish a process and demonstrate that it reduces enteric viruses and helminth ova. Once demonstrated, maintain and monitor demonstrated operating parameters.
4) Unknown Process | Monitor for helminth ova and enteric viruses in the final product - NOT ALLOWED
5) Use of PFRP (Process to Further Reduce Pathogens | Follow a defined process in Appendix B of Part 503 – composting, heat drying, heat treatment, thermophillic aerobic digestion, beta ray irradiation, gamma ray irradiation, pasteurization.
6) Use of a Process Equivalent to PFRP | Use a newer process approved by the EPA Pathogen Equivalency Committee (PEC) or submit and obtain approval from the PEC for a new process (demonstrate reduction of enteric viruses and helminth ova)

## Slide 24: Class B Pathogen Reduction
There are three alternatives for achieving Class B pathogen reduction under Part 503
EPA Alternative | Description
1) Monitoring of Fecal Coliform | Collect seven representative samples of the biosolids and the geometric mean of fecal coliform in the samples shall be less than either 2,000,000 Most Probable Number (MPN) per gram of total solids (dry weight basis) or 2,000,000 Colony Forming Units (CFU) per gram of total solids (dry weight basis)
2 ) Use of a PSRP (Process to Significantly Reduce Pathogens) | Follow a defined process in Appendix B of Part 503 – aerobic digestion, air drying, anaerobic digestion, composting, lime stabilization
3) Use of a Process Equivalent to PSRP | Use a newer process approved by the EPA Pathogen Equivalency Committee (PEC) or submit and obtain approval from the PEC for a new process (demonstrate a 2-log reduction of fecal coliform density)
For Class B Alternative 1, the seven representative samples should be taken over at least a two week period. The period can be longer than two weeks.

## Slide 25: Vector Attraction Reduction
While Part 503 has 12 vector attraction reduction options, only 1-10 are applicable to beneficial use and only 1-8 are applicable to distributed and marketed biosolids.
Option | What is Required? | Most Appropriate For:
1 | At least 38% reduction in volatile solids during biosolids treatment | Biosolids processed by anaerobic biological treatment or aerobic biological treatment
2 | Less than 17% additional volatile solids loss during bench-scale anaerobic batch digestion of the biosolids for 40 additional days at 30°C to 37°C | Only for anaerobically digested biosolids that cannot meet the requirements of Option 1
3 | Less than 15% additional volatile solids reduction during bench-scale aerobic batch digestion for 30 additional days at 20°C | Only for aerobically digested liquid biosolids with 2% or less solids that cannot meet the requirements of Option 1. Sludges with 2% solids must be diluted
4 | SOUR at 20°C is ≤ 1.5 mg oxygen/hr/g total solids | Liquid biosolids from aerobic processes run at temperatures between 10°C to 30°C
5 | Aerobic treatment of the biosolids for at least 14 days at over 40°C with an average temperature of over 45°C | Composted biosolids

## Slide 26: Vector Attraction Reduction Chart
Option | What is Required? | Most Appropriate For:
6 | Addition of sufficient alkali to raise the pH to at least 12 at 25°C and maintain a pH ≥ 12 for 2 hours and a pH ≥ 11.5 for 22 more hours | Alkali-treated biosolids (alkaline materials include lime, fly ash, kiln dust, and wood ash)
7 | Percent solids ≥ 75% prior to mixing with other materials | Biosolids treated by an aerobic or anaerobic process (i.e. biosolids that do not contain unstabilized solids generated in primary wastewater treatment)
8 | Percent solids ≥ 90% prior to mixing with other materials | Biosolids that contain unstabilized solids generated in primary wastewater treatment (e.g. heat-dried biosolids)
9 | Biosolids are injected into soil so that no significant amount of biosolids is present on the land surface 1 hour after injection (Class A biosolids must be injected within 8 hours after the pathogen reduction process | Biosolids applied to the land
10 | Biosolids are incorporated into the soil within 6 hours after application to land (Class A biosolids must be applied to the land within 8 hours after the pathogen reduction process | Biosolids applied to the land

## Slide 27: Biosolids Monitoring
Biosolids monitoring is required and must demonstrate that biosolids meet the required treatment and parameter requirements to be beneficially used
Two general types of monitoring are conducted:
  Parameter monitoring – sampling for metals, nutrients, total solids, pH, etc.
    Monitored at specific frequency; methods specified by rule; representative samples required after final treatment but before use; certified lab must be used
    Limits for pollutants
    Class A/AA fecal coliform/salmonella sampling
  Operational and process monitoring
      Specific to the treatment process and equipment
      Continuous or routine in accordance with process

## Slide 28: Biosolids Monitoring
These monitoring frequencies apply to microbial parameters and required parameters
Biosolids Generated (dry tons per year) | Monitoring frequency
Greater than zero but less than 160 | Once per year
Equal to or greater than 160 but less than 800 | Once per quarter
Equal to or greater than 800 but less than 8000 | Once per 60 days
Equal to or greater than 8000 | Once per Month
For biosolids that are distributed and marketed, monitoring shall be once per month
For biosolids treatment facilities that land apply biosolids, the minimum frequency shall be in accordance with the table but at least once per quarter

## Slide 29: Biosolids Monitoring
Biosolids that will be land applied or distributed and marketed must be analyzed routinely by the treatment facility for the following parameters:
Parameter | Units
Total Nitrogen | % dry weight basis
Total Phosphorus | % dry weight basis
Total Potassium | % dry weight basis
Arsenic (As) | mg/kg dry weight basis
Cadmium (Cd) | mg/kg dry weight basis
Copper (Cu) | mg/kg dry weight basis
Lead (Pb) | mg/kg dry weight basis
Mercury (Hg) | mg/kg dry weight basis
Molybdenum (Mo) | mg/kg dry weight basis
Nickel (Ni) | mg/kg dry weight basis
Selenium (Se) | mg/kg dry weight basis
Zinc (Zn) | mg/kg dry weight basis
pH | Standard units
Total Solids (TS) | %
Calcium Carbonate Equivalent (only for biosolids treated by alkaline addition) | mg/kg dry weight basis

## Slide 30: Biosolids Monitoring
Parameter | Class AA Monthly Average Concentration (mg/kg dry weight basis) | Ceiling Concentration Single Sample Concentration (mg/kg dry weight basis)
Arsenic (As) | 41 | 75
Cadmium (Cd) | 39 | 85
Copper (Cu) | 1500 | 4300
Lead (Pb) | 300 | 840
Mercury (Hg) | 17 | 57
Molybdenum (Mo) | Not applicable | 75
Nickel (Ni) | 420 | 420
Selenium (Se) | 100 | 100
Zinc (Zn) | 2800 | 7500
Class AA biosolids must meet the monthly average concentration limits and the ceiling concentration limits to be distributed and marketed

## Slide 31: Facility Record Keeping
Quantities of all biosolids generated, received, treated, distributed and marketed, land applied, used as a biofuel or for bioenergy, transferred to another facility, or landfilled
Monitoring results
  Operational and process monitoring to demonstrate compliance with pathogen reduction and vector attraction reduction
  Parameter sampling and analysis
Hauling records – transfer to another facility or sent to land application
Annual summaries including copies of Biosolids Application Site Annual Summaries received from sites

## Slide 32: Facility Reporting
Monthly Discharge Monitoring Report
  Biosolids quantities – e.g. received, landfilled, transferred, land applied, distributed and marketed (inside and outside Florida)
  Monitoring results for nutrients, pollutants (i.e. metals), etc.
Treatment Facility Biosolids Annual Summary – for facilities that send biosolids to land application sites
  Total amount land applied during the previous calendar year and number of land application sites used
  Amount sent to each land application site used
  Submitted annually to DEP by February 19

## Slide 33: Biosolids Permitting – Sites
Biosolids sites must be permitted
  Individual permit is required, except a site may be permitted as part of a facility permit if the facility is the only facility using the site
  Must submit a site-specific nutrient management plan (NMP) with the permit application
  Must meet site requirements addressing site slope, storage, seasonal high ground water table, setbacks, signage, cumulative application limits, public access, and harvesting restrictions, etc.
  After operating for five years, site permit renewals would potentially be eligible for ten-year permits in accordance with Chapter 62-620, F.A.C.
  The site permittee does not have to be the land owner – instead, the site permittee could be a biosolids hauler/contractor, or a wastewater treatment facility permittee

## Slide 34: Biosolids Permitting – Sites
Application package includes:
  DEP Form 62-620.910(1) Wastewater Facility or Activity Permit Application—General Information—Form 1
  Biosolids Site Permit Application, DEP Form 62-640.210(2)(d), and related attachments as indicated on the form, such as:
    Maps, documentation, background soil sampling, etc.
    Descriptions of any storage areas, application methods, etc.
    Ground water monitoring plan, if required
    $1000 fee (unless being permitted as an exclusive site under a treatment facility permit)
  Nutrient management plan (NMP) must be submitted with the biosolids site permit application (site-specific)

## Slide 35: Biosolids Site Permit Application
Checkbox: Type of Permit – new or renewal
Checkbox: Type of Issuance – individual permit or included as part of facility permit
Checkbox: Type of Site – agricultural or reclamation
Part I General Information
  Site ID, name, address, latitude/longitude, section/township/range, county, driving directions
  Site permittee name, address, phone, email, alternate contact info
  Site manager name, address, phone, email, etc.
  Land owner name, address, phone, email (this is verified through cadastral GIS layer, property appraiser websites, Sunbiz, etc.)
  Total acreage of all application zones at the site

## Slide 36: Biosolids Site Permit Application
Part II. Site Information Checklist
  Map (aerial, other similar) indicating site boundaries and zones, and:
    ID of each zone
    Biosolids storage areas, if applicable
    Property lines and neighboring properties
      75 ft setback from property lines for land application
      1320 ft setback from property lines for application of alkaline-treated biosolids
    Occupied buildings on the site or with ¼ mile of the site
    300 ft setback from buildings occupied by the general public (100 ft if injected)
    1320 ft setback from buildings occupied by the general public from storage areas
    Water supply wells on site or within 500 ft of the site
    300 ft setback from private drinking water well, 500 ft setback from public well

## Slide 37: Biosolids Site Permit Application
Part II. Site Information Checklist (continued)
  Map (continued)
    Surface water on the site or within 1000 ft of the site
      1000 ft vegetated setback to Class I water bodies, Outstanding Florida Waters, or Outstanding National Resource Waters
      200 ft vegetated setback to surface waters, including wetlands
    200 ft setback from conduits for direct contamination of ground water (e.g. sinkholes)
    Grouund water monitoring locations
      Piezometers or monitoring wells for monitoring ground water table level, if applicable
      Ground water monitoring wells for ground water quality monitoring, if applicable
    Frequently flooded areas
    Attach ground water monitoring plan, if applicable

## Slide 38: Biosolids Site Permit Application
Part II. Site Information Checklist (continued)
  Attach a description of any biosolids storage, stockpiling, or staging at the site
    Verify fencing or other features to control access to storage and staging areas
    Indicate if storage for more than seven days is being requested; if yes, then attach documentation showing rule’s storage requirements will be met
  Verify seasonal high water table (NRCS soil survey maps, other)
    Indicate if seasonal high ground water level can be determined by maps and attach maps
    Indicate the depth of biosolids placement (0” if surface applied)
    Indicate if any of the application zones will have a seasonal high water level within 2 ft of biosolids placement (monitoring of ground water level will be required)
    Use map, such as a topo map, to determine site slope (max slope of 8%, slopes between 3 – 8% need to retain 10 year, 1 hour storm or inject/incorporate biosolids)

## Slide 39: Biosolids Site Permit Application
Part II. Site Information Checklist (continued)
  Verify that soil fertility testing will be conducted at frequency given in NMP
    Verify soil fertility testing results are in NMP and are less than 1 year old
    Verify the pH result of soil fertility testing is 5 or greater
  Attach documentation of initial background soil monitoring of metals (new sites only)
  Verify provisions for record keeping
    Verify provisions for hauling records and sending receipts back to facilities
    Attach description of where copies site logs and records will be kept on site and how to access them
    Verify that advisory signs are posted (English and Spanish) at entrances and, for unfenced sites, at 500 ft intervals

## Slide 40: Biosolids Site Permit Application
Part II. Site Information Checklist (continued)
  Attach description of application techniques, methods, and equipment to ensure uniform application
    Are spray guns being requested? If yes, indicate why they are needed and how aerosols will be minimized
  Attach the signed and prepared nutrient management plan (NMP)
  Reclamation site checklist items
    Need for land reclamation, existing condition of land
    How will biosolids be used as part of reclamation activities
    Descriptions of grading, incorporation, type of vegetation to be established, schedule
    Application quantity
    Include permit fee

## Slide 41: Biosolids Site Permit Application
Part III. Application Zone Summary
  Total acreage of all application zones
  Table for entering physical characteristics/information about each zone:
    Zone ID
    Acreage
    Depth to high seasonal ground water level
    Slope
    Application method to be used
    Latitude (deg-min-sec)
    Longitude (deg-min-sec)

## Slide 42: Biosolids Site Permit Application
Part IV. Application Zone Initial Background Soil Testing Results
  Table for entering the results for the nine regulated metals:
    Zone ID
    Arsenic
    Cadmium
    Copper
    Lead
    Mercury
    Molybdenum
    Nickel
    Selenium
    Zinc

## Slide 43: Biosolids Site Permit Application
Part V. Application Zone Current Cumulative Loadings
  Enter year and the cumulative loadings in lbs/ac and estimated site life for each zone:
    Zone ID
    Arsenic, Cadmium, Copper, Lead, Mercury, Molybdenum, Nickel, Selenium, Zinc
    Estimated life of zone in years
    Calculated from the first date of application subject to Part 503 or Chapter 62-640, F.A.C.
    Based on average concentrations in biosolids applied

## Slide 44: Biosolids Site Permit Application
Part VI. Application Zones – NMP Summary
  Enter the nutrient information for each application zone from the NMP:
    Zone ID
Year | Crop(s) to be grown on the application zone | Basis for Nutrient Budget (N or P) | Crop Demand N (PAN) from All Sources (lbs/ac) | Crop Demand P2O5 from All Sources (lbs/ac) | Maximum Allowed PAN from Biosolids (lbs/ac) | Maximum Allowed P2O5 from Biosolids (lbs/ac) | Maximum Allowed TN from Biosolids (lbs/ac) | Maximum Allowed TP from Biosolids (lbs/ac)
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 

## Slide 45: Biosolids Site Permit Application
Part VII. NMP Checklist
  Prepared in accordance with nutrient management standards, Code 590, and by a certified nutrient management planner or P.E.
  Identifies zones, includes guidance on implementation, record keeping, operations
  Aerial maps, soil survey maps, etc.
  Soil fertility testing frequency, any soil, water, plant, biosolids testing results
  Establishes rate of application for five years, application method
  Table for entering physical characteristics/information about each zone:
    Phosphorus assessment/P-Index
    Accounts for all sources of nutrients, planned plant production, realistic yields, crop demands, calcium carbonate equivalency
    Methodology and calculations
    Phosphorus restrictive areas/NEEPP watersheds

## Slide 46: Biosolids Site Permit Application
Part VIII. Land Owner Consent
    Land owner acknowledges:
    Consent to use property as a biosolids land application site
    Accuracy of information in permit application
    Having been provided a copy of Chapter 62-640, F.A.C., and understanding it
    Understand that the requirements of Chapter 62-640, F.A.C., the information in the permit application, and the site nutrient management plan (NMP) must be followed and apply to all parties using the property and to the use of biosolids on the property
  Signature and date

## Slide 47: Biosolids Site Permit Application
Part VIII. Site Permittee
    Site permittee certifies:
    Familiar with and shall comply with Chapter 62-640, F.A.C.
    Shall only allow application of biosolids meeting the criteria for land application
    Shall maintain the required records and logs for the site
    Shall file an annual summary with DEP
  Signature and date

## Slide 48: NMP Review – Key Items
Is the NMP included with the site permit application?
Signed by a certified nutrient management planner or a P.E.?
Does it have language regarding site operations, recordkeeping, etc.?
Does it have the required maps including soil survey maps for the site?
Are any applicable soil, water, plant tissue, biosolids testing results included?
  Soil fertility test results – P result used in P index
  Biosolids N and P results used in nutrient calculations and P-Index
  Phosphorus assessment/P-Index conducted correctly? Results?
  Calcium carbonate equivalency for alkaline-treated biosolids/
  Crops? All sources of nutrients addressed? Method of application (affects calculations)
  How is nitrogen availability addressed when calculating the application rates? Correct?
  Northern Everglades and Estuaries Protection Program watershed, etc.?

## Slide 49: Request for Additional Information (RAI)
DEP has 30 days to review a submitted permit application to determine if the application is complete or if additional information is needed
If more information is needed, a Request for Additional Information (RAI) is sent and the time clock for permit processing is stopped
When the response to the RAI is received, DEP has 30 days to review the response to determine if the response provided the requested information or if a second RAI will be sent; the second RAI should only address items from the first RAI, not new issues
If a second RAI is sent, the permit processing time clock stops
Additional RAIs may be sent if necessary
Once the application is deemed complete, DEP has 90 days to determine agency action on the permit (will the permit be issued or denied?)

## Slide 50: Contact Information
Maurice Barker
Florida Department of Environmental Protection
Division of Water Resource Management
850-245-8614
Maurice.Barker@dep.state.fl.us