## Slide 1
Engineering, Hydrology and Geology
DAM, EMBANKMENT AND LEVEE SAFETY FEATURES,
EMBANKED STORMWATER PONDS

## Slide 2: Inventory of Dams
In the U.S.A.:
– 79,000 Dams
  57,000 Dams have inadequate protection against
overtopping
  3,500 Structurally Unsafe Dams (Actual Number Considered to be much Higher)
  ASCE 2005 Report Card on US Infrastructure:
    Dams received a “D”
    More than ¼ older than 50 years
    $10.1 Billion needed to rehab critical non-federal dams that pose a direct risk to human life.

## Slide 3: Inventory of Dams Continued
In Florida:
  National Inventory shows 796 entries
  FDEP preliminary count shows >4000
  Much of infrastructure associated with dams, levees, and reservoirs is 50 years or older
  Comprehensive inventory and assessment needed

## Slide 4: Causes of Dam Failures
Seepage and soil piping
Overtopping
Spillways and other outlets
Slope instability
  Steep Slopes
  Poor Selection of Materials
  Inadequate Placement and Compaction
  Lack of Positive Seepage Control
  Weak Foundation

## Slide 5: Dams in Florida—Geologic Considerations
Relatively flat topography
  Maximum height for “natural” dams approximately 50 feet
  Maximum height for “impoundments” exceeds 100 feet
(tailings dams, gypsum stacks)
Unique geologic setting
  Relief created by sand ridges and wave-carved escarpments
  Primary construction material is sand
  Lots of unsuitable materials (organic soils, soft clay, uniform fine sands)
  Rock exposures uncommon

## Slide 6: How and Why Dams Fail

## Slide 7: Causes of Dam Incidents
Fundamental Causes Percentage Sabotage. 0....... Earthquake Instability 1....... Faulty Construction. 2....... Gate Failure. 2.......
Sliding. 10.......
Deformation. 11.......
Overtopping 25.......
Seepage/Piping 35.......
75%
7

## Slide 8
Baldwin Hills Dam, Los Angeles - 1963
Catastrophic Failure Within 4.5 Hours of Observation
Problems noted at 12:20 p.m.
Evacuation Began at 1:00 p.m.
Helicopters With Speakers
1,600 People Evacuated by
3:20
Dam Failed at 3:38 p.m.
41 Homes Destroyed
1,000 Homes Damaged
5 People Drowned
Reservoir Empty by 4:55 p.m.
232 Feet High

## Slide 9
Failure By Overtopping

## Slide 10: Taum Sauk, 2005

## Slide 11: Taum Sauk Dam Failure, Reynolds County, Missouri December 14, 2005
Source: AmerenUE

## Slide 12: Taum Sauk, 2005

## Slide 13: Source: Paul Rizzo & Associates Report
UNISTRUT ASSEMBLY

## Slide 14
Photo by David Hoffman

## Slide 17: Failure By Uncontrolled Seepage

## Slide 18
Teton Dam
June 5, 1976
Clear Water Springs from Joints
In Rock
Hydropower Plant

## Slide 19: Teton Dam June 5, 1976
Muddy Seepage Observed at Right
Abutment 8:30 a.m.

## Slide 20
June 5, 1976
10:45 a.m.

## Slide 23: 11:20 a.m. Large Vortex Observed In Reservoir

## Slide 26: Dam Crest Breaching, 11:55 a.m.

## Slide 28
••
•
•
..
••

## Slide 32: Early Afternoon

## Slide 33: Early Afternoon

## Slide 34: Late Afternoon

## Slide 36: Topics to Discuss
1928 Hurricane and Lake O Dike Failure
Current Condition of Herbert Hoover Dike
Hurricane Katrina—Levee Failures
Independent Review of HHD
CERP Reservoirs
Pensacola Dam Failure

## Slide 37: Lake Okeechobee
970 square miles in natural state
Before drainage projects, when lake reached ~Elev. 21 ft. water overflowed a low natural levee at South end into the Everglades

## Slide 38: Lake Okeechobee
Drainage and reclamation projects began with Hamilton Disston in 1860’s.
In early 1900’s, Governor Napoleon Bonaparte Broward was elected on platform to aggressively drain the Everglades.
By 1920, six canals dug that lowered the Lake by 6 feet and reduced its area by 250 sq. miles.

## Slide 39: Pahokee – Before the Dike

## Slide 40: Lake Okeechobee Muck Dike
Beginning in 1923, EDD build earthen dike 57 miles long from Moore Haven to Pahokee using hopper dredges.
– Dike ranged in height
from 5 to 9 feet
Constructed from locally dredged material, including muck
Where dike crossed dead rivers, loose silt was dredged as fill
Settlement and slumping required re-dredging several times
5/20/2014
40

## Slide 41: Prelude to Disaster
Protection from flooding brought new surge of settlers. From less than 100 settlers in 1915, lake area by 1928 had
increased to more than 6000.
Many from Broward/Dade, where economy had
collapsed following1926
hurricane.
1926 hurricane spared south side of lake, but wind tides and rains caused overtopping of dike on western shore, killing approximately 200 in Moore Haven.
1926 hurricane exposed weakness of muck dike, and plans
were made to build a larger dike.
41

## Slide 42: 1928 Events
Despite various funding attempts, Florida’s deep depression prevented legislature from funding new projects for the EDD.
In 1928, an early season Cat. 2 hurricane, plus numerous thunderstorms, raised the Lake to within 2 feet of the top of muck dike by mid- September.
Then, as now, outlet works could discharge less than 1 foot of water per month, while inflow could be more than 1 foot per day during major storms.

## Slide 43: 1928 Dike Failure
On September 16, a Cat. 4 hurricane, with 155 mph winds, struck.
Wind tide forced water to height of 8 feet above the dike between South Bay and Pahokee
Dike quickly eroded,
producing massive flood
wave that killed more than 2500 people.
Largest dam catastrophe in U.S. history, exceeding
Johnstown Flood of 1889 (2209 deaths)

## Slide 44: 1928 Hurricane References
Killer Cane, by Robert Mykle, 2002, Coopers Square Press, NY, NY.
Black Cloud, by Eliot Kleinberg, 2003, Carroll &
Graf Publishers, NY, NY.
Okeechobee Hurricane, by Lawrence E. Will, 1990, 3rd ed., The Glades Historical Society, Belle Glade, FL.
Beyond the Fourth Generation, by Lamar Johnson, 1974, Univ. of FL Press, Gainesville.

## Slide 45: Herbert Hoover Dike

## Slide 46: Herbert Hoover Dike
After the disastrous hurricane of 1928, USACE
rebuilt the dike beginning in 1932.
By 1938 the dike encompassed 85 miles from
Moore Haven to Port Myakka.
Following the 1940’s hurricanes, the dike was enlarged and completed around the entire perimeter of 140 miles.
Downstream muck subsidence of 1 inch per year made the dike even more essential for flood control (Note that peat formed over 3000 years at rate of one inch per 33 years).

## Slide 47: Herbert Hoover Dike
Constructed using hydraulic dredges and draglines
Fill includes silts, clays, peat, sand, shell, and gravel
Crest ranges in elevation from 33 to 45 feet.
Lake level normally regulated between 15.5 and
17.5 feet.
The side slopes range from 2:1 to 5:1.
Foundation has pervious layers (limestone, shell, clean sands), and cohesive layers (hardpan, sandstone, limestone).
Interior borrow channels and exterior rim ditches expose uninterrupted flow paths from lakeside to landside

## Slide 48
Draglines Constructing
Retaining Dikes

## Slide 49
Pipeline Dredge and Dipper
Dredge at Work

## Slide 50
Levee Construction South Side
Lake Okeechobee C. 1932

## Slide 51: Completed Dam

## Slide 52: Typical Existing Cross-Section

## Slide 53
East Side of Lake Okeechobee

## Slide 54: Herbert Hoover Dike
No selection of suitable materials
No compaction for suitable density
No seepage control through fill
No cutoff to prevent high pore pressures in landside slope and toe

## Slide 55: Problems Noted by USACE

## Slide 56: Seepage Problems
During late summer 1995, the lake level reached
18.6 ft.
Excessive seepage was observed.
Sand boils and cloudy water at toe of dam.
Sinkholes appeared on the crest.

## Slide 57: Sandbags Around Soil Pipes

## Slide 58
Sinkhole on Dam Crest
Lake Harbor

## Slide 59: Seepage Problems
Following the 1995 event, seepage control berms, filters, and drains were installed at worst areas.
Surveillance increased to identify and repair
problem areas.
In March 1998, the lake rose to 18.5 feet.
Additional areas exhibited boils and excessive
seepage.

## Slide 60: 1995 and 1998 High Stages

## Slide 61: 1998 Review Panel
Expert panel convened by USACE to review
status of the HHD, included:
  Dr. Michael Duncan, John Bischoff, Dr. Thomas Wolff
  Dr. Ronald Hirschfeld, Dr. Hans Sellmeijer
The panel concluded that if the lake level had remained at 18.5 feet for an extended period, failure could have occurred.
Elev.18.5 level is a 30-year event.
Failure is “high probability” if lake reaches 21 feet.
Elev. 21 level is a 100-year event.

## Slide 62
Lake Elevations for 100 Year Storm Event
(USACE, 2000)

## Slide 63
USACE REGULATION 1110-8-2
DESIGN FLOODS
INFLOW DESIGN FLOODS FOR DAMS AND RESERVOIRS
5. General Policy. It is the Corps of Engineers policy that dams designed, constructed, or operated by the Corps will not create a threat of loss of life or inordinate property damage. Departures from accepted policy or practice will not be made in the design of a dam simply to reduce cost. Every phase of the planning, design, construction, and operation of a dam will be accomplished to assure that it is safe, efficient, and reliable.
6. Discussion.
b. The requirement that a dam failure must not present a hazard to human life remains a fixed condition that must be met by all designs.
7. Safety Dam Standards.
b. Standard 1: Standard 1 applies to the design of dams capable of placing human life at risk or causing a catastrophe, should they fail. Dam height with appropriate freeboard, spillways, regulating outlets, and structural designs will be such that the dam will safely pass an IDF computed from probable maximum precipitation (PMP) occurring over the watershed above the dam site.

## Slide 64: Rehabilitation Plan (1999)
USACE proposed an extensive rehab program for HHD.
Beginning with critical SE 22 miles from Belle Glade to Port Mayaca
Construct downstream berm of pervious material
beginning at Elev. 28
Install relief trench into foundation soils

## Slide 65: View of Wave Scarps

## Slide 66: New Orleans August 30, 2005

## Slide 67
Damage to the Flood Protection
System

## Slide 68: Levee Wall Types

## Slide 69: I-Wall Schematic

## Slide 70: Distressed I-wall

## Slide 71: Overturned I-wall

## Slide 72
Overtopped Earth Embankment
During Storm Surge

## Slide 73: Earth Levee

## Slide 74
E Of Pointe a la Hache
Levee Breach

## Slide 75
17th Street Levee Failure

## Slide 76: Levee Failure Analysis

## Slide 77
Hurricane Katrina References
Preliminary Report on Performance of the New Orleans Levee Systems, NSF, November 17, 2005
(www.asce.org/files/pdf/katrina/teamdatareport1121.pdf)
New Orleans Hurricane Protection Project
Data, IPET, January 10, 2006
(https://ipet.wes.army.mil/)

## Slide 78: Independent Review Panel
Les Bromwell
  Geotechnical, Panel Chair
Robert Dean
  Hydrology, Hydrodynamics
Steve Vick
  Risk Analysis, Probability
Art Sengupta
  SFWMD Technical Investigation Manager

## Slide 79: Review Panel Scope of Work
Review & Analysis of Documents and Data
Dike Stability Evaluation
Wind and Precipitation Analyses
Preparation of Evaluation Report by April 30, 2006

## Slide 80
Review Panel Site Inspection
January 13, 2006

## Slide 81: Wright’s Lake Dam, Clay Cnty

## Slide 82: Pensacola Dam Failure

## Slide 83: Pensacola

## Slide 84: Blue Springs Ave.

## Slide 85: Blue Springs Ave. at 2 am

## Slide 86: CERP Reservoirs
70,000 Acres of Reservoirs Planned
Dam Heights Ranging 15-30 feet
Constructed to Modern Safety Standards
  Will include positive seepage control features
  Will include foundation improvement features
  Will have adequate freeboard for storm surges
  Will have emergency discharge provisions
Will be expensive structures!

## Slide 87
CERP RESERVOIRS
--DESIGN CRITERIA
Freeboard must accommodate most severe of 4 extreme wind and precipitation conditions
  PMP + 100-year wind
  100-yr precipitation + Category 5 winds
  PMW + Full Reservoir Level
  Hurricane Easy (Cat 3 + 38.7 inches rain)
Positive seepage control required
  Slurry cut-off wall
  Filters & Drains of non-carbonate sand/gravel
Interior slopes protected against wave erosion
  Soil Cement
  Roller-Compacted Concrete
  Rip-Rap

## Slide 88: Florida’s Aging Infrastructure
C&SF Facilities Mostly 50+ Years Old
Maintenance Costs Increasing
Risk of Failures Is Increasing
What is the Plan for Replacement?
What will it Cost?
Where Will the Funding Come From?