## Slide 1
EHG Program
Hydrographic Review: Issues and Criteria
Mariano Guardo PhD, PE, D.WRE
June 10, 2014

## Slide 2: Hydrographic Review
Issues
  When is a Hydrographic Analysis, Study or Assessment (HASA) needed? A HASA is required when changes imposed by a project may cause adverse impacts in the water quantity and/or quality of a waterbody
  What is obtained from a HASA? The results from a HASA will allow us to determine with reasonable assurance whether the proposed modifications of the project will not originate violations in the water quality standards

## Slide 3: Hydrographic Review
Issues (cont’d)
  There are four typical types of projects that could eventually alter the water quantity and/or quality conditions of a waterbody:
  Proposed Structures
  Flow Diversion and Augmentation
  Configuration Changes
  Dredging

## Slide 4: Hydrographic Review
Category 1
  Includes those projects dealing with activities or facility construction that may result in a change in flow patterns or circulation and in diverting flow
  1.1 Structures that provide access to waterbodies: Docks, Piers, Boat Ramps, Wharves
  1.2 Structures used for transportation: Bridges, Causeways, Trestles

## Slide 5: Hydrographic Review
Category 1 (cont’d)
  1.3 Hydraulic Structures used for drainage and control of flows and stages: Culverts, Spillways, Weirs, Risers
  1.4 Hydraulic Structures that convey flows into and discharge flows from waterbodies: Intakes and Outfalls
  1.5 Shoreline Structures that are used for coastal protection, mitigation and restoration: Groins, Breakwaters, Jetties, Seawalls, Revetments, Bulkheads

## Slide 6: Hydrographic Review
Hydrographic Information. Cat. 1
  Details of existing and proposed conditions
  Existing survey and waterbody bathymetry
  Sediment gradation and fine soil content
  Mean tidal range, periodicity and tidal records (coastal projects)
  Existing and proposed flow area cross-section (2,3,4)
  Dimensions and specific elevations (3,4)
  Storm hydrographs for specific durations and frequencies (3)
  Normal operational flows (4)
  Wind data (magnitude and direction) for project area (5)

## Slide 7: Hydrographic Review
Category 2
  Includes those projects dealing with changes to the bottom bathymetric features, such as dredging and reconfiguration of marine, conveyance and navigation projects that could result in stratification, sills, deep zones, separation zones, stagnation; and beach nourishment

## Slide 8: Hydrographic Review
Category 2 (cont’d)
  2.1 Channels and Canal Systems
  2.2 Boat Basins and Marinas
  2.3 Drainage Canals
  2.4 Navigation Channels
  2.5 Dredging Tidal Inlets
  2.6 Beach Nourishment

## Slide 9: Hydrographic Review
Hydrographic Information. Cat. 2
  Details of existing and proposed conditions
  Existing survey and waterbody bathymetry
  Sediment gradation and fine soil content
  Mean tidal range, periodicity and tidal records (coastal projects)
  Flushing time estimates by appropriate computations or calibrated/verified modeling simulations (1,2)

## Slide 10: Hydrographic Review
Hydrographic Information. Cat. 2 (cont’d)
  Peak flows and flood hydrographs for various (storm duration and return period) storm events (3)
  Hydraulic and energy grade lines (3)
  Aggradation/degradation (sediment) zones (4)
  Hydraulic flows (maximum and mean) for flood and ebb tides (4)
  Maximum/minimum and mean flows for flood and ebb tides (5)

## Slide 11: Hydrographic Review
Hydrographic Information. Cat. 2 (cont’d)
  Historical and existing inlet cross-section (5)
  Inlet and embayment tidal prism (5)
  History of inlet stability due to movement/change (6)
  Borrow area quantification (6)
  Design template including the fill toe location (6)
  Dredging, pumping and outfall design with turbidity curtailment, and material placement method
  Report on structures affecting the littoral system (6)

## Slide 12: Hydrographic Review
Category 3
  Includes those projects dealing with spoil disposal associated with dredging
Hydrographic Information. Cat. 3
  Gradation analysis and fine soil content for proposed nourishment zone and borrow area
  Proposed dredging, pumping and outfall design including turbidity curtailment, fluidity and material placement methods

## Slide 13: Hydrographic Review
Hydrographic Information. Cat. 3 (cont’d)
  Spoil area/volume computations (bulking factors, settling times, surface overflow rate, void ratio, etc.)
  Criteria for a HASA
  Hydrodynamic and water quality simulations
  The Environmental Protection Agency (EPA) has published recommendations on marina basin design and best management practice to enhance flushing (EPA 2001, 1993, 1985).

## Slide 14: Hydrographic Review
  Criteria for a HASA (cont’d)
  The main factors controlling flushing of a coastal waterbody includes its location with respect to the tidal action, shape, volume of tidal exchange (tidal prism), depth relative to adjacent waterbodies, and effect of wind and wave generated currents
  DEP flushing compliance specify that a hypothetical point-source conservative pollutant spilled over in the basin would flush to 10% or less of the original concentration within a 96-hour (4-day) period. This certifies the State of Florida water standards