## Slide 1: Revised Dissolved Oxygen Criteria: New Science for the 21st Century
Russ Frydenborg
Frydenborg EcoLogic, L.L.C.
Garry Payne, FDEP

## Slide 2: Dissolved Oxygen
Former criteria based on 1970s (outdated) science
Extensive DO and biological study conducted
Revisions based on:
  DO vs. Stream Condition Index relationship (applied to streams and lakes) and reference site evaluation
  DO vs. laboratory toxicity tests for marine waters (EPA Virginian Province approach)

## Slide 3: Previous Criteria Resulted in High Type I Error
DO Study Reference Systems (Natural Surrounding Landscape) | Percent in Nonattainment of Previous Criteria
82 Lakes | 52.4%
81 Streams | 70.4%

## Slide 4: Use of SCI vs. DO Relationship to Determine Freshwater Criteria (Panhandle West)
Regression line = 62 % Saturation to pass SCI (score of 40)
Lower Confidence Limit = 67 % Saturation to pass SCI

## Slide 5: DO Criteria Derived from Regressions are Supported by Reference Site Data
The proposed criteria based on the SCI-2012 versus DO saturation regression analyses are supported by the reference distribution of DO saturation levels
Thresholds based on lower 90% Confidence limit for SCI-2012 versus daily average DO saturation agree well with the 10th percentile of the reference distribution

## Slide 6: DO Concentration - Water Temperature Relationships
DO Concentrations Required to Achieve Proposed Criteria Based on Water Temperature

## Slide 7: Summary of Revised Florida Freshwater DO Criteria
No more than 10 percent of the daily average percent dissolved oxygen (DO) saturation values shall be below the following values:
67 percent in the Panhandle West bioregion,
38 percent in the Peninsula and Everglades bioregions, or
34 percent in the Northeast and Big Bend bioregions

## Slide 8: Application of Freshwater DO Criteria: Sampling Depth
Criteria for streams will be assessed using data collected throughout the water column
Criteria for lakes will be assessed using data collected in the upper 2 meters of the water column
  DO levels naturally decline with depth in lakes (stratification, SOD, respiration
  Targets protection of area (littoral zone) inhabited by DO sensitive fauna
  Recommended by DO Peer Review Committee

## Slide 9: Application of Freshwater Criteria: Diel Data
Criteria will be preferentially assessed using diel data
If instantaneous DO measurements are used for assessment, daily average criteria will be translated to give time of day specific criteria based on time measurement was made

## Slide 10: Time of Day Correction
Typical diel curves developed for lakes and streams in each bioregion (red curve)
Diel curves were shifted so that daily average was equal to the criteria (blue curve)
Polynomial equation was fitted to shifted curve
Equations can be used to predict DO level at any time for a site with a daily average equal to the criteria and a typical diel fluctuation

## Slide 11: Time of Day Correction
Equations for time of day interpretation of daily average criteria for lakes and streams in each region
To assess criteria using grab samples, measured DO level compared to equation result using time at which sample was collected
Region | Equations for the Time of Day Interpretation of Criteria *
Streams | 
Northeast + Big Bend | 1.1844 x 10-13 • T5 – 4.1432 x 10-10 • T4 + 4.7729 x 10-7 • T3 – 1.9692 x 10-4• T2 + 0.02314 • T + 31.24
Peninsula + Everglades | 1.9888 x 10-13 • T5 – 6.8941 x 10-10 • T4 + 7.8373 x 10-7 • T3 – 3.1598 x 10-4• T2 + 0.03551 • T + 33.43
Panhandle West | 9.0851 x 10-14 • T5 – 2.9941 x 10-10 • T4 + 3.1560 x 10-7 • T3 – 1.0851 x 10-4• T2 + 0.006285 • T + 65.61
Lakes | 
Northeast + Big Bend | 1.4578 x 10-13 • T5 – 5.5607 x 10-10 • T4 + 7.0683 x 10-7 • T3 – 3.1879 x 10-4• T2 + 0.02817 • T + 34.19
Peninsula + Everglades | 1.3709 x 10-13 • T5 – 5.0496 x 10-10 • T4 + 6.1352 x 10-7 • T3 - 2.5817 x 10-4• T2 + 0.01960 • T + 37.14
Panhandle West | 7.1190 x 10-14 • T5 – 2.6420 x 10-10 • T4 + 3.2247 x 10-7 • T3 – 1.3607 x 10-4• T2 + 0.01071 • T + 66.35
* T in the equations is the time of day in minutes past midnight. | 

## Slide 12
Threatened and Endangered Species Considerations

## Slide 13: Protection of Threatened and Endangered Species
Criteria protective of most threatened and endangered species (Panhandle)
Gulf Sturgeon and Oval Pigtoe Mussel found in portions of the Suwannee, Santa Fe, New, and Withlacoochee Rivers and Shortnose and Atlantic sturgeon in the St. Johns River
Criteria include provision to maintaining existing DO levels that are protective of Gulf sturgeon and mussel
In the St. Johns River current criteria of 5.0 mg/L (53% saturation) will be maintained during February and March to protect potential spawning of Shortnose and Atlantic sturgeon

## Slide 14: Marine DO Criteria Based on Virginian Province Approach
EPA’s Virginian Province Approach (EPA 2000) uses measured response of sensitive organisms to low DO levels to establish allowable exposure durations

## Slide 15: Florida Species Used to Derive Marine DO Criteria CMC
The CMC was calculated based on the acute effects data for 25 genera
Genera mean acute values (LC50) of the test organisms ranged from 6 to 33% Saturation
CMC was calculated as the FAV (95th percentile genus GMAV) multiplied by the mean LC5 to LC50 ratio (1.35)
Resulting CMC is 42% Saturation

## Slide 16: Florida Marine DO Criteria Based on Virginian Province Approach
The daily average DO concentrations shall not be below 42 percent saturation
AND
The 7- and 30-day average DO percent saturations shall not be below 51 and 56 percent, respectively
Criteria applied as a water column average
Assessment will be consistent with Impaired Waters Rule
Protective of threatened and endangered species

## Slide 17: Marine DO Concentration vs. Temperature

## Slide 18: Addressing Natural Background
  Allow for a 0.1 mg/L (1% saturation) deficit from the natural dissolved oxygen value
      Can be granted when implemented through permitting or other Department Action.
  Up to 10 percent deficit will be allowed if it is demonstrated that resident aquatic species shall not be adversely affected
      Plan to use USEPA spreadsheet model to determine acceptable deviation from natural background DO Levels.
      Will be implemented through site specific alternative criteria procedures
Natural Conditions

## Slide 19: Addressing Natural Background
If natural ambient DO levels are above the minimum criteria, those higher DO levels shall be maintained
Subject to Rules 62-302.300 and 62-4.242, F.A.C.
Implemented through Seasonal Kendall trend test
Statistically significant decreasing trends in DO percent saturation or an increasing trend in the range of daily DO fluctuations shall not be allowed
Natural Conditions

## Slide 20: New DO Rule Now In Effect
Approved by Environmental regulation Commission in April, 2013
Approved by EPA in October 2013

## Slide 21: Implications of New DO Criteria
Reasonable Assurance demonstration (that water quality criteria are achieved) for new projects will change
New criteria are more accurate
Panhandle freshwater criteria are more stringent
Marine monthly average criteria are more stringent at cool temperatures

## Slide 22: Questions? www.frecologic.com