## Slide 1
Mining and Mitigation Program
Crafting Effective Mitigation Success Criteria
Connie Bersok and Matt Wilson
June 11, 2014

## Slide 2: SWERP – Mitigation Success AH1 10.3.6
  Mitigation success will be measured in terms of whether the objectives of the mitigation are expected to be realized. The success criteria to be included in permit conditions will specify the minimum requirements necessary to attain a determination of success. The mitigation shall be deemed successful by the Agency when all applicable water quality standards are met, the mitigation area has achieved viable and sustainable ecological and hydrological functions and the specific success criteria contained in the permit are met. If success is not achieved within the time frame specified within the permit, remedial measures shall be required. Monitoring requirements shall remain in effect until success is achieved as specified in the permit. Maintenance requirements shall remain in effect as specified in the permit.

## Slide 3: Mining and Mitigation Program Permit Review:
  Task: Review contemporary success criteria from permits three former program areas: mitigation banking, phosphate mining, and non-phosphate mining. Identify successes and shortcomings, and develop recommendations for establishment of future success criteria.
    Team members: Connie Bersok, Howard Hayes, Jay Kamke, Christine Keenan, and Matt Wilson
Reviewed mitigation success criteria in 39 mining and mitigation bank permits
  Large mitigation projects (generally thousands of acres)
  Multiple target community types
  Typically a combination of mitigation types
    Preservation, Enhancement, Restoration, and Creation

## Slide 4: Permit Review: Findings
The success criteria used by each program area were similar.
  Common ancestry
  Convergent evolution
Some common differences were noted.
  Differences in values for common attributes (e.g. nuisance/exotic species)
  Differences in criteria for similar ecosystem components
Most permits included some success criteria that are applicable regardless of community type.
Most permits included community-specific success criteria.
  Mitigation success criteria have been developed for several target community types.
Success criteria often varied due to project-specific circumstances.
  Type of mitigation being conducted
  Starting condition
  Community Type

## Slide 5: Common Literature Recommendations
Project goals should be clearly articulated a priori.
  Performance standards should relate to project goals
Attributes should be simple to measure and be cost-effective.
  Targets should be attainable within a reasonable time frame
    Time frames to achieve success should be established (required by SWERP AH1 10.3.6)
Attributes measured should be indicative of wetland function.
  Ecological Processes: Biological interactions, nutrient pools, herbivory, dispersal, pollination, predation, parasitism, and litter dynamics/decomposition processes, soil biota, etc…
    Ecological processes are rarely used for assessment of mitigation
      slower to recover in comparison with diversity or vegetation structure
      time, cost, and confounding factors
  Structural Attributes: Typically measures of vegetation and hydrology
    Function follows form
    Role of academia

## Slide 6: SER Restoration Primer
“An ecosystem has recovered - and is restored – when it contains sufficient biotic and abiotic resources to continue its development without further assistance or subsidy. It will sustain itself structurally and functionally. It will demonstrate resilience to normal ranges of environmental stress and disturbance. It will interact with contiguous ecosystems in terms of biotic and abiotic flows and cultural interactions.” (SER, 2004).
Nine ecosystem attributes for determining when restoration has been accomplished:
  similar diversity and community structure in comparison with reference sites;
  presence of indigenous species;
  presence of all functional groups (e.g. primary producers, herbivores, carnivores, decomposers, nitrogen fixers, pollinators), necessary for long-term stability;
  capacity of the physical environment to sustain reproducing populations;
  normal functioning;
  integration with the landscape (ecological matrix);
  elimination of potential threats;
  resilience to natural disturbances; and
  self-sustainability

## Slide 7: Literature Review: Self-Reflection
  The approaches being used by our respective program areas are similar to approaches being used across the US.
    Mostly attribute analysis based mostly on vegetation and hydrology, often combined with direct comparisons to reference sites
      Some soil criteria and faunal criteria are being used in addition to vegetation and hydrology
    Trajectory analysis is a component of a few recent permits
      Mitigation Adaptive Management Analysis (MAMA)
  Most of the nine ecosystem attributes listed by the SER are included (directly or indirectly) in most of the permits we reviewed.

## Slide 8: All Mitigation Success Criteria should:
State the type of native, natural community or communities and acres of each.
Example: “Mitigation area shall consist of 2.3 acres freshwater basin marsh, 15.7 acres hydric flatwoods, and 12 acres mesic flatwoods.”
  Florida Natural Area Inventory: Guide to the Natural Communities of Florida, 2010 edition.
  Florida Fish and Wildlife Conservation Commission: Florida Land Cover Classification, 2009 report.

## Slide 9: Natural Communities
Natural communities containing
cypress
vs
Cypress trees

## Slide 10: All Mitigation Success Criteria should:
2. State that wetlands must be able to be delineated as wetlands.
Example: “At least 2.3 acres freshwater basin marsh and 15.7 acres hydric flatwoods must be determined to be wetlands, as delineated pursuant to Chapter 62-340, FAC.”
This condition integrates:
  Vegetation
  Soils
  Hydrology*
*3. Also specify anticipated range of hydrologic conditions for specific wetland community, especially for created wetlands and those with control structures.

## Slide 11: All Mitigation Success Criteria should:
4. Require that plants appropriate for the community are healthy and reproductive.
Example: “Non-nuisance, native groundcover, shrub, and tree species appropriate to the target community are healthy and reproducing naturally, either by normal, healthy vegetative reproduction or through seedling establishment, growth, and survival.”

## Slide 12: All Mitigation Success Criteria should:
Allow no more than minimal, if any, presence by invasive exotic plants
(See definition: 2.0(a) 41, Applicants Handbook)
Example: “Cover by Category I and II invasive exotic plant species (see www.fleppc.org) shall be 1% or less in each plant stratum.”
Limit nuisance plant species
(See definition: 2.0(a) 64, Applicants Handbook)
Example: “Cover by nuisance species shall be 5% or less in each plant stratum.”

## Slide 13: All Mitigation Success Criteria should:
7. Require that the mitigation area provide the expected habitat.
Example: “Evidence of use by native fish and wildlife expected for the target communities. Examples of evidence can include direct observation, vocalization, tracks, scat, nest, dens and burrows.”
8. Require that the mitigation area exhibit viability and be self-sustaining.
Example: “The determination of final success requires a minimum of one year non-intervention in the form of irrigation, artificial manipulation of water levels, exotic or nuisance plant treatment or additional planting or seeding.”

## Slide 14: Project-Specific Success Criteria
Every mitigation project is unique, and success criteria should be tailored to account for project-specific circumstances.
  mitigation starting point, nature of the degradation being repaired, habitat for specific fauna or flora, ecological processes to be restored

## Slide 15: Project-Specific Success Criteria
Base success criteria on the objectives of the mitigation.
Example: Canopy - wet flatwoods:
  [for “start from scratch” creation mitigation on mine tailings] Objective: Establish a pine canopy that will be self-sustaining
    Hydric pine flatwoods areas shall have an average of at least 150 trees per acre that are at least 12 feet tall. No area greater than an acre in size shall have less than 50 trees per acre.
    Planted trees have doubled in height, canopy cover by both planted and volunteer trees (slash pine, long leaf pine, pond pine, or South Florida slash, where appropriate) have increased annually and have a 10% canopy coverage at the end of the growing season.
  [for restoration of drained wet flatwoods converted to pine plantation] Objective: Thin slash pines to open up the canopy to better represent the target community, and establish a population of longleaf pines in a density appropriate for the target community
    There are less than 50 canopy slash pine trees per acre, with d.b.h. > 4”
    The density of longleaf pine (Pinus palustris) [or South Florida Slash pine in South Florida, south of Lake Okeechobee] in the subcanopy and/or canopy is between 50 - 150 trees/acre.

## Slide 16: Project-Specific Success Criteria
Base success criteria on natural community descriptions.
Establish numeric targets/ranges (diversity, abundance, relative proportions) for each community component, as applicable
  Canopy
  Subcanopy
  Ground cover
    Limit inappropriate plants
    Establish a target vegetation list (not just diversity, but the right kind of diversity)
  Minimum/Maximum acceptable extent of open water
  Hydrology (timing, depth, duration)
  Fauna (fish, invertebrates, reptiles, amphibians, birds)
  Natural processes
    Fire
  What are the critical components of the target community?

## Slide 17: Project-Specific Success Criteria
Think about how each component you use should be expressed at the time of success.

## Slide 18: Project-Specific Success Criteria
Tip: Write out what you want to achieve (i.e. your objective) in plain language to help with development of success criteria…
Example: Wet prairie - Canopy and subcanopy sparse to absent with extremely diverse groundcover dominated by grasses and sedges and containing a diversity of showy flowering herbs. The ground cover is typically dominated by dense wiregrass (Aristida stricta var. beyrichiana) in drier portions and by members of the sedge family (e.g., Rhynchospora spp. and Scleria spp.), longleaved threeawn (Aristida palustris), and/or carnivorous plants (Sarracenia spp., Drosera spp., Pinguicula spp., and Utricularia spp.) in the wetter portions.

## Slide 19: Project-Specific Success Criteria
…and develop the success criteria based on your stated objectives using specific numeric targets.
Example – Wet Prairie:
Canopy: (none) A few stunted P. elliottii, Taxodium, and Nyssa sylvatica var. biflora may be present.
  The wetland area shall support no more than 5 trees per acre that are greater than six feet tall. Canopy species present shall be limited to species from the approved target vegetation list.
Subcanopy: (sparse and suppressed) Often contains resprouting short shrubs (Hypericum brachyphyllum, Hypericum myrtifolium, Myrica heterophylla; In North Florida also Cyrilla, Clethra, Ilex coriacea, Ilex cassine)
  Shrubs are reduced to coppice, averaging < 1.5m in height. Areas with shrubs averaging more than 1.5 meters in height and having a collective canopy coverage of more than 5 percent shall be limited to random spots of [X] acres or less where fire did not burn and shall represent an insignificant feature in this community type.
Groundcover: extremely diverse groundcover dominated by grasses and sedges and containing a diversity of showy flowering herbs
  Total ground cover shall be at least 95%;
  Relative ground cover by native grasses and sedges from the target vegetation list shall be at least [50]%;
  At least [25] species from the ground cover target vegetation list shall be present.
  Populations of at least [5] species from the wet prairie specialist list shall be present and self-sustaining.

## Slide 20: Project-Specific Success Criteria
Grade the mitigation in a number of ways.
  Establish multiple ways to measure success
    Numeric targets
      Ranges may work best for certain attributes
    Comparisons with appropriate reference sites and natural community descriptions
    Allow room for reasonable scientific judgment

## Slide 21: Take home message
Know your natural communities
Focus on the mitigation goal, natural communities
Think!
What should success look like?
Clear numeric targets (ranges)
Specific to the mitigation

## Slide 22: References
Environmental Law Institute (2004) Measuring Mitigation: A Review of the Science for Compensatory Mitigation Performance Standards. Environmental Law Institute, Washington, D.C. ISBN # 1-58576-084-6 (http://www.eli.org/sites/default/files/eli-pubs/revision.pdf).
Florida Department of Environmental Protection (2013) Environmental Resource Permit Applicant’s handbook Volume I. Florida Administrative Code (F.A.C.) Rule 62-330 (Incorporated by reference) https://www.flrules.org/gateway/reference.asp?No=Ref-03174).
Florida Natural Areas Inventory (FNAI) (2010) Guide to the Natural Communities of Florida: 2010 edition. Florida Natural Areas Inventory, Tallahassee, FL (http://www.fnai.org/naturalcommguide.cfm).
Society of Wetland Scientists (SWS) Position Paper (2013) Performance Standards for Wetland Restoration and Creation (http://www.bioone.org/doi/abs/10.1672/0732-9393%282001%29018%5B0021%3APPOPSF%5D2.0.CO%3B2?journalCode=wtbl).
SER (Society for Ecological Restoration International Science & Policy Working Group) (2004) The SER International Primer on Ecological Restoration. (available from http//www.ser.org) accessed in January 2014. Society for Ecological Restoration International, Tucson, Arizona (http://www.ser.org/docs/default-document-library/english.pdf).